## Slide 1: Beam Diagnostics at CERN‘s Linac-4
Contribution to the ESS mini-workshop
Lund 2012
Uli Raich CERN BE/BI

## Slide 2: The LHC and its injectors

## Slide 3: The LHC injector chain

## Slide 4: Why an injector upgrade?
Performance limitations: The nominal luminosity can be reached with the current injector chain but the ultimate luminosity needs higher brightness, which cannot be achieved with the current chain.
Reliability: Linac-2, Booster and PS are old machines which had problems in the past. Vacuum leaks, radiation damage on the PS magnets etc.
Nominal | 1 x 1034 cm-2 s-1 | 1.15 x 1011 ppb
Ultimate | 2.5 x 1034 cm-2s-1 | 1.7 x 1011 ppb

## Slide 5: A new injector chain for the LHC

## Slide 6: Linac-4 placement in the injector chain

## Slide 7: Layout of the Linac

## Slide 8: Virtual tour of the building

## Slide 9: Current State

## Slide 10: Linac-4 parameters
Ion Species | H- | 
Output Energy | 160 | MeV
Bunch Frequency | 352.2 | MHz
Max. Repetition Rate | 2 | Hz
Max. Pulse length | 1.2 | ms
Max. Beam Duty Cycle | 0.24 | %
Beam Chopping Factor | 62 | %
Chopping scheme | 222 transmitted, 133 empty buckets | 
Source current | 80 | mA
RFQ output current | 70 | mA
No. of particle per pulse | 1014 | 
Transverse emittance | 0.4 | π mm mrad

## Slide 11: Linac-4 Layout
Slide by M. Vretenar

## Slide 12: Parameters to be measured
Intensity at different energies (connected to interlock system)
Beam trajectory and energy (phase)
Beam profile
Energy spread, will be measured at low energy up to 3 MeV only
Transverse emittance at 45 keV, 3 Mev, 12 MeV, 160 MeV
Chopping efficiency
Bunch shape
Beam loss (connected to interlock system) max beam loss: 1 W/m not more than 1 full beam pulse may be lost
Diagnostics for charge exchange injection into the Booster

## Slide 13: LEBT Commissioning Stages
Source
Source
Source
Source
Emittance meter
Emittance meter
Emittance meter
Faraday’s Cup
Faraday Cup + SEM Grid
Faraday’s Cup
Sol. 1
Sol. 1
Sol. 1
Sol. 2
Slit
SEM grid
Beam Current Transformer (BCT)
Faraday’s Cup
RFQ Input
Completed with
35 keV H- and
45 keV Protons
Completed with 45 keV Protons
1
2
3
4

## Slide 14: Machine sections and their instrumentation
Installed at the 3 MeV test stand
Ion source and LEBT:
  Currently: proton source, ~ 40 mA, 450 μs
  Faraday Cup, SEMGrid, transformer and transverse emittance meter (slit/grid) are installed and running.

## Slide 15: Faraday Cup
Source intensity measured by a retractable Faraday Cup
Secondary electron emission will be suppressed by polarization voltage which also eliminates parasitic electrons created in the source (HV installation to be done)
Pneumatic in/out mechanism on PLC like LEIR is available
Oscilloscope will be used for signal observation
For final operation a 1 MHz sampling ADC is foreseen

## Slide 16: Transverse Emittance Measurement
Slit and grid phase space scanner
L-shaped 0.1mm slit moves under
45 degrees
Slit and grids move independently
Positioning precision: 50 µm
Movement PLC controlled
Slit and grids mounted in 2 independent vacuum boxes which can be separated
Horizontal and vertical SEMGrid
wire distance .75 mm
40 signal wires
readout with home built 36 channel 250 kHz ADC
time resolved profiles

## Slide 17: Emittance Evaluation

## Slide 18: Pseudo Scubexx exvaluation
Histogram of signal levels
Background for each slit
Position
Emittance Plot
Emittance when taking less
and less channels around
peak

## Slide 19: RFQ, Chopper and measurement line
RFQ and chopper line
  RFQ is foreseen to arrive in October.
  Measurement line is in preparation:
    2 transformers
    3 BPMs measuring position and phase
    Transverse emittance meter with new slit
    Bunch shape monitor being assembled and tested in October
    Halo monitor to test chopping
    Spectrometer with SEMGrid
  Will be moved after use and finally removed from the machine
  Chopper Line
    2 transformers
    2 wire scanners

## Slide 20: Measurement line for commissioning only

## Slide 21: 3 MeV measurement line

## Slide 22: Slit at 12 MeV
Mechanical problems due to heating
Slit material: carbon on copper
Water cooled
Slit material inclined to distribute
thermal load over a bigger
surface.

## Slide 23: Chopper
Losses at 160 MeV must be minimized
Chopper eliminates unstable beam and during rise of the Booster distributor
Chopped beam is injected into the RF buckets of the Booster
Correct functioning of the chopper must be monitored

## Slide 24: Halo Monitor

## Slide 25: Photo of Halo Monitor
Individual buckets will be chopped out
352 MHz <> 2.8 ns between buckets
Must be able to measure 1000 ions in the chopped
beam in the vicinity of 5 108 ions
Beam traverses thin carbon foil and creates secondary
Electrons which are accelerated towards a
Phosphor screen
Monitor can be gated off during the intense beam and
switched on within 500 ps

## Slide 26: SEMGrids for Profile Meas.
SEMGrid resolution: up to 0.5mm, up to 36 tungsten or carbon wires
New analogue electronics for 36 under design
Needs time resolved measurements (200 kHz)
New VME readout card has been developed (36 channels), series of 50 cards have been produced
In/out mechanism by motor with PLC control

## Slide 27: SEMGrids
Simulations of energy deposition done
Simulation of signal levels to be expected
New, time resolved electronics under preparation
Fabrication of grids with carbon wires
40 mA, 400 µs, σx=1mm, σy=2mm

## Slide 28: Wire Scanners
Uses carbon wires
Beam pulse restricted to 100 µs for heating reasons

## Slide 29: Current Transformers
Good magnetic shielding
avoids interference from
nearby pulsing quads
Shielding simulation and
test measurements have
Been done

## Slide 30: Typical Transformer Signal
Calibration signal before after
beam pulse
Digitization of 400 µs pulse
at 10 MHz
Measures
total intensity
intensity per Booster ring
Background suppression by
software

## Slide 31: Inter-tank regions
Very little space
Special design to limit
Longitudinal dimensions
BPM built inside a quad

## Slide 32: BPMs: Shorted stripline
Linear
Fair sensitivity
Compact
Cheap
Not beta-dependent
But highly resonating
Shorted
45
Z0= 50

## Slide 33: Pick-Ups: What should be measured?
Absolute beam position with respect to an external reference.
Relative beam intensity measured by two consecutive pick-ups.
Absolute beam intensity after calibration with BCT.
Absolute beam phase with respect to distributed RF reference.
TOF flight between two pick-ups.
Int. = 109/bunch
Pulse l.= 400ms
I ave. = 40mA
sbunch = 20ps – 777ps
FB = 352MHz
1/sbunch = 50 GHz
Low freq. cut off = 15 Hz

## Slide 34: Bunch structure along TL: Concerns
End of Linac
FRMS = 2.5
Debuncher
FRMS = 17
PSB Stripper foil
FRMS = 55
Beam energy at 160MeV

## Slide 35: The measurement line

## Slide 36: Bunch Shape Monitor
Device being build at INR Troitsk
Should be ready next month

## Slide 37: List of instruments
Instrument | number | location | energy | details
Faraday Cup | 2 | LEBT | 45 KeV | only scope
Emittance meter | 1 | LEBT, MEBT | 45 KeV 3 MeV – 12 MeV | 
BPMs | 31 | MEBT - Booster | 3 MeV – 160 MeV L2-Booster transfer | Pos, intensity Phase
SEMGrids | 18 | LEBT – Booster | 45 KeV – 160 MeV | 
Transformers | 16 | LEBT - Booster | 45 KeV – 160 MeV | 
BSM | 1 | MEBT - PIMS | 3 MeV – 160 MeV | Russian coll
Halo Monitor | 1 | MEBT | 3 MeV | M. Hori (finished)

## Slide 38: List of Instruments
Instrument | number | Location | energy | details
Wire Scanners | 6 | MEBT, CCDTL, PIMS | 3 MeV – 160 MeV | 
BLMs | 26 | MEBT - Booster | 3 MeV – 160 MeV | Badly defined
TV screens | 13 | Booster inj | 160 MeV | 
Wide band PU | 1 | Booster |  | Not defined
Upgrade Booster orbit | 64 BPMs | Booster | 160 MeV – 1.4 GeV | Not specified yet
Laser Wire tests | 1 | MEBT - Booster | 3 MeV – 160 MeV | R&D for SPL

## Slide 39: RFQ brazing problems