## Slide 1
ESS BPM
Pick-ups
Andreas Jansson
Beam Diagnostics Mini-Workshop
Lund, 2012-03-21

## Slide 2: Buttons vs Striplines
Strip-lines give a stronger signal, but are more complicated (and expensive) to build.
The gain in signal is not large compared to the extra cost.
Our sensitivity requirements are not extremely high.
Use buttons if and when we can!

## Slide 3: Error sensitivity
Most buttons are designed with very small gap around it, to reduce beam impedance.
Capacitance to ground shunts the signal.
Sensitivity to manufacturing tolerances.
R. Bepour & E Vafa, Masters Thesis

## Slide 4: XFEL button
Designed for XFEL linac with large gap
Prototypes tested by DESY, currently in series production.
Have samples at ESS for prototyping.

## Slide 5: ESS Cold Linac BPMs
In the process of designing
prototype.

## Slide 6: SCL Warm Sections
One Pick-up per Quad
  Beam based alignment of BPM relative to Quad
  Possibility of on-line TOF
  Possibility of beam angle measurement
  Posibility of quadrupole moment based beam size monitoring.

## Slide 8: DTL BPMs
DTL now similar to SNS
Use SNS DTL BPMs as starting point

## Slide 9
DTL BPMs

## Slide 10: MEBT Quads
Design concept not determined yet.
  Depending on magnet design, may be buttons (in the shadow of the coils) or striplines (inside magnets).