## Slide 1
Mechanical design.
Robert Svensson
Work Unit Lead for Neutron Beam Port Blocks,
Monolith systems, Target Division
3

## Slide 2: Potential deformation of vessel main cylinder during welding
Measurement of the vessel after final machining.
mm
Vector from nominal to measured.
Background:
In 2020, AVS highlighted that there is a risk that the vessel will deform when the port tubes are welded.
To simulate this is not easy as the current amount of un-relieved stress is unknown.
Mitigation:
New design of the Neutron Beam Windows
Allow shimming of the LSS
Extra clearance must be added between the port tube and bottom plate step to avoid a collision even if we are out of the worst case scenario.

## Slide 3: X-position of the port tube
Background:
The interface between the port tube and the Neutron Beam Window / Light Shutter System was earlier stated to be within +/- 1mm. However, the stack-up ends up in 0 to -10 mm.
Solution:
A new design of the NBW to allow it to compensate for the port tube X-position.
Shim out the LSS to maintain its relation to NBW.
Benefit:
The instrument/NBW/LSS will be positioned
at nominal in X-direction.
Shim to LSS frame.
New window design.
Insert to be located at nominal position.

## Slide 4: New NBW design
Thickness to be adapted to the tube’s final X-position.
The thickness of the window where the beam passes will always be the same.

## Slide 5: Tolerance stacking in X-direction (Radial)
As installed (welded)
BPCS-X Positive direction
Vessel main cylinder deformation 0,0 -4,0
Welding transverse shrinkage ± 1,5 Stated in the feasibility report to 3-6mm
Geometrical uncertainties ± 1,5 (Porttube lengths resolution) * (Monolith Vessel window frame position) (Pre-welding alignment alignment)
Installation tolerance (welded) 0,0 -10,0 mm
CAD nominal X 0 TCS R5500
0 -1 -2 -3 -4 -5 -6 -7 -8 -9 -10 (mm) BPCS-X
From ESS-3185128 Port tube Installation Drawing
Means 0 to -10 mm
* To compensate the position of the vessel windows there will be three different port tube lengths.

## Slide 6: Tolerance stacking – Y-direction (Sideways)
As installed (welded)
From ESS-3185128 Port tube Installation Drawing
BPCS-Y
0 1 2 3 4 5 6 7 (mm) BPCS-Y
Manufacturing NBPI ± 0,5
Manufacturing Port tube ± 0,75
Installation Alignment ± 0,75
Nominal Clearance 7,0 mm
NBPI
Port tube
Minimum Gap 2,0 (operation condition)

## Slide 7: Tolerance Stacking – Z-direction (Height)
As installed (welded)
From ESS-3185128 Port tube Installation Drawing
(mm) BPCS-Z 0 1 2 3 4 5
NBPI
Port tube
Nominal Clearance 5,0 mm
Manufacturing Port tube ± 1,0
Welding / Alignment ± 1,5 Including alignment ±0,2
Manufacturing NBPI ± 0,5
Minimum Gap 2,0 (operation condition)

## Slide 8: Tolerance Stacking – Z-direction (Height) Insertion of NBPI
As installed (welded)
From ESS-3185128 Port tube Installation Drawing
(mm) BPCS-Z 0 1 2 3
NBPI
Port tube
Nominal Clearance 3,5 mm
Manufacturing Port tube ± 1,0 Toward rail
Manufacturing NBPI ± 0,9
Gap 1,1* (insertion condition)
From ESS-2969343.3 Port tube functional Drawing
NBPI = Neutron Beam Port Insert
Welding / Alignment ± 0,5
* Minimum gap was agreed to 2,0 mm. This can be solved by lowering the rail and/or the wheel on the NBPI.

## Slide 9: Final tolerance towards the insert
The alignment block in the port tube will be adjusted so the final position of the alignment surface to the insert will be within ± 0,2 mm in all directions. The insert will always end up at nominal position.
Z
X/Y
Z
Y/Z
* Adjustability range ± 1 mm
* Adjustability range ± 1 mm
*Adjustability range ± 1 mm in Y
and +10 mm in X.
* Adjustability range ± 1 mm
in X/Z

## Slide 10: NN-bar frame and adapter
The requirements and predicted shrinkage for the NN-bar is equal as for the port tube.
However, the NN-bar has 2+2mm narrower instrument slots due to its narrow design. This might result in space problem for future instruments.
Welding distortions might further worsen the situation.

## Slide 11: Required work to increase the clearance in X
To allow the port tubes to move inwards, up to 10mm, the following modifications need to be performed:
Top and bottom plate
The bottom plate are time critical and might delay the port tube welding.
All wedges
NN-bar

## Slide 12: Finish presentation