## Slide 1: Status of Elliptical Cavities Cryomodule Demonstrator ECCTD
Franck PEAUGER, CEA Saclay
On behalf of the ECCTD team:
C. Arcambal, G. Devanz, P. Bosland, P. Hardy, F. Leseigneur, J. Plouin, G. Ferrand, F. Eozenou, C. Servouin,
D. Roudier, L. Maurice, X. Hanus, C. Madec, JP. Poupeau, N. Bazin, N. Berton, V. Hennion, JP. Charrier, O. Piquet,
P. Carbonnier, B. Renard, P. Sahuquet, A. Hamdi, CEA Saclay
G. Olivier, JP. Thermeau, IPN Orsay
C. Darve, N. Elias, ESS
AD and ICS Retreat mtg 2014
11 December 2014

## Slide 2: ECCTD in ESS Superconducting linac
 | MEDIUM-β | HIGH-β
β | 0.67 | 0.86
# CM | 9 | 21
Cav. /CM | 4 | 4
# Cav. | 36 | 84
CM L [m] | 6.584 | 6.584
Sector L [m] | 77 | 179
Proton Beam
Elliptical cavity Cryomodules ECCTD
Klystron gallery
→ 70% of the total length of the linac

## Slide 3: Cryomodule design
Similar to CEBAF/SNS cryomodule concept with 4 cavities per cryomodule
Common design for medium (6 cells) and high beta (5 cells) cavities
Proton Beam
Jumper connection
Cold to warm transition
Magnetic shielding
Power coupler
Cavity with Helium tank
Diphasic He pipe
Thermal shielding
Regulation He valve
Intercavities belows
Vacuum valve
Spaceframe support
Heat exchanger
Alignement fiducial
G. Olivier

## Slide 4: ²
Spaceframe
Cavity supporting rods
Three supports at 120°C for the spaceframe
Access trap
Cold tuning system
Bursting disk
Cryomodule support (no ground support design yet)
Vacuum vessel
G. Olivier

## Slide 5: Cavity design
57,5 mm
High beta (0,86):
5 cells
Length 1316,91mm
Medium beta (0,67):
6 cells
Length 1259,40mm
 | Medium | High
Geometrical beta | 0.67 | 0.86
Frequency (MHz) | 704.42 | 
Operating temperature (K) | 2 | 
Maximum surface field in operation (MV/m) | 44 | 44
Nominal Accelerating gradient (MV/m) | 16.7 | 19.9
Nominal Accelerating Voltage (MV) | 14,3 | 18,2
Q0 at nominal gradient | > 5e9 | 
Cavity dynamic heat load (W) | 4,9 | 6,5
Qext | 7.5 105 | 7.6 105
 | Medium | High
Iris diameter (mm) | 94 | 120
Cell to cell coupling k (%) | 1.22 | 1.8
p and 5p/6 (or 4p/5) mode separation (MHz) | 0.54 | 1.2
Epk/Eacc | 2.36 | 2.2
Bpk/Eacc (mT/(MV/m)) | 4.79 | 4.3
Maximum. r/Q (W) | 394 | 477
Optimum b | 0.705 | 0.92
G (W) | 196.63 | 241
Challenging accelerating gradients and Q0
No HOM couplers
  HOM frequencies and internal cavity shape must be carefully controlled
Tank (Ti)
Magnetic shielding
Cold tuning system
G. Devanz, J. Plouin,
G. Constanza

## Slide 6: The two prototype high beta cavities
P01 manufactured by E. ZANON (Italy)
P02 manufactured by RI (Germany)
HOM ports only for HOM measurements
Niobium from Tokyo Denkai
Kick-off in Sept. 2012
Trimming operations of dumbbells in presence of CEA staff
Fp = 703.553 MHz
Fp = 703.704 MHz
Design, at 300 K before chemical etching:
Fp = 703.822 MHz

## Slide 7: Field flatness tooling at CEA
D. Roudier
Tooling for high beta ready
Tooling for medium beta
New pieces ordered
Exemple of cavity tuning (High beta Prototype n°2 from RI)
→ adapted for prototypes only (not for large series cavities)

## Slide 8: Chemical treatment set-up
F. Eozenou, C. Servouin
Vertical EP or BCP
BCP
→ Two independant installations compatible with 704 MHz cavities and one is qualified

## Slide 9: Cavity clean room assembly with High Pressure Rinsing
F. Eozenou, C. Servouin
For the moment we have used our “historical” small clean room (Orme des Meurisiers site)
The new clean room (Saclay site) will be equipped with a newly developped HPR system and will be qualified in 2015
HPR 100 bars - Ultra pure water
Flanges and antenna pick-up assembly under class 100 laminar flow

## Slide 10: Vertical test results
High beta prototype cavity n°1 from ZANON
Mounting on vertical insert , Connexion to RF system and vacuum pumping station
Both prototype cavities already met the ESS requirements after the first test
→ Very encouraging results

## Slide 11: Radioprotection improvement for CV tests
Vertical cryostat
Concrete blocks
Eucard / SPL beta=1 704 MHz cavity
at 19 MV/m, radiation level decreased from 50 to 0.25 µSv/h close to workstation (public limit < 0.5 µSv/h)

## Slide 12: Dangerous HOM close to 1408.8 MHz
704 MHz
1421,32 MHz
Slater coefficient
Theory (at 300K) | Measure P01 | Measure P02
1418.178 | 1402.254 | 1407.848
1418.674 | 1404.666 | 1408.258
ESS Requirement (at 2K):
→ HOM at more than 5 MHz from beamline frequencies (here 1408.84 MHz)
Freq (Hz) Q Max. r/Q
1,420314E+09 1,58E+05 8
1,421856E+09 4,30E+03 17
Design
~ same frequency without power coupler

## Slide 13: 3D geometrical measurements
Deviation of 1.4 mm
 Measured shape reconstructed in HFSS
Theory (300K) | Measured on P01 | Calculated with measured shape (HFSS)
1418.178 | 1402.254 | 1403.8
1418.674 | 1404.666 | 1406.8
 The frequency diminution of the two dangerous HOM is understood by a strong internal shape deviation in this region

## Slide 14: Power coupler procurement strategy
→ For the prototype cryomodules, the coupler procurement is divided into three parts
8 x RF window+antenna
→ TOSHIBA
6 x double wall external conductor
→ 2 companies in tender
6 x Door Knob
→ Spec. in progress

## Slide 15: Power coupler conditioning set-up
Assembled in clean room
Tested with a 1.1 MW klystron and variable short circuit / matched load

## Slide 16: Internal cryogenic circuit
bursting disk
Heat exchanger
The circuit is designed to reduce as low as possible the overpressure in case of beam vacuum failure by using a continuous DN100 diameter for the diphasic pipe, large curvatures and 2 DN100 bursting disks at each extremity.
To valve box
Cooling down Valve
bursting disk
JP Thermeau
Regulation Valve

## Slide 17: Instrumentation for prototype cryomodule
DN160 – 3 connectors
Cernox extremity
Pt100-50K extremity + 2 couplers
Pt100-300K extremity + 2 couplers
DN160 – 3 connectors
Cernox extremity + cavity 1
Pt100-50K extremity + 2 couplers
Pt100-300K extremity + 2 couplers
DN160 – 3 connectors
Cernox cavity 2
Cernox cavity 3
Cernox cavity 4
DN160 – 3 connectors
Heater + He level
Motor Cold Tuning System
Piezo Cold Tuning System
DN100 – 2 N-type connectors
RF pick-up cavity 3
RF pick-up cavity 4
DN100 – 2 fiches N
RF pick-up cavity 1
RF pick-up cavity 2
DN100
Vacuum pumping
DN100
Vacuum pumping
(Spare)
DN40
Instrumentation vacuum
DN40
Spare
G. Olivier, C. Darve, N. Elias

## Slide 18: Cavity string clean room assembly
Cart in two parts with clean room rails
Each cavity is supported by two posts and beam valves on one post
Cavity string put under vacuum for the first prototype
Coupler / cavity assembly vertically
Tooling compatible for both cavity types
Adjustment of the coupler position relative to the cavity flange
N. Bazin, C. Madec, JP Poupeau, Ph. Hardy, F. Leseigneur

## Slide 19: Spaceframe and thermal shielding insertion and cryostating
Design of toolings and assembly procedure almost finished

## Slide 20: Test stand new cryolines installation
JP Charrier,
P. Sahuquet,
B. Renard
Dewar LHe
2000 L
Pumping line DN250
Test bunker
(cryomodule will be installed inside)
Cryogenic line
He Supply, 50 m long
(from CERN)
He return line

## Slide 21: 704 MHZ - 1 MW RF power source upgrade
A. Hamdi, M. Desmons, F. Ballester
C’
R’
C//C’=10µF
(Energie=60,5kJ)
R’//R2=25 Ohms
(tenue: 84kJ)
Adding of new capacitors and resistances in parrallel on the HV modulator
Conditionning of the CPI 1.2 MW klystron up to the ESS duty cycle will start soon
Objective: increase the pulse length from 2 ms to 3.5 ms

## Slide 22: Conclusion
Important orders (cavities, couplers) are placed
Good progress in understanding the HOM issues on the high beta prototypes
Compliance with Pressure Equipment Directive (PED) under study for the cryomodule « alone »
  But will we have additionnal external constraints for the full accelerator ?
High power tests of the first cryomodule with medium beta cavities foreseen mid of 2016

## Slide 23: Extra slides

## Slide 24: ECCTD in ESS Superconducting linac
Interfaces with ESS:
  Accelerator Cryoplant
  Cryogenics Transfer Line
  Vacuum system
  RF waveguide and LLRF
  Integrated control Systems
  Machine protection system
  Test stands
Design philosophy:
Segmented:
  Independent cryogenic cooling and control
  Warm-up of a individual cryostat is possible
  Individually removable cryostats for repair is possible
Focusing elements at warm temperature
Cryoline
Valve box
Elliptical cavity cryomodule
Proton Beam
Warmline
Quadrupole

## Slide 25: Cryomodule Development plan
IPN ORSAY in charge of the cryostat,
design and fabrication
Vacuum vessel
Space frame – cavity supports
Thermal screen
Superinsulation
Internal cryogenic pipes
Instrumentation
CEA SACLAY in charge of of the “cavity package”, the cryomodule assembly and RF power tests
Cavities + helium tank
Power coupler design, manufacturing, RF tests
Piezo tuner
Magnetic shield
Tooling: field flatness, cavity preparation, cryomodule assembling, …
Cryomodule assembly
Tests stand for cryogenic and RF power tests
Tests of the ECCTD cryomodule
Design, build and test an Elliptical Cavity Cryomodule Technological Demonstrator (ECCTD)
2012 - 2016: with medium beta cavities
  Work done within the FR-SW agreement
  Collaboration IPNO and IRFU
2014 – 2017: with high beta cavities
  Early In-kind

## Slide 26
Very important : distance between mode and beam harmonics
Qext=105, Q0=108
Qext=104, Q0=104
f (Hz)
Pav. (W)
Power deposited on the non-propagating longitudinal modes
f= 1420.764480 MHz
f (Hz)
Pav. (W)
QL=104
QL=105
QL=106
QL=107
Most dangerous mode : 2nd mode of the 1st HOM L-band at f= 1420.764480 MHz
1408.84 MHz
Max. expected average power for each mode
f= 1409.84 MHz
1 MHz
Pav. (W)
f (Hz)
QL=104
QL=105
QL=106
QL=107
What would happen if this mode was at 1 MHz from the beam line ?
1408.84 MHz
Low power even for
worst cases!
Conclusion: If longitudinal HOMs are more than 1MHz away from beam harmonics:
-no extra damping is necessary
-more damping harmful
26
G. Devanz –WP 4-5 Audit - Orsay

## Slide 27: Fundamental power coupler
Pmax = 1.1 MW peak at 10% duty cycle → critical component
RF ceramic window
  Conical tip for stronger coupling
  Inner conductor (water cooling)
Outer conductor cooled with Liquid He in the vac. Vessel
Coax to rectangular RF transition (Door Knob)
  HV bias with RF trap
Vacuum gauge
Arc detector (PM) air side
Arc detector (PM) vacuum side

## Slide 29: HOM mode identification
Bead pull on ESS086 P02 (03/11/2014) after +/- 0,5mm traction / compression of cell 1

## Slide 30
Cell 1
Cell 2
Cell 3
Cell 4
Cell 5

## Slide 31: Qx calculation
C. Arcambal
Chart: Qext
| 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67
high beta | 392857.16 | 420349.835 | 452206.6 | 488427.455 | 529012.4 | 573961.435 | 623274.56 | 676951.775 | 734993.08 | 797398.475 | 864167.96 | 935301.535
medium beta | 495347 | 534230 | 577562.2 | 625343.6 | 677574.2 | 734254 | 795383 | 860961.2
Double wall external conductor different
(same antenna)

## Slide 32: Magnetic shielding design
J. Plouin
Catia Model Vs simulated model in CST
Material caracterisation used in the studies
At 700 MHz , DRs/DH = 0.3 nOhm/mG.
Goal: limit the magnetic field to DRs max = 4 nW equivalent to:
Bres max = 14 mG = 1.4 µT
Thickness = 2 mm

## Slide 33: Cryomodule elements procurements (by IPN Orsay)
G. Olivier
call for tender started in Dec. 2014
Delivery foreseen in Oct. 2015
…

## Slide 34: Magnetic shielding design
Tesla
Magnetic field on the cavity surface for Hy=40 A/m
Magnetic field on the cavity surface for Hz=40 A/m
Tesla
Tesla
Tesla
Technical specification and call for tender will start beginning of 2015
4 (medium beta) + 4 (high beta) will be ordered
J. Plouin
1 µT
1.5 µT

## Slide 35: Cold tuning system
Saclay V type adapted for ESS cavities
+/- 3 mm range
1+1 piezo
Cold motor and planetary gearbox (1/100e)
Piezo support has a stiffness 10 times higher than the cavity  piezo preload at 2K is independant of the cavity springback force
Type V for SPL beta = 1 5-cell prototype
G. Devanz

## Slide 36: Heat loads
Values in Watts

## Slide 37
Helium cooling scheme of the CM
Special boxes allowing the axial moving and the thermalization of the thermal shield
Vacuum pumping
Cavity tank filling with LHe at 4,5 K
Pumping to produce Superfluid He at 2 K
Thermal shield cooling with LHe at 40 K
Power coupler cooling (outer conductor) with He at 4.5 K – 3 bar (supercritical fluid) → not possible at CEA, cryogenic adaptation to be performed
Power coupler cooling (window and inner conductor) with water

## Slide 38: Pressure vessels European rules
Vessels
Pipes
PS<0,5bar:
The equipment is not on the scope of the 97/23/CE directive
Article 3.3
The equipment must be designed and manufactured according to workmanlike way
Category I
The manufacturing must be more documented, especially with internal production control
Objective: stay within « Article 3.3 » area
50 L
Elliptical cavity
1 bar
Relative pressure

## Slide 39: Helium pressure relief devices
Safety devices
European rules compliance Article 3.3
ESS Helium factory, circuits
and operating modes
Working pressure = nominal pressure
WP
PSET Set Pressure
PS
Maximum allowable overpressure
PS + 10%
Bursting disk
Safety devices
PSET
POPENING = + 5 % PSET
(overpressure when opening)
PMAX APERTURE = + 10 % POPENING
PCLOSING = - 5 % PSET
PMIN CLOSING = - 10 % PCLOSING
(hysteresis before closing)
PSET + 10%
PSET – 10%
Relief valve
Bursting area
Opening area
WP upper limit
Max. allowable press.
Safety margin
Safety margin
1,9 bar
1,431 bar
(1,3 +10%)
1,729 bar
1,301 bar
MAWP 1,58bar
1,670 bar
1,496 bar
1,891 bar
59mbar
65mbar
1,81 bar
Bursting disks
+/- 10%
2,09 bar
Cavity pressure test
1,43 PS
2,72 bar
1,609 bar
1,551 bar
Absolute pressure

## Slide 40: Cryoline design
2 bursting disk at each tip
+ upstream safety relief valve (with he guard)
36°
Heat exchanger
The circuit is designed to reduce as low as possible the overpressure in case of beam vacuum failure by using a continuous DN100 diameter for the diphasic pipe, large curvatures and 2 DN100 bursting disks at each extremity.
A 36° angle is set up for the tank nozzle in order to allow the insertion of the cavity string and the cooling circuit inside the spaceframe
To valve box
Worst scenario: beam vacuum failure
38KW/m2 applied on the cavity wall
Accidental overpressure: 550mbar reduced
to 230mbar after rupture of the disks

## Slide 41
Reflector brackets
(coupler flange)
Reflector brackets
(cavity flange)
Alignment made by laser tracker
Alignment of the cryomodule in the tunnel (source ESS)
1,5" Corner cube reflector
(source ESS)
Reflector brackets
(vessel alignment)
Alignment of the cavity string within 1,5 mm of the beam axis
1
2
3
4
Beam axis reported to reflector bracket on beam flanges
Vessel alignment with respect to cavity string

## Slide 42: Cavity string transfer out of the clean room
Transfer the cavity string from the clean room cart to another support for the post-clean room assembly (40 cm step between the floor of the clean room and the floor of the hall)
Alignment constraints between the rails of the clean room cart and the rails of the post clean room support: 0.1 mm
The loaded post clean room support shall be manipulated with a crane -> mechanical constraints on the design

## Slide 43: Cold mass assembly

## Slide 44: Cryostating