## Slide 1: NON INVASIVE TRANSVERSE BEAM PROFILE MONITORS
Charlotte Roose
AD and ICS Retreat mtg 2014
11 December 2014

## Slide 2: PROJECT
Transverse Beam Profile Monitor of a High Intensity Beam
Non Invasive Methods using the interaction between the beam and the residual gas
Composed of H2 (65-80%) the rest being a mixture of CO, CO2, CH4, Ar and H20

## Slide 3: PROJECT
Ionisation Profile Monitor
Beam Induced Fluorescence monitor

## Slide 4: BEAM INDUCED FLUORESCENCE MONITOR
Space avalaible 10 cm
10-7 – 10-8 mbar
300 K
Energy: from 75 keV to 90 MeV and 2 GeV
H2 wavelength spectrum
Spectrum analysis of a residual gas composed of 98% of H2 interacting with a 95 keV proton beam
[1]
[1] B. Pottin ’Etude d’un profileur optique de faisceaux intenses de protons par absorption laser’, PhD diss, Université Paris Sud, France, 2013

## Slide 5: BEAM INDUCED FLUORESCENCE MONITOR
Fluorescence Yield
Experiment at the COSY facility
  Energy at 45 MeV, 135 MeV, 500 MeV, 1 GeV and 2 GeV
  Around 1010 particles
  H2 gas inject into the ring with a maximum pressure of 10-6 mbar
Notes: COSY is a cooler synchrotron and storage ring for protons in the momentum range between 600 and 3700 MeV/c (corresponding to 175 and 2880 MeV). Protons with the desired energy are available for experiments with the circulating beam ("internal experiments") as well as for experiments with the extracted beam ("external experiments").

## Slide 6: BEAM INDUCED FLUORESCENCE MONITOR
Fluorescence Yield
Experiment at the COSY facility
  Mass spectrometer to check the gas composition evolution
  Test with a filter to cut photons coming from N2 fluorescence
       More in January
Notes: COSY is a cooler synchrotron and storage ring for protons in the momentum range between 600 and 3700 MeV/c (corresponding to 175 and 2880 MeV). Protons with the desired energy are available for experiments with the circulating beam ("internal experiments") as well as for experiments with the extracted beam ("external experiments").

## Slide 7: IONISATION PROFILE MONITOR
Space avalaible 327 cm and 359 cm
10-9 mbar
2 K
Energy: from 90 MeV to 2 GeV
Scintillator screen
  P47 screen with a ITO layer
  P47 screen with an Al layer
  YAG:Ce screen with a conductive layer
  CaF2:Eu screen with a conductive layer
 Degradation ?

## Slide 8: IONISATION PROFILE MONITOR
Space charge influence on the IPM Design
  Dynamic electric field strength produced by a moving bunch was simulated with the use of the Particle-in-Cell solver of CST
  MATLAB routine to track the H+ secondary ions moving in the total electric field
  Preliminary results

## Slide 9: THANK YOU FOR YOUR ATTENTION
This project has received funding from the European Union’s Seventh Framework Programme for research, technological development and demonstration under grant agreement no 289485