## Slide 1: Numerical modelling of cold helium safety discharges from the cryogenic distribution line
Jonathan Persson
MSc. Engineering Physics
AD and ICS Retreat mtg 2014
11 December 2014

## Slide 2: Problem formulation
Failure modes, such as vacuum loss in CDL
System protection
ODH - Oxygen Deficiency Hazard
Is venting from CDL to atmosphere viable option?
My part:
Numerical model to simulate relief pipes
  Various geometries, worst case scenarios

## Slide 3: Linac CDS – function and layouts
Cryogenic Distribution Line (310 m)
comprising 43 valve boxes
Endbox
Cryogenic
Transfer
Line (75 m)
Splitting
box
21 High Beta Cryomodules (174 m)
9 Medium Beta
Cryomodules
(75 m)
13 Spoke
Cryomodules
(54 m)
Linac
Cryoplant
Superconducting section of the Optimus linac (303 m)
Auxiliary process lines
Linac Cryogenic System
Layout

## Slide 4: Problem formulation
Problem setup
  Relief system of valves and burst disk
Main focus on the joint vent line for mechanisms
  Back pressures
Steady-state vs. Transient models
  How well do worst cases correspond?
Heat transfer modeling
  Bare pipe, frosting and air condensation

## Slide 5: End box – 3D model isometric view

## Slide 6: End box in the ESS linac tunnel

## Slide 7: Methods
Main modelling software
  ANSYS Fluent (first ANSYS CFX, OpenFoam considered)
    CAD, Mesh, Pre-processing, Solver, Post-processing
    Good 2D (axisymmetric) modelling
    C-scripts for ”User Defined Functions”
Hepak – reference data software
  Thermodynamic properties of He
  Similar sources for stainless steel and comparable gases
Matlab
  Analytical approximations for verification
  Fanno flow, Rayleigh flow and combination

## Slide 8: Methods – Meshing axisymmetric 2D
Inlet
Centreline
Tri-dominant
Quad-dominant
Inflation

## Slide 9: Methods – Pre-processing
Turbulence: available alternatives
  k-ω (SST/Standard) (Best results for Fanno flow)
  k-ε (Realizable)
  Reynolds stress tensor (k-ε)
  Transition SST (k-ω)
Heat transfer : (Forced convection dominant – Dittus-Bölter eq)

## Slide 10: Post processing - verification cases
Fanno flow
  Only friction (as derived from Moody chart)
Rayleigh flow
  Only heat transfer
Assumptions
  Quasi-1D flow
  Perfect gas
  Constant

## Slide 11: Desired results
Validation & benchmarking
  No experiments found; venting of cold He
  Set of comparable, scalable cases
Transient simulations:
Steady simulations:
Investigation of specification of optimal choice for different setups

## Slide 12: Fanno flow – example comparison

## Slide 13: Fanno flow – example comparison
1D-flow assumption reasonable
  Velocity profile assumed almost flat (except boundary zones)
Model error of 1.3% for mass flow rate,
  Internal error for model 0.2%
  Comparable with assumptions