## Slide 1: RAMI analysis at ESS (RAMI = Reliability Availability Maintainability Inspectability)
Enric Bargalló
ESS accelerator reliability expert
www.europeanspallationsource.se
December 11, 2014

## Slide 2: RAMI definitions
Reliability: Probability of success over a certain period of time
  E.g. probability that the proton beam will not have any trip for one hour
Availability:
Maintainability: capability of performing maintenance to a system or component.
Inspectability: capability to inspect, test and monitor a system and its possible failures.

## Slide 3: RAMI at ESS
ESS goal: science produced by the users
  High brightness neutron beam
  High availability and reliability of the beam
RAMI goals:
  Translate users needs to technical requirements
  Analyze the design to see if the requirements can be achieved
  Propose changes if necessary
  Give a global overview of the future operation of the machine in the design phase

## Slide 4: Users at ESS
22 instruments
Beam time for a user: from 1 day to 7 days
Neutron beam needs:
Kinetic experiments
90% reliability for the duration of the measurement
Failure: Beam trip with a duration of more than 1/10th of the measurement length
Integrated-flux experiments
90% beam availability and 80% average beam power for the duration of the experiments
Beam unavailable: power less than 50% for more than one minute

## Slide 5: RAMI for the users
The global ESS availability figure is not the most important
What is important for them is the distribution of failures:
  Failures (or beam trips) of less than 1 hour can be easily accepted
  Failures from 1 hour to 48 hours are the most problematic
  Failures longer than some days will imply to reschedule the experiments (also happen in reactors)

## Slide 6: Possible kinetic ESS requirements compared with values achieved at SNS
Chart: Duration of the trip
| 1 second - 6 seconds | 6 seconds - 1 minute | 1 minute - 6 minutes | 6 minutes - 20 minutes | 20 minutes - 1 hour | 1 hour - 3 hours
SNS FY13-FY14 | 6.7048 | 9.1881 | 1.4857 | 1.3952 | 0.65714 | 0.20952
ESS requirement | 758.5957 | 758.5957 | 136.5472 | 136.5472 | 12.6433 | 12.6433 | 1.7701 | 1.7701 | 0.50573 | 0.50573 | 0.16858 | 0.16858
Data from SNS provided by Charles C. Peters

## Slide 7: Possible requirements for Integrated-flux experiments (compared with SNS)
Chart: Duration of the trip
| 1h-3h | 3h-8h | 8h-24h | More than 24h
SNS (2010-2013) | 47.3039 | 49.7549 | 24.0196 | 8.3333
ESS requirements | 33.7154 | 33.7154 | 10.5361 | 10.5361 | 4.2144 | 4.2144 | 2.1072 | 2.1072
Data from SNS provided by George Dodson

## Slide 8: RAMI focus
Reduce number of failures (reliability)
  Quality of the components
  Simplicity of the design
Failures of components don’t imply ESS to stop
  Redundancies
  Flexibility (overcapacity, operate at reduced beam power…)
If implies to stop ESS
  Be able to foresee it (inspectability)
  Reduce duration of the downtime (maintainability, spare parts, manpower…)

## Slide 9: How are we going to do it?
Some things can’t be foreseen
  We have to start commissioning and operation
  Might be related to a catastrophic events
  Risks that have been accepted or unknown risks
A lot of things can be only done in the design phase!!
  It might be impossible to change afterwards!!
Many things can be highlighted right now and we can start finding solutions
  The sooner, the cheaper and easier

## Slide 10: RAMI approach
Clarify goals and requirements and allocate the among subsystems
Estimate the accomplishment of the requirements (iterative)
Guide the design, construction, commissioning and operation phases to obtain high RAMI performances
Other outputs
  Maintenance plans
  Manpower
  Logistics and spares
  Estimation of degradation of beam parameters
  …

## Slide 11: Organization
XFWG on reliability
RAMI group
Accelerator
  Enric Bargalló
  Andreas Jansson
Target
  Eric Pitcher
Instruments and science
  Ken Andersen
  Arno Hiess
  Robert Connatser
ICS
  Annika Nordt
Site infrastructure
  Ronny Sjöholm
Systems engineering
  Johan Waldeck
Accelerator
  Enric Bargalló
  Iñigo Alonso
Target
  Alex Garcia
Instruments and science
  Peter Sångberg
ICS
  Riccard Andersson
Site infrastructure
  Björn Yndemark

## Slide 12
Thanks for your attention!

## Slide 13: Kinetic experiments
The key metric is beam reliability: minimize the probability of having a beam trip during a measurement.
Kinetic experiments needs:
A reliability of at least 90% should be provided for the duration of the measurement. The measurement will be considered failed when the beam power is reduced to less than 50% of the scheduled power for more than 1/10th of the measurement length.

## Slide 14: Integrated-flux experiments
The key metrics are beam availability and average beam power
Integrated-flux experiments needs:
At least 90% of the experiments should have at least 90% of beam availability and more than 80% of the scheduled beam power for the duration of the experiments. The beam will be considered unavailable when its power is less than 50% of its scheduled power for more than one minute.

## Slide 15: Reliability data from other facilities
Chart: Duration of the trip
| 1 seg - 1 min (Trips/day) | 1 min - 1 h (Trips/day) | 1h - 3 h (Trips/day) | 3h - 1 day (Trips/day)
PSI | 50 | 20 | 0.4 | 0.1
ISIS | 35 | 0.35 | 0.2
SNS | 200 | 9 | 0.6 | 0.4
LANSCE (H+) | 29.3937 | 8.9477 | 0.49338 | 0.091986

## Slide 16: SNS trip frequency evolution

## Slide 17: PSI: Availability vs. Beam current
Availability decreases with the beam current but increases with facility maturity

## Slide 18: A. Estimate accomplishment of requirements
ESS requirements
Accelerator requirements
Stakeholders
Users
Systems requirements
Experiences in other facilities or experts opinion
Previous analyses
Allocation
Allocation
Individual models
Global model
Top-down
Bottom-up
Redefine requirements
Reallocate requirements
Change design
Requirements allocation and definition
Models and RAMI parameters estimation
Outcomes
Systems and components
Functions
Reliability data
Operations information
Components’ requirements
Availability
Reliability
Failures
Trips
Number of stops and durations
Trips in similar systems
Comparison with other facilities
Trips in similar components

## Slide 19: Requirements allocation
L2
ESS SYSTEMS ‘PROJECTS’
ACC – LINEAR ACCELERATOR (LINAC)
‘ACCSYS’
L4
DISCIPLINE SYSTEMS (Mapping to WBS Work Packages shown)
BMD
Beam Magnets &, Deflectors (BM*)
RFS
Radio Frequency Systems
EMR
EM Resonators
(Bunchers, RFQ, DTL tanks,
CMs)
PBI
Proton Beam Instrumentation
CRYO
Cryo Plant (ACP*) & Distribution (CDS*)
VAC
Vacuum
WTRC
Water Cooling
CNPW*
Conventional Power
SUPPLIED BY WP 6
SUPPLIED BY WP 3,4,5
SUPPLIED BY WP 7
SUPPLIED BY WP 8
SUPPLIED BY WP 12
SUPPLIED BY WP 11
SUPPLIED BY WP 15
SUPPLIED BY WP 15
ISrc
Ion Source
Specialties
SUPPLIED BY WP 3
SUPPLIED BY WP 6,8
PWRC*
PS*, HV Power Convertors*
Labels to identify LINAC sections
Subsystems and components following the PBS
Allocation structure should consider:
  Possibility to track requirements
  Easy to compare with other facilities
  Easy to model and to analyze