## Slide 1: SNS chopper - Approach to the problem, past experience at SNS and proposal for ESS specific conditions.
A. Aleksandrov
Spallation Neutron Source
Oak Ridge, USA

## Slide 2: Outline
SNS chopper requirements
  Purpose
  Requirements
  Implementation
LEBT chopper
  performance and problems
MEBT chopper
  performance and problems
Future plans
ESS chopper thoughts

## Slide 3: SNS Accelerator Complex
945 ns
1 ms macropulse
Current
mini-pulse
H- stripped to protons
Current
1ms
Front-End: Produce a 1-msec long, chopped, low-energy H- beam
LINAC: Accelerate the beam to 1 GeV
Accumulator Ring: Compress 1 msec long pulse to 700 nsec
Deliver beam to Target
Chopper system makes gaps
Ion Source
2.5 MeV
1000 MeV
86.8 MeV
CCL
SRF, b=0.61
SRF, b=0.81
186 MeV
387 MeV
DTL
RFQ

## Slide 4: Why do we need chopper?
End of accumulation
Extraction
To target
Electromagnetic extraction deflector
V=0
From linac
Stripping foil
V=Vmax
Answer: to provide low loss single-turn extraction from the ring

## Slide 5
V<Vmax
volts
time
Vmax
Deflector rise-time
accumulation
extraction
?
Extraction losses
Deflector can’t switch on instantly
Typical rise-time ~ 200ns
Half-deflected beam misses extraction channel and hits the wall
Power of lost beam
Unacceptably high.

## Slide 6
How to mitigate extraction losses ?
Divide beam on separate chunks synchronized with ring revolution period
Gap between chunks longer than deflector rise-time
Switch on deflector during the gap
No beam during deflector rise-time. No extraction losses.
Electromagnetic extraction deflector
V<Vmax
Stripping foil
Revolution period 1us
Deflector rise-time
645ns
300ns
Answer:
Requirements :
beam current in the gap less than 10-4 of peak current
rise/fall time < 50ns

## Slide 7
2.4845 ns (1/402.5 MHz)
260 micro-pulses
645 ns
300 ns
945 ns (1/1.059 MHz)
1ms
16.7ms (1/60 Hz)
15.7ms
Macro-pulse
Structure (made by the Ion Source)
Mini-pulse
Structure (made by the choppers)
Micro-pulse
structure
(made by the RFQ)
SNS Beam pulse structure

## Slide 8: How to make the gaps ?
Answer: use “chopper” (has nothing to do with helicopters or motorcycles)
Possible scheme of a chopper:
deflector
beam absorber
(target)
L
a
HV pulse generator
Gap cleanness depends on:
  deflection angle
  distance to target
  beam transverse size and quality (tails)

## Slide 9: Transients in chopped beam
Rise/fall time of chopped pulse depends on:
  HV pulse generator rise/fall time
  deflector response time
  particle travel time in the deflector
a
t
a,V
In case of electrostatic deflector:

## Slide 10: Why transient time is important?
Answer: transients produce partially deflected beam, which can increase losses in the downstream accelerator
Nominal beam size
Effective beam size during transient

## Slide 11: How to avoid partial deflection losses?
Answer:
  switch on chopper during the gap between bunches
    faster than 2.5ns for SNS
  use anti-chopper to compensate partial kick
  live with losses if they are small enough
chopper + anti-chopper compensation scheme:

## Slide 12: Where to place chopper?
Answer: at low energy
  lower energy beam is easier to deflect
  chopper target has to absorb less power at lower energy
    Example: in SNS 65kV LEBT ~ 50W (800W peak)
    in SNS 2.5MeV MEBT ~ 1.9 kW (32kW peak)
  but not at too low
  difficult to make fast deflector when particles are slow and travel time through deflector is high
Optimized solution : two stage chopping
  remove most of the power at low energy with slow chopper
  clean up gap at intermediate energy with fast chopper

## Slide 13: SNS Front End chopping system
time
MEBT chopper (10ns, 1e-4)
current
LEBT chopper (50ns, 1e-2)
Chopper | LEBT | MEBT
Ion energy | ~25 kV | 2.5 MeV
 = v/c | ~ 0.0073 | .073
Max Voltage |  3 kV |  2.5 kV
gap | ~ 14 mm | 18 mm
Effective length | ~ 27 mm | ~370 mm
Max deflection | 14 o | 1.07 o
Time of flight | ~ 12 ns | ~ 17 ns
Two stage: LEBT + MEBT
Mitigation of partial chopping: compensation using anti-chopper
Compensated by using slow traveling wave deflector

## Slide 14: What other use the SNS chopper has?
Answer: macro-pulse shaping
  cut off beam during the ion source transient
  create single mini-pulse for turn-by-turn measurements in the ring
  decimate mini-pulses (N-on-M-off ) to facilitate injection painting tuning
  ramp up current at the beginning of the macro-pulse to help LLRF system in compensating beam loading effects
Ion source
transient
Chopper
window
single
mini-pulse

## Slide 16: The LEBT chopper:
The 2nd lens in the LEBT is divided into four electrically insulated quadrants, which serve as steerer and chopper
All chopper and steerer voltages operate on top of ~45 kV.
Lens 1
Lens 2
RFQ entrance

## Slide 18: The LEBT chopper: Electric Schematic
Lens 2 supply ~ 45 kV
3 kV 33 mA supply
-
- - -
Ex
Ey
- -
d
3 kV 33 mA supply
3 kV 33 mA supply
3 kV 33 mA supply
Rs
Rs
Cc
Rc
+3 kV 400 mA supply
HV pulser
Quad Gate Driver
EPICS
- 3 kV 400 mA supply
HV pulser
HV pulser
HV pulser
Chopper electrodes have to be AC coupled to the pulse generator
Network of Rs and Cs in oil filled “mixer box” to combine all signal together
Commercial HV pulser custom designed by DEI:
- bipolar
- 3kV max voltage
- 60ns rise/fall time (capacitive load, 150pF + 4’ of RG-59 cable )

## Slide 19
Because of AC coupling 4-Phase deflection scheme has to be used:

## Slide 20: LEBT chopper gap cleanness and rise time satisfy requirements

## Slide 21: Finite transition speed between 4 states during beam-off cycle cause beam leakage
1
2
3
4
Beam-off pattern
1
2
3
4
Nominal chopping pattern

## Slide 22: Experimental verification of using MEBT chopper to clean the “islands”
Single mini-pulse generated with LEBT chopper alone
Single mini-pulse generated with LEBT and MEBT choppers

## Slide 23: MEBT layout

## Slide 25: Slow traveling wave deflector
When beam is deflected by traveling wave, deflection transient depends on relative velocities of particle and the wave:
There are many ways to slow down wave in transmission line: folded lines, dielectric or ferrite loaded line, corrugated line, etc.

## Slide 26: MEBT chopper deflector : slow traveling wave folded (meander) strip line

## Slide 28: The MEBT chopper target
Moly (TZM) target used
Microchannel water cooling
Beam hits at 75 glancing angle
Can dissipate 500 W of average power.
Max energy per pulse: 8.4J (for design beam spot size)
Without LEBT pre-chopping
Tpulse[38 mA] < 88 s
Tpulse[20 mA] < 170 s
Estimated lifetime due to material sputtering: ~100 years

## Slide 29: The MEBT chopper: Electric Schematic
Pos HV supply
HV pulser
Control Interface
EPICS
Neg HV supply
HV pulser
50 
50 
Commercial HV pulser custom designed by DEI:
- two unipolar units
- 3kV max voltage
- 10ns rise/fall time (matched 50 Ohm load)
- 60 A peak current

## Slide 30: MEBT chopper rise time satisfy requirements. Did not measure gap cleanness

## Slide 31: Water cooling of MEBT chopper structure

## Slide 32: MEBT Chopper after anti-chopper removal
Deflector
Target

## Slide 33: Beam scrapers at the entrance

## Slide 34: Damage to MEBT chopper deflecting structure

## Slide 36: New SNS chopper design
35 cm strip-line : 17 ns transient
25% more efficient than old meander line
2x17 cm strip-lines : 8 ns transient

## Slide 37: SNS chopper performance (1MW operation)
High voltage pulse: ~9ns rise time, ~14ns fall time
Beam current: pre-chopper only is in red, pre-chopper and MEBT chopper is in blue
~ 10 ns fall time
~ 15 ns rise time
Measured extinction ratio is < 10-4

## Slide 38: Effect of MEBT chopper on extraction losses

## Slide 39: MEBT chopper target failure in September 2014
Massive water leak in the MEBT during maintenance (no beam running)
Whole MEBT vacuum chamber completely filled with water, pressure relief valves opened
1mm thick wall of cooling channels in MEBT chopper target failed
Resulted in >30days of downtime for clean up and recover
Chopper target was removed making MEBT chopper inoperable
Chopper deflector is still in place to provide scraping functions
  Collecting a list of equipment to put in place of the deflector: scrapers, diagnostics
There is no plans to recover chopper while SNS is operating at up to 1.4MW beam power

## Slide 40: MEBT chopper target after failure

## Slide 41: MEBT chopper target after failure

## Slide 42: Entrance scraper of the MEBT chopper

## Slide 43: Beam current measured on the entrance scraper
HV =+ 50V
Peak current ~ 10uA;
corresponds to 25W peak or 1.5W average power

## Slide 44: Chopper development plans at SNS
New magnetic LEBT for SNS Front End
  Chopper design should be as closed to the existing LEBT chopper as possible. Same HV pulser
  May need to reinstall MEBT chopper If magnetic LEBT chopper will perform worse than the current LEBT chopper
Beam line switch deflector for Neutron Moderator Demonstration Facility
  Should finish design in FY15

## Slide 45
NORTH
MODERATOR DEMONSTRATION FACILITY

## Slide 46
SECTION VIEW THROUGH UPPER BEAM LINE
chopper
Pulse width: 1- 20us
Repetition rate: 60Hz
Rise/fall time: <20ns
Electrostatic deflector
30-40cm long
6-10kV pulse V

## Slide 47: Integrated Test Stand Facility in January 2015

## Slide 48: Relevance of SNS experience for ESS MEBT chopper
How difficult will be incorporating the idea of (new) SNS chopper structure for ESS MEBT (design and fabrication of driver, electrodes, etc.)?
  The new SNS MEBT chopper kicker is very simple to design and easy to build
  The most difficult part was to find suitable vacuum feedthrough

## Slide 49: Relevance of SNS experience for ESS MEBT chopper
2)-In case of using SNS chopper technology for ESS MEBT chopper structure, How difficult will be modification of its power driver based on available standard components in the market (we have 4kV/10 ns with flat top of minimum 20 us)?
  The SNS HV pulse driver still requires significant development to achieve acceptable reliability. Maybe it is easier to start from scratch with modern components
  The SNS HV pulse driver has much higher average power requirements compared to ESS chopper

## Slide 50
3)-Apart from the 'new' SNS Chopper, what do you think as an other mature proven(tested) option of chopper structure and its power supply for ESS MEBT parameters? (considering our limited resources of 1-2 persons and 1-2 years time) First beam tests are foreseen for 2018 in Lund. Considering the developments and Lab. tests we have to perform in-house…
  Electrostatic kicker
    Very simple mechanically
    Only one or two non-RF HV feedthroughs
    No need for HV high power load
    Commercial HV switches are available: 10kV, 50A, 20ns
  Matched stripline kicker with disconnected load
    Commercial HV switches for commissioned
    Upgrade to high power HV driver if needed