## Slide 1: Spoke cryomodule and valve box designs
P. DUTHIL (CNRS-IN2P3 IPN Orsay / Division Accélérateurs)
on behalf of the IPNO team
SLHiPP 5
2015 March 18th
ESS – WP4

## Slide 2: WP4 & CNRS contribution
Valve box
Spoke cryomodule
Cryomodule support
Spoke cryogenic distribution line
CNRS’ contribution:
Spoke cryomodule & Cryogenic Distribution System for Spoke section
    13 cryomodules;
    Spoke Cryogenic Distribution System (CDS):
      13 valve boxes
      Cryogenic Distribution Line (CDL)
      1 end box

## Slide 3: Spoke section: contents
Tooling and test of components
Valve box
Cryomodule components

## Slide 4: The Spoke cryomodule
Vacuum vessel
L = 2.37 m
(2,86 m for CM)
Ø = 1.3 m
 Manufacturing done
     Measured global leak rate: OK
    Dimensional controls have to be achieved before shipment to IPNO
     reception of the vaccum vessel at the beginning of April
Pcrit = 1.2 MPa
 Linear buckling analysis
 Thickness = 8 mm
 Static analysis
σmax = 65 MPa

## Slide 5: The Spoke cryomodule
Cryomodule support
     Support delivered

## Slide 6: The Spoke cryomodule
RF couplers / vacuum vessel interfaces: compensators
Connecting sleeve
RF Coupler double wall
    Goal: To compensate the forces acting on the coupler and due to vacuum forces and thermal restrain. To avoid cavity misalignment
3D printed mock-up of the RF Coupler double wall
     Test of the assembly
3D printed mock-up of the RF Coupler double wall
     Measurement of displacements and forces compensations

## Slide 7: The Spoke cryomodule
Beam line components
 Inter-cavities belows
Cold warm transitions assembly test
 Gate valves
 Cold warm transitions

## Slide 8: The Spoke cryomodule
Cavities support and alignment system
    Supporting system :
    rods based solution
     possibility of adjusting the alignment under vacuum and cryogenic working conditions
    Call for tender of the alignment systems done
    Ordered this week
     Optical monitoring system for alignment diag. inside the cold CM
    Rod made of two parts for cryostating
Inner rod
Outer rod
Elastic interface with the thermal shield
Adjustable interface with the vacuum vessel
    Thermal and thermo-mechanical analysis
     Measurement of the coaxiality of the cavities beam axis

## Slide 9: The Spoke cryomodule
Cryomodule thermal shield
    Call for tender done
    Ordered this week
    Material: Al6060
    Thickness: 2 mm

## Slide 10: The Spoke cryomodule
Cavities magnetic shield
Tuner side ends
Cavity bellow side ends
External shield
Coupler shield
Internal shield
Cooling circuit
Shield support
Shrim
 Material: Cryophy®
    Cooling circuit received
    Magnetic shields to be received by the end of March

## Slide 11: The Spoke cryomodule
RF power couplers
    Leak tests of the couplers and double walls
Double wall tube
(SHe cooled)
RF coupler
(ceramic window)
    Verification of the pressure drops inside the double walls cooling circuits

## Slide 12: Tooling
Example of the clean room tooling for
 assembly of the RF coupler on the cavity:
 assembly of the string of cavities:

## Slide 13: Assembly tooling
Testing of the tooling
3D printed mock-ups of:
the double wall tube
the RF coupler
 Test of the protections and transportation tooling
 Test of the assembly procedure

## Slide 14: Testing-qualifying tools
Conditionning bench for the RF couplers
RF cavity of the conditionning bench
 Integration of the condionning bench at CEA Saclay
Conditionning bench received
(1 doorknob still missing)
Electronics being developped and manufactured at IPN Orsay

## Slide 15: Testing-qualifying tools
Conditionning bench for the RF couplers
  RF cavity: simulating the cooling requirements
Plunger area
Coupler port area
(place of peaks of H field)
Plunger area
RF simulation (ANSYS-HFSS)
Stainless steel cavity
Cooling circuit
Fluid
PRF = 400 000 W; DC = 5%
Water mass flow rate: 3.6 g/s
Thermal simulation (ANSYS)

## Slide 16: Testing-qualifying tools
Conditionning bench for the RF couplers
  RF cavity: preliminary test of the cooling capacity
IR heating inside the cavity
Radiated heat: up to 1 kW for the tests
    Verification of the pressure drop inside the cooling circuits
    Verification with the simulation
    (rough agreement)

## Slide 17: Spoke Cryogenic Distribution System
    13 cryomodules;
    Spoke Cryogenic Distribution System (CDS):
      13 valve boxes
      Cryogenic Distribution Line (CDL)
      1 end box
Prototype valve box
courtesy of ess

## Slide 18: Spoke valve box
PID
Machine
version

## Slide 19: Spoke valve box
PID
Prototype
version
Main differences:
instrumentation
He and N2 supply
   RF coupler cooling:
  Cold vapours used
  (but SHe in HNOOS FREIA)
Interfaces with the infrastructures

## Slide 20: Spoke valve box
PID
Proto
version
From a liquefier

## Slide 21: Spoke valve box
UPPSALA / IPNO integration
  Studies of the integration of the valve box (and the Spoke CM):
    at IPNO site (SUPRATECH technological platform)
    at FREIA test stand in Uppsala.
  Cryogenic interfaces
  To be validated with Uppsala
Interfaces for the supply of cryoliquids
Interfaces for the vapours exhausts

## Slide 22: Prototype valve box
Valve box connection to the cryomodule: the jumper
Vacuum barrier
    Mech. Analysis (pressure forces + thermal shrinkage)
    Thermal analysis
    0.25 W @ 2K
    7.4 W @ 50 K

## Slide 23: Conclusion
Crymodule components
  Mechanical package: all components received except:
    vacuum vessel, cavities supporting system and thermal shield
    qualification of components under progress
  Assembly phases started
    start of real components assemblies
    but also test of the assembly procedures
Spoke prototype valve box
  Specifications for the heat exchanger and the cryovalves are being written
    → to be ordered by end of April
  Detailed design of the valve box is still under progress (finalizing)
    Detailed drawing started
    Technical specifications to be written
  Goal: to order the valve box this spring
  cf. S. Bousson’s presentation on Spoke RF cavities and cold tuners

## Slide 24: Thank you for your attention This work was achieved by the WP4 IPNO team:
CSP12
28 Novembre 2014
Sébastien BOUSSON Sylvain BRAULT Patricia DUCHESNE Patxi DUTHIL Nicolas GANDOLFO Guillaume OLRY Matthieu PIERENS
Emmanuel RAMPNOUX Denis REYNET
Jérôme DAULT
Frédéric CHATELET
Virginie LAURENCIER
David LONGUEVERGNE
Richard MARTRET
Thierry PEPIN-DONAT
Véronique POUX
Fetra RABEHASY
Ludovic RENARD
Philippe SZOTT
Elodie MOUREY