## Slide 1: ADS Project and Material Irradiation Facility in China
Yuan He
On behalf of ADS Linac Team
Institute of Modern Physics, CAS
Notes: This talk is based on the experience and understanding on our demo linac and SARAF

## Slide 2: Outlines
Introduction of CIADS
R&D Progress of CIADS
Introduction of CMIF
Summary

## Slide 3: Motivation (development of NPP in China)

## Slide 4: Nuclear Fuel Cycle (IAEA-TECDOC-1613)
ADS + Close Cycle is better at burning waste.
Total radiotoxicity of spent fuel relative
to that of natural uranium ore.
Used fuel  Open Cycle (~300,000y)
Open
Cycle
Close Cycle
ADS+Close Cycle
Pu & U removed Close Cycle (~5000y)
Pu, U, & MA removed  ADS + Close Cycle (~300y)

## Slide 5: Roadmap of ADS project in China
“Strategic Technology Pilot Project”
of the Chinese Academy of Sciences
Key technology R&D
Y2011-2017, 1.78 B CNY
Stage 1: Research facility (CIADS)
(250 MeV, 10 mA, 10 MWt)
Y2017-2022, 2.25 B CNY
Stage 2: Demo facility (CDADS)
(1.2~1.5GeV, 10~25 mA, 100 MWt)
Y2030
Goal in 2015.06, 5 MeV
Goal in 2015.12, 10 MeV
Goal in 2016.09, 25 MeV
2014.06, 2.1 MeV/10 mA/CW
Injector II, 162.5 MHz
Injector I, 325 MHz

## Slide 6: High power SRF Linacs in the world
Existing SC machines
Under construction SC machines
Planned SC machines
Non exhaustive plot!
CDADS

## Slide 7
New Project CIADS (2017-2022)
Proposal listed in the “twelfth-five plan for large scale research facility
Budget: ~2.25 B CNY
LINAC: 250 MeV@10 mA with CW mode
Spallation Target: granular flow spallation target, 2.5 MW
Sub-critical core: 10 MWt
Location: Huizhou, Guangdong Prov.
China Initiative Accelerator Driven System

## Slide 8: Accelerator configuration of CIADS
Freq. | 162.5 | 162.5 | 325 | 325 | 650 | MHz
βg | 0.1 | 0.15 | 0.21 | 0.4 | 0.63 | -
Aperture | 40 | 40 | 50 | 50 | 100 | mm
Uacc | 0.78 | 1.82 | 1.64 | 2.86 | 10.3 | MV
Epeak | 25 | 32 | 24/31 | 25/32 | 29/38 | MV/m
Bpeak | 50 | 40 | 50/65 | 50/65 | 50/65 | mT
Temp. | 4.5 | 4.5 | 4.5 | 2 | 2 | K
Ploss | 10 | 10 | 10 | 6.5 | 21 | W
Number | 6 | 6 | 28 | 72 | 28 | 
Resonators of SRF Linacs
ECR ion sources
Particle | Proton | 
energy | ~250 | MeV
Max current | ~10 | mA
Max beam power | ~2.5 | MW
Duty factor | 100 | %
Beam loss | <1 | W/m
energy | 35 | keV
emittance | 0.2 | mm.mrad
Max current | 15 | mA
Energy of exit | 2.1 | MeV
frequency | 162.5 | MHz
Long. Emitance at exit | 0.09 | MeV.deg
RFQs
Two injectors Down Selection
162.5 MHz RFQ+HWR
Main Linac, spoke, ellip, 250 MeV
Main Parameters

## Slide 9: Location of CIADS
CIADS
CSNS
Daya Bay

## Slide 10: Outlines
Introduction of CIADS
R&D Progress of CIADS
Introduction of CMIF
Summary

## Slide 11: Demo of SRF LINAC for CIADS in 2011-2016
162.5 MHz HWR010
325 MHz Spoke021
~25 MeV, Sept. 2016 – 2017
Cooperate with IHEP
1
2
3
4
ECRIS + LEBT + RFQ + MEBT + TCM1, 2.5 MeV
RFQ commissioning, validate CM design.
Ongoing to CW at 10 mA
162.5 MHz HWR010
ECRIS+LEBT+RFQ+MEBT+CM6, 5 MeV
Beam commissioning in March 2015
162.5 MHz HWR010
ECRIS + LEBT + RFQ + MEBT + 2xCM6 +HEBT, 10 MeV
Dec. 2015—Feb. 2016
162.5 MHz HWR010

## Slide 12: Commissioning of 162.5-MHz CW RFQ
June 30th, 2.1 MeV/10 mA/CW, 4.5 hours, 21.6 kW, efficiency is 95%
Total operation time is ~900 hours, including CW@10mA around 10 hours；Record of non-trip operation is ~220 hours
Details will presented by Dr. Zhijun Wang

## Slide 13: Commissioning of MEBT and TCM(HWR)
Sept. 29th, 2014, first beam from TCM1, 2.6 MeV, 2.3 mA, Transmission ~100%
Feb. 13th, 2015, 2.55MeV/~11mA/CW, 28kW.
Total operation time was ~ 200 hours. The non-stop operation is ~46 hours.
Details will presented by Dr. Zhijun Wang
4K and HWR technique proven, injector

## Slide 14: Commissioning of 325-MHz Linac
Pules: 11 mA, 50 Hz, duty factor>90%
Efficiency > 97%（duty factor 70%）
Energy 3.2 MeV, average power > 31 kW
Two spokes
Pules: 10 mA, 30~130 us, 1 Hz
Efficiency > 99.7%
Energy 3.61MeV
2K and spoke technique proven, main linac

## Slide 15: Status of SRF Resonators
Chart: Ellip063 @4.2K
HWR010@4.2K
Spoke012@4.2K
Spoke021@4.2K

## Slide 16: Reactor and target coupling of CIADS
LBE coolant sub-critical reactor
Pipe of target goes through and is insulated with reactor

## Slide 17: High Power Targets
? : tens of MW
Liquid target
Solid target:
rotating target can enlarge relatively the beam spot
Porosint target:
Packed beds (rod, ball, etc), increasing coolant contact surface.
Beam intensity：
<10 μA/cm^2
Beam intensity ：
<50 μA/cm^2
Beam intensity ：
<20 μA/cm^2
Beam intensity ：
？>500 μA/cm^2
rotating target
For HP-target, now the off-line heat exchange is one of best choice.

## Slide 18: Granular Target

## Slide 19: Target test with electron beam
Power density on target is comparable with the proton beam of 2.5 MW or much higher.
Tungsten particles <1000kg
Heat exchanger
<20mA@2.5MeV e
Target
Lifter setup

## Slide 20: Granular Target Testing Setup
Target: tungsten granular, windowless, vacuum differential
Beam: 25 MeV, 10 mA, 250 kW
Lifter: mechanical
HEBT of 25 MeV
Vacuum differential
Notes: 20

## Slide 21: Outlines
Introduction of CIADS
R&D Progress of CIADS
Introduction of CMIF
Summary

## Slide 22: Material problems in fusion reactor
Gen. II & III
SCWR
VHTR
LFR
GFR
SFR
MSR
FUSION REACTOR
The accelerator-based neutron source can simulate 14 MeV neutrons from Deuterium-Tritium fusion reactions rather than fission reactors.

## Slide 23: Concept of IFMIF
The International Fusion Materials Irradiation Facility (IFMIF) | 
Target | High Neutron Flux High Neutron Yield 10 MW Liquid Li Jet Target
Beam | 40 MeV@125 mA *2 (CW)
Radio Protection | integral neutron flux ~2*1017 n/s
IFMIF technology is very challenging (125 mA accelerator; jet target)
High Cost , budget €665M (2003)  >€1B (2012)
Long Time (Operational>2028)

## Slide 24: Concept of CMIF
New fluidized granular Beryllium alloy target system for high power density in small size;
Based on techniques of Chinese ADS project .
The Compact Materials Irradiation Facility in China(CMIF) | 
Target | High Neutron Flux Low Neutron Yield Small Sample Size ~1 MW granular Be Target
Beam | 50~100 MeV@(5~10) mA (CW)
Cost | Low
ECR
RFQ
Superconductor DTL
LEBT
MEBT
Superconductor Linac
HEBT + scanning + Vacuum differential
sample
Granular Target
Dense granular flow
Heat exchanger
Granular lift system
Granular deposited

## Slide 25: Neutron yield compare
For different D energy, the neutron yield on Be target and Li targets.
Angular distribution:
Thin targets
40 MeV D+Be/Li

## Slide 26: Simulation of flux at the sample
Simple 1：from back 1 mm
Simple 2：from back 10 mm
Deutron beam
Energy spectrum
 | Energy | 20 MeV | 50 MeV
1 | Flux (D-Be) | 3.6*1013 @ 5 mA | 1.99*1014 @ 10 mA
 | Y (n·cm-2·mA-1·s-1) |  | 
 | Flux (D+Li) | 2.41*1013 | 7.85*1013
2 | Flux (D-Be) | 9.81*1012 @ 5 mA | 7.54*1013 @10 mA
 | Y (n·cm-2·mA-1·s-1) |  | 
 | Flux (D+Li) | 7.79*1012 | 3.96*1013

## Slide 27: Development roadmap of CMIF
 | Specifications | Cost and Time | dpa/year |  |  | 
Phase I (Test Facility) 2014-2018 | 100kW=20MeV @5mA | ~35 M$ 4.5 years | Sample size L╳W╳H(mm) | 30╳30╳10 | 20╳20╳5 | 10╳10╳2.5
 |  |  |  |  | 2.5 | 8.5
Phase II (User Facility) | 500kW~1MW=50~100MeV @(5~10)mA | +2.5 years | Sample size L╳W╳H(mm) | 30╳30╳10 | 20╳20╳5 | 10╳10╳2.5
 |  |  |  | 15.4 | 30.2 | 93

## Slide 28: Compare between IFMIF and CMIF
 | IFMIF | CMIF
Reaction Channel | D+Li | D+Be
Deuterium Beam | 40 MeV@125 mA*2 | 50~100 MeV@(5~10) mA
Neutron peak Energy | ~14 MeV | ~14 MeV
Sample Size | ~10 cm | 1~3 cm
dpa | 20~50 dpa/year | 20~50 dpa/year
Neutron Total Yield | High | Low
Technical challenges | 125 mA LINAC | ~10 mA SRF LINAC
 | 10 MW liquid jet target | 0.5~1 MW granular Be target*
 | Large Sample Size Large Scale Facility High Radiation Dose High Construct & operation cost | Small Sample Size# Small Scale Facility Low Radiation Dose Low Construct & Operation Cost
 |  | Based on Chinese ADS Tech; Short time of Construction period ~7years
#Small Sample techniques need to be developed
*The international patent application in processing

## Slide 29: Outlines
Introduction of CIADS
R&D Progress of CIADS
Introduction of CMIF
Summary

## Slide 30: Summary
Chinese Initiative ADS project (CIADS) will be approved. 250 MeV SRF proton linac, Granular target and 10 MWt subcritical LBE FR are chosen.
A demo SRF linac with 25 MeV/10 mA/CW will be build in 2016 and coupled with granular target.
The prototype of 2.5 MeV/10 mA/CW SRF linac is in operation around 200 hours, 11 mA/CW/1 hr was achieved.
Material Irradiation Facility in China (CMIF) was proposed. It is a compact, high-flux neutron source base on D-Be reaction and SRF linac.
The first stage of CMIF is supported by MOST. A 20 MeV/5 mA SRF linac of Deutron will be built in 2018.

## Slide 31: Acknowledgements
Thanks for your attention
&
Team of China ADS Linac
Thanks for the helps
from LBNL, ANL, J-Lab, MSU/FRIB, FNAL, ORNL, TRIUMF, CEA/Saclay, IPN/Orsay, IAP, RIKEN, KEK, ……
HIT, PKU, SINAP,……
Welcome Collaboration!