## Slide 1: HNOSS: first results and FREIA status
Rocío Santiago Kern
FREIA Laboratory, Uppsala University
19th of March 2015

## Slide 2: What and Whom?
cryogenics
- liquid helium
- liquid nitrogen
control room
- equipment controls
- data acquisition
RF power sources
3 bunkers
with test stands
horizontal cryostat
vertical cryostat
Facility for Research Instrumentation and Accelerator Development
Competent and motivated staff
collaboration with physics (IFA), engineering (Teknikum), TSL
and Ångström workshop
Funded by KAWS, Government, Uppsala Univ.
State-of-the-art Equipment

## Slide 3: Responsibility for ESS Accelerator
Development power station for spoke cavities
  soak test with water cooled load, then accelerating cavity, incl. controls
  collaboration with industry to develop vacuum tube and solid-state based prototypes
System test, power station with spoke cavity and cryostat-module
  fully dressed prototype cavity (in test cryostat)
  complete prototype module (2 spoke cavities)
  test of switch-on procedures & LLRF
Acceptance test spoke cryostat-modules
  all spoke cryomodules before installation
Test of 704 MHz modulator and klystron
  prototype and pre-series
Funded by ESS

## Slide 4: The Test Stand
Three main subsystems needed
RF Power Station
Cryostat
Cryogenics
Spoke Cavity
(superconducting)
Courtesy of P. Duthil
Bunker
To avoid radiation in public areas:

## Slide 5
HNOSS: 1st Results

## Slide 6: Flow Scheme & Vacuum Barriers
Valve box
Horizontal Cryostat
Supercritical Circulation
Inter
Connection
Box
Valve box &
Cryomodule
2K and 10 K
Heater
2K pumps
Gasbag
Storage Dewar
Cold Box
Outside
building
300 K
1.1 bar
He 10 K 1.1bar
He 4 K 1.2bar
LN2 80K 1.4 bar
He 300 K
3 bar
N2 300 K
1.1 bar
He 5 K
16 mbar
He 300 K
17 mbar
He 300 K
1.1 bar
Bunker

## Slide 7: ICB
Total volume ICB+ TL < 1 m3
The interconnection box (ICB) is to switch cryogens between HNOSS and the cryomodule.
The ICB has a thermal shield cooled by LN2
The ICB vacuum includes also the transfer line (TL) to the VB

## Slide 8: HNOSS
Has two parts:
  Valvebox (VB): contains all the valves and tanks and most of the piping
  The cryostat itself (HCS): houses the cavities and the table
Both parts have:
  Magnetic shield (room temperature)
  Thermal shield (LN2 temperature)
Total volume ca. 7 m3
The GHe outputs (low and high pressure), can be independently connected to:
  The main compressor of the LHe plant
  The gasbag

## Slide 9: Cavities
Simple double-wall cylinder
Approx. same LHe volume as double spoke
No beam vacuum
CF 40 connection for 2K tank
CF16 connections for cooling and LHe level probe
3 heaters installed for RF power simulation
Dummy Cavity
Single spoke
Courtesy of IPNO
With beam vacuum
Two RF antennas
Preparing for tests
Hélène

## Slide 10: Dummy Cavity Installation
Insert cavity with support table
Connect tie-beams, lift and remove table
Connect rest of cryogenic piping

## Slide 11: ICB Vacuum
P [mbar]
LN2 cooling start
Pump down time from 1000 mbar to 1x10-3 mbar : 15h
Outgassing?
LN2 leak in ICB
Pumping group: 80 l/s turbo pump backed by a 5 m3/h scroll

## Slide 12: ICB Vacuum
P [mbar]
Pressure bursts from LN2
For next run: regulated pressure between 1.5 bar and 2 bar
Pressure bursts between 1.5 and 4.5 bar generated in the phase separator

## Slide 13: HNOSS Vacuum
P [mbar]
Pumping group: 1000 l/s turbo pump backed by a 30 m3/h scroll
LN2 cooling start
Pump down time from 1000 mbar to 1x10-4 mbar : 24h

## Slide 14: Thermal Shields
T [K]
ICB
HNOSS
VB
HNOSS’ doors
VB top flange
Cool down time for ICB (290K to 100K) : 1.5h
Cool down time for HNOSS (290K to 100K): 26h
BUT to be reduced once there are no pressure bursts in the LN2 circuit

## Slide 15: Heat loads
Validating sequences of the control system for HNOSS  not possible to give proper values.
A very coarse approximation: 10h from LN2 temperatures to the steady state.
The steady state is defined as:
  Table temperature stable,
  Flow from the 2K tank < 5 m3/h and
  Dummy cavity, 4K and 2K tanks filled with LHe at 4.5K
Preliminary values for the heat loads:
  7.2 W for the 4K tank,
  4 W from table (at 4K),
  1 W at 2K for the 2K tank and dummy cavity

## Slide 16: 2K pumps
Two modes of operation
  Pressure regulation: not used (butterfly valve in place)
  ”Maximum speed”: normal mode of operation
Have reached 2K in the dummy cavity
Pumping speeds
  7250 m3/h at 10 mbar (required 7180 m3/h, 3.2 g/s)
  6747 m3/h at 15 mbar (required 5900 m3/h, 4 g/s)
  1120 m3/h at P > 200 mbar
  (required, not measured, 10 g/s)
Ultimate pressure 0.19 mbar
Maximum capacity at 2K: 110W
(by means of power applied to the heaters)

## Slide 17: Details to Consider
Loss of temperature sensors at low T
Long cooling times
Problems with pressure regulation of the 2K tank coming from Taconis effect
Redundancy is neccesary
Hopefully to be solved by the pressure changes in the LN2 phase separator
Most probably due to the safety valve of the 2K tank. Will add a heater close to 2K tank, where the safety valve line starts

## Slide 18
FREIA Status

## Slide 19: High Power RF Amplifiers
4 systems foreseen to come in operation during 2015
  1st contract with Electrosys (target delivery end May)
    long delays (bankrupt Spring 2014)
    company has finally restarted (new name: Itelco Broadcast)
    legal problems regarding ownership of Thales tubes (could again delay project)
  2nd contract with DB Electronica (target delivery end May)
    different concept regarding power supplies: in-house design as compared to Electrosys using standard catalogue items from sub-contractors
    same solid-state pre-amplifier as CERN Linac 4 design
  Borrowed 50 kW amplifier from CERN (arrived 18-Feb-2015)
    commissioning start next week
    to test RF equipment & procedures
  Siemens solid-state (target delivery end May)
    R&D by Siemens itself
    4 racks of 100 kW amplifiers
    testing start foreseen in April

## Slide 20: RF Measurements
Typical measurements with the bare cavity:
Loaded Q-factor,eigen and external Q, Q0=f(E)curve
Lorentz detuning and microphonics
Sensitivity to helium pressure fluctuations
Achieve nominal gradient and nominal Q0
RF measurements with self-excited loop
Complete the design and setting up of the self exited loop
(now hooked to a home-made copper cavity)
Calibration and digital phase shifter under development
Stub-Tuner
To reduce required RF power by increasing Qext : present RF source is 50 kW compared to min. required 100kW (large Q0)
A matching network in the form of a waveguide-based stub tuners is under development
2R
L
L
to cavity
from a source
L = lambda/8

## Slide 21: Solid State Amplifier
Single ended RF Power Amplifier (BLF188XR) tested in pulsed mode at 14 Hz and 3.5 ms
amplifier slightly modified on RO3003 for series production
Max efficiency: 67% (pulsed)
Gain: 19 dB
Independent measurements at NXP
Individually: delivering up to 1500 W
Two combined: Delivering up to 1700 W
Max efficiency: 50% (1 dB IL in the output combiner)
Working on improving values
1 kW level hot-S
parameter measurements
100 kW radial power combiner
30 mm
500 mm
output coupler connected to 3-1/8 inch coaxial line
7/16 inch input connector

## Slide 22: Control Systems
Control system and interlock development ongoing
  EPICS as main interface
  Siemens PLC and Nat.Instr. cRIO hardware
  connects all sub-systems to one user interface and archive database
  safety interlocks for all sub-systems
(Radiation) safety system installation ongoing
  Rotem MediSmarts hardware
LLRF
  in-house development LLRF (Nat. Instr. PXI based with LabVIEW)
  digital phase control of Self-excited Loop
  RF power measurement and control
    complementary to Lund Univ./ESS LLRF (minimal system as required in accelerator)

## Slide 23: Conclusions
Received single spoke cavity Hélène (courtesy of IPNO)
  To test our procedures until the double spoke comes to FREIA
  RF measurements at room temperature: resonance frequency at 360.04 MHz and bandwidth of 100 KHz = IPNO measurements
Right now:
  Hélène almost ready to be cooled and tested next week
Planning:
  Bare double spoke prototype : approx. mid April
  Dressed double spoke prototype: approx. end May
  Double spoke cryomodule: approx. end of the year
This means that:
  We won’t be bored