## Slide 1: Helium Purification
Håkan Carlsson
WP Manager Fluid Systems
Per Nilsson, Leif Emås
www.europeanspallationsource.se
1 April 2015

## Slide 2: Outline
Purposes
Old (TDR) baseline
New system design (for Target Change Control)
Conclusions

## Slide 3: Purposes of chemical purification
Remove spallation products, e.g. 3H and 125I (mainly produced in target, ~ 2, 0.3 g/year )
Remove moist air leaking into monolith, N2, O2, Ar, H2O
Particles / dust is removed by filters, mechanical purification - not detailed here!

## Slide 4: TDR baseline
Monolith Loop
40 m3, 1 bar
6 kg Helium
Target Loop
20 m3, 3.6 bar
9 kg Helium
Seal
3.8 bar
0.1 mg/s He
18 mg/s Air
3 g/s He
7 g/s He
Target
PCS
Monolith
PCS
7 g/s He
3 g/s He
Monolith
Purification
Target
Purification
Contaminants
(mainly spallation products form target)

## Slide 5: TDR Baseline features
Conservative seal and leak flow estimates
Some H2 chemistry (mainly for steel), ~ 10 ppm
Separate purification systems Target & Monolith - Target: CuO + Mol.-Sieves + Cryotrap - Monolith: Mol.-Sieves
ppm levels of impurities

## Slide 6: New system principle
Monolith
95 m3, 1 bar
15 kg Helium
Target
20 m3, 10 bar
23 kg Helium
0.23 mg/s
4 μg/s Air
1 g/s
Circulating and cooling system
Circulating and cooling system
80 mg/s
He purification
(getter)
Contaminants
Contaminants
30 mg/s
Purity performance
I2
H2
O2
N2
CO2
H2O
He purity in
Helium loops: >99.9%
(72 g/year)
(6.58 kg/year)
3 kg/s
40 g/s
PCool
MonAtm
Target wheel rotary seal
< 1 ppb
< 1 ppb
< 1 ppb
< 1 ppb
< 1 ppb
< 1 ppb
Mix

## Slide 7: Important parameters for sizing the system
Leakage Out of Target Cooling Loop = 0.23 mg / s
  Based on (ESS-0012524):
    Data from two different valve suppliers
    Sum of leakage from all flange joints
Leakage In to the Monolith Helium Tank = 4 μg/s Air
  Based on (ESS-0025649) and largest value of:
    Sum of leakage from all flange joints
    SNS data scaled to ESS (size & pressure)
No H2 chemistry needed for the steel pipes and components
  (Literature study, Target Material Group)

## Slide 8: New system features
Improved designs (seals) and estimates
Only one purification system, much smaller (waste!)
Removed H2 chemistry, not needed
Orders of magnitude less impurities (ppb) after getter purification
Can operate in batch, can be out for one week, good for availability
Sizing depends on leak rates out of Target (beneficial) and into Monolith (demanding) not so much on rotary seal flows
Notes: H2 chemistry – Material group ESS, no problem with corrosion

## Slide 9: Example equipment (off the shelf)
Heated getters

## Slide 10: Preliminary Results
Can maintain 99.9 % purity
Can keep releases below ~ 10 TBq / year (all species)
Can stay below dose limit, 3,5 µSv/year
Detailed calculations of all species will be made

## Slide 11: Conclusions/Questions
Natural improved development, going for Best Available Technique (BAT)
Decreased risks, costs and release/waste
Relies on reasonable tightness requirements
Maintenance & Accidents to be studied
t-TAC
Are the new design developments for the helium purification system sound and do they represent a reasonable balance between system performance and other parameters, e.g. manufacturability, operability, maintainability, cost, schedule, upgradeability, and flexibility?