## Slide 2: Experiment Control and Data Curation Overview / Keywords / DAQ & Controls
PRESENTED BY Tobias richter / DMSC instrument scientist workshop

## Slide 3: Idea of Day 1 and this Presentation
interactive with hands-on
learn things that are valuable to have some idea of
    some things you may need day to day
    others are background knowledge useful for commissioning and diagnostics
    no need to remember everything
    there will be maintenance and support in operations
software will not be used in exactly the current format – feedback welcome
this presentation: concepts and general overview (fun comes later)
Ymir (B02) is soon ready for more in depth individual sessions

## Slide 4: ECDC Scope
  Experiment Control
  Beamline and Device Controls mostly via EPICS in collaboration with ICS WP12 and technology groups
  Data Acquisition – Readout and File Writing
  Detector Software Event Formation
  Data Management / Curation
Experiment Control and Data Curation
Image credit: Jason Sultana https://formulaoneinsights.com/the-formula-1-car-cockpit/

## Slide 5: Low Level Control and Engineering Interfaces
Three types of interfaces:
User The average facility user
Expert An expert user, also often the instrument scientist
Engineering ESS support staff with special needs outside of running an experiment
We aim to cater for users and experts in NICOS.
The ideal way to support engineering tasks for a specific device depends on many factors.
Maintenance and Operations
CSS/Phoebus/EPICS interface example

## Slide 6: Flow of an Experiment
From an earlier UX workshop
Introduction to instrument
Set up initial measurement
Run measurement
”Look” at data
Adjust settings
Start measurement
Coffee time / analysis
Stop measurement
Prepare next measurement

## Slide 7: Experiment Control Programme
Integrated high level interface and device abstraction to low level EPICS controls.
  Python CLI
  Qt user interface
  Extensible and customizable
Current activities:
  baseline UI delivery for ODIN and BIFROST
  filewriter control and configuration
  sample and proposal information
NICOS

## Slide 8: Motion Control
To simplify requirements and implementation common motion types have been classified and MCAG and ECDC have decided which functionality to implement at which level.
Until November the following standard options should be integrated and verified:
  Pneumatic Axis
  Discrete Positioning
  Continuous Motion
  Slit System
  Special Cases are allowed and instruments are encouraged to highlight them as soon as possible.
Standard Classes for Most Typical Applications
NICOS
EPICS IOC
Beckhoff PLC
Motor
Encoder

## Slide 9: ESS Controls (and Readout) Architecture
Old, but still somewhat true

## Slide 10: NSS/ICS Interface (Simplified)
ECDC
Motion Control and Automation Group
LOKI
ICS WP12
DREAM
ODIN
TBL
ICS WP07
Infrastructure
ICS WP04
Hardware
BIFROST
CSPEC
ESTIA
MAGIC
BEER
NMX
HEIMDAL
SCADI
FREIA
TREX
MIRACLES
VESPA
ICS WP03
Software
Neutron Choppers
Neutron Detectors
Sample Environment
DMSC DST
DMSC DRAM

## Slide 11: Choppers
Timing & Control
  Highly standardised ESS-PLC (CHIC) Interfaces with timing system Independent of spindle vendor
  Alarms and archiver needed for engineer use
  For users there will be a higher level interface for an entire chopper cascade
  Already quite well tested. Verified that commissioning can be done “cold” with light (laser).

## Slide 12: Timestamping Chopper TDC pulses
Recorded in the EVR

## Slide 13: Detectors
Also standardised interface: Detector backend master by the NSS detector group
Provides:
  Timing integration with frontends electronics
  High rate data path – direct to DMSC/ECDC event formation
  Slow Control interface via EPICS
Beam Monitors (single pixel detectors) operate in a similar way.
Time-of-flight event-based

## Slide 14: Detectors
Detectors need software to do
  Control of the detector electronics, power supplies and other infrastructure (gases, etc)
  Online processing of detector output
  Store information about the pixel (voxel) positions in space at all times for downstream processing
In addition
  All other (meta-)data needs to have timestamps to be able to correlate neutron detection with other events
  Imaging (ODIN) will use cameras as well as time-of-flight detectors
Event Formation and Slow Control
EFU processed (and corrected/calibrated) data from LoKI tubes, straight from the frontend electronics
Nexus geometry model for the DREAM detector

## Slide 15: Instrument Readout Streaming Architecture
BrightnESS is funded by the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 676548
Site Infrastructure
Instrument Hardware
Motion
Chopper
Detector Backend
Event Formation Unit
EPICS FW
NeXus File Writer
Live Feedback
Time
Time
EPICS
100 GB/s fibre
Connects many different services and sub-systems
Experiment and File Writer Control
Data Aggregation Cluster (Kafka)

## Slide 16: Live Operation Demonstrated
  Integrated LoKI detector and LAMOR beam monitors through readout master to Software Event Formation
  Diagnostics and commissioning tools available
  Was beneficial to have relatively well defined goals for the experiment.
  Three days of beamtime is short, which is a challenge. Thankfully no major problems.
  Learned various valuable lessons, mainly about what to agree, test and prepare in advance (mostly ECDC internal scope)
LoKI detector and LAMOR beam monitor data
LoKI @ LAMOR

## Slide 17: Let’s talk about files

## Slide 18: “Traditional Files”
One Aggregated Readout per Scan Point, Angle, or Setting

## Slide 19: Data Acquisition
rotation_angle
temperature
polarisation
time
Every data source sends their information independently asynchronously:
  detectors & beam monitors in event mode
  cameras
  choppers
  motion
  sample environment (temperatures, pressures, fields)
Data only updated on change.
Flexible, sparse efficient storage, little hardware support needed, adequate timing synchronisation is critical.
Post processing needed in most cases – but possible!
Asynchronous and Timestamped
updated value
Timing synchronisation options:
  MRF EVR (Detectors, Choppers)
  PTP (Beckhoff: Motion, Sample Environment)
  NTP (Slow Sample Env, e.g. temperature)

## Slide 20: How We Write Files
Live Data
Creating NeXus Templates “With Ease” – Sprint Planned for November
Detector Voxel Geometry
File Template
NeXus File
Instrument Layout
Neutron Events
File Writer
Motion and Chopper Information
Other Metadata (Proposal, Sample)
Sample Environment Metadata
  File contains all pertinent measurable facts about the experiment
  Contents can be interpreted and reduced (processed) without external information
Up to date Template sent to File Writer for each File
Live data streamed into file for entire duration of “exposure”

## Slide 21: Embedded Geometry
NeXus borrowed from CIF

## Slide 22: ESS NeXus Raw Data
All instruments follow the same generic NeXus principles:
  No application definitions are being followed
  Application of base classes wherever possible. Extending them, where needed.
  Extensive use of NXlog for any parameter that could change during the experiment (as well as for the ones that definitely will)
  Event-based recording of neutron detection & time-stamp based correlation of images (with source pulse as reference)
Encoding of the full geometry information in NeXus (locations and orientation). No need for Mantid IDF files, or any other external resources to understand the data. Running a Monte-Carlo Simulation should be possible from the NeXus file.
Mini-Summary
NeXus
Geometry Mapping to scipp
LoKI @ LAMOR

## Slide 23: Development, Integration, Testing and Verification
167 m2
Ymir Integration Platform (Instrument) – moved to B02
  Main driver of progress across groups, through integration tests and demos
  Routinely used for engagement with instrument teams for feedback and evaluation
  Opportunity to run strawman experiments, like light tomography
  Site installation relies on production network and compute infrastructure and enables all groups to gain valuable experience
  Supported by 800 kEUR co-funding grant from Swedish Tillväxtverket

## Slide 24
Questions?