## Slide 1: RF and Cavity Integration with Beam
Rihua Zeng
2022-09-16

## Slide 2: Outline
Outline
Part 1:
Summary of Cavity & RF/LLRF Performance (from cavity perspective)
    From known to unknowns
Part 2:
What need to solve before next beam commissioning
    Specific techniques
    What’s more….
Some ideas
    …….
Open Discussions

## Slide 3
Known Issue I:
Detuning and Dynamic Detuning

## Slide 4: RFQ frequency shift due to Transient heat loading
The Problem
The RF power does not heat up directly the whole RFQ body, it affects first only 3.5 μm thick skin.
The transient temperature rise could be ~60 K (don’t consider heat transfer to other part of body and cooling)
worst case is recovery from a RF trip, frequency jump up to around 50kHz(consistent with simulation). Water temperature loop is too slow to catch it (delay time around 30 seconds)
Simulation by Michel (step response, RF offRF on) indicates the maximum(abs) detuning of -37.5kHz at t=25s. It takes about 4s to reach -17kHz giving 10% of refected power.
Measurement data by Daniel

## Slide 5: RFQ frequency shift due to dynamic heat loading
The Solution
For RF trip, auto-reset (<1second) is essential to avoid big detuning jump.
For RF power ramping, frequency tracking with decay method works pretty well
Tracked even 300kHz detuning! (~8 cavity bandwidth for Bunchers)
S. Simrock, DESY

## Slide 6: Detuning measurement by delta phase (forward – cavity)
Both decay method and delta phase method are implemented for RFQ
It works for static detuning.
Not for dynamic detuning. It should include dynamic factor
Doesn’t work when close to 90 deg.

## Slide 7: Cavity Equation based Dynamic Detuning
LFD Measurement in TS2
Detuning from cavity decay is just a special case of this method
LFD(Lorentz Force Detuning)
https://newsline.linearcollider.org/wp-content/uploads/2011/07/Lorentz-force-detuning.jpg

## Slide 8
Known Issue II
Phase Perturbation by Klystron-Modulator Ripples

## Slide 9: Klystron-Modulator Ripples
The Problem
Perturbations in the cathode voltage results in the change of the beam velocities, and then led to the variations of the RF output phase
1% error in cathode voltage leads to more than 10 deg. variation in RF output phase
High frequency ripple with larger amplitude is hard to compensate by feedback, especially in normal conducting cavities
SNS
JPARC
Further reading: R. Zeng et, al. The Droop and Ripple’s Influence on Klystron Output, ESS tech-note.
https://docdb01.esss.lu.se/DocDB/0001/000173/001/InfluenceOfTheRippleOnKlystronOutput.pdf

## Slide 10: Klystron-Modulator Ripples
The Problem
Plot by Anders S.

## Slide 11: Klystron-Modulator Ripples
The Solution

## Slide 12
Known Issue III
Beam Loading

## Slide 13: Beam Loading in RFQ

## Slide 14: Beam Loading at DTL1
Measurement and Simulation

## Slide 15
Unknowns Blackbox I
Breakdown

## Slide 16: Breakdowns at RFQ/DTL1 Conditioning,
RFQ:
~50, 000 reflect interlocks
(mostly caused by breakdown)
~5,000 vacuum interlocks
DTL1:
~30, 000 breakdowns
( by cavity decay interlock)
2 vacuum interlocks

## Slide 17
RFQ:
Intensive breakdowns were frequently observed at peak of conditioning
DTL1:
Breakdown are mostly gentle ones

## Slide 18: Breakdown in RFQ and DTL1
Forward Power

## Slide 19: Breakdown
Locate where breakdown happens

## Slide 20: Beam Loading in Bunchers
At 90 deg bunching

## Slide 21
Unknow blackbox II
Multipacting

## Slide 22: Multipacting after Long Break(no RF in Cavity)
Multipacting is hidden behind and invisible by e-current pickup
    Electron current is hide behind(not visible from electron current pick up measurement)
    But electron current interlock triggered immediately whenever increase pulse length to some level
    It seems it need adequate pulse length for electron to get resonant with RF
    Need to trigger it!

## Slide 23: Multipacting patterns Depends on RF Power Level
After Multipacting gets triggered, it appears all over RF pulse
110kW, 14Hz, 3200us
80kW, 14Hz, 3200us

## Slide 24: Multipacting Pattern after long time RF Running
spark e-current appears at beginning and/or end of RF pulse

## Slide 25: Use Special Long Pulse to trigger Multipacting
Micro-RF pulse Trigger
using micro-pulses to trigger Multipacting and identify the Multipacting regions in low power level: (The macro-RF pulse length is under control by timing setting )
After trigger, Multipacting appears all over RF pulse, and normal conditioning technique can be applied

## Slide 26: Multipacting grow rates
Multipacting occurs at beginning or/and end of pulses

## Slide 27: Multipacting in Cavity(not only couplers)
Sometimes detected by BCMs in beginning of RFQ (in LEBT)and end of RFQ

## Slide 28: Multipacting in Very Low Power
Similar pattern between RFQ(20kW) and Bunchers(0.2kW)

## Slide 29: Uncertainties: Power and Field Calibration
X-ray measurement
By Emanuele L.
https://accelconf.web.cern.ch/ipac2022/papers/tupotk030.pdf

## Slide 30: Uncertainties: Power and Field Calibration
Net Power in Cavity
Reconditioning, x-ray detector at end of RFQ(at 4.25m from RFQ beginning)
Conditioning, x-ray detector at 3.03m from
RFQ beginning
by Emmanouil T.

## Slide 31: Uncertainties: Phase and Beam Phase
Beam Transmissioning Affected by Beam Loading

## Slide 32
Uncertainties: Phase and Beam Phase
Beam Effective Phase Affected by Beam Loading

## Slide 33
Beam Phase measured by BPM

## Slide 34
Part II

## Slide 35
High Power Integrated Test
After Conditioning, before beam commissioning:
  Close loop operation at least 8 hours
  Simulated beam to verify feedback performance
  Recover from trip
  Full duty cycle running
  Cavity operation parameters
    List of parameters and range
    List of interlock thresold range

## Slide 36
Beam time for RF&Cavity
Buncher cavities test with beam
RFQ test with beam(fast bpm, beam phase, etc)
Close loop optimization with beam
Cross check the Amplitude and phase
Beam phase by RF method
Cavity parameter tuning(Optimum detuning, injection time, etc)

## Slide 37: Dynamic Detuning, Beam Phase& Beam Velocity Calibration by Cavity Equations
From Cavity LCR circuits model, the following equations can be derived:
the blue ones are cavity voltages(magnitude and phase) measured in real time, and the black ones are constant parameters.
The read ones are variables to be determined. Dynamic detuning△𝜔(t) is the only unknown variable in the case of no beam operation. It is accurately predicted by the equations, as shown in later slides.
With Beam, will be a new variable to be determined, which include beam velocity information.
Further reading: Transient Beam Loading Based Calibration for Cavity Phase and Amplitude Setting, R.Zeng, O. Troeng. HB2016.
https://accelconf.web.cern.ch/hb2016/papers/mopl025.pdf
Beam phase:

## Slide 38
Open Discussion