## Slide 1: Iterative learning control algorithm and Transient Beam based cavity phase detection
Chengye Xu
Institute of Modern Physics (IMP),Chinese Academy of Sciences

## Slide 2: Research Background（CAFe）
4 Cryomodules，23 Superconducting Cavities，Half-bandwidth：80 Hz~200 Hz,HWR010+HWR015）
CAFe：China ADS Front-end （162.5 MHz，CW mode）
  To validate the availability of 10 mA high power CW proton beam for CiADS
  2021.3：17.3 MeV, 7.2 mA, 127kW, 108 hrs; 17.3 MeV, 10 mA, 174 kW, 12 hrs
Beta=0.1
Beta=0.15
162.5 MHz Taper HWR
CiADS

## Slide 3: Research Background
Repetitive rate: 100 Hz
CW Mode
Inc. Duty cycle
Transient beam-loading
Beam
5 deg
Beam-induced transient (∆A/A≈2.4%)
Beam = 10 mA
∆A/A>2%
Required stability at LINAC: for Amplitude: ±0.1%. for Phase: ±0.1%.
Start the beam-commissioning with a short pulse duration and repetition rate. Next, the pulse duration and repletion rate of the beam will be increased.
The beam loading makes a significant drop of accelerating gradient.

## Slide 4: Basic Principle of ILC
DESY and SNS implemented the method, the difference between them is the learning function .
A large of and data need to deal with, the data can be hardly processed in FPGA in real-time.
Difficult to meet the 100Hz repetition frequency requirement.
Upload to upper computer
ILC update law:
Schematic diagram of ILC scheme

## Slide 5
Modified ILC feedforward algorithm
“Quasi-square wave” beam
Beam waveform in CAFe
Traditional ILC:
Proposed ILC:
Iterative process of the proposed ILC algorithm
In this proposed ILC algorithm the FF output is considered as a constant value rather than a list of data.
Chengye Xu et al. Application of a modified iterative learning control algorithm for superconducting radio-frequency cavities. Nuclear Instruments and Methods in Physics Research Section A. 2022, Volume 1026, 166237

## Slide 6
Epeak
FF table
Feedforward compensation results
Amplitude and phase of cavity gradient and FF output during iterations
Parameters | Value
Beam current | 3.0mA
Beam phase | -40°
Duration of the beam pulse | 518μs
 | 0.038m
Parameters | Value
Beam current | 3.0mA
Beam phase | -40°
Duration of the beam pulse | 518μs
 | 0.038m

## Slide 7
Feedforward compensation results
Effect of ILC Gain on the system performance
Larger gain helps ILC complete the iterative convergence process in less time which is consistent with the simulation results.
parameters | Value
 | Value

## Slide 8
Feedforward compensation results
A s deviation exists between beam and FF
Cavity gradient in initial state and steady state
There is a slight overshoot in either amplitude or phase of the cavity gradient even in the steady-state was achieved.
FF output signal 3μs earlier than the accurate arrival time of the beam

## Slide 9
Problem to be Resolved
Target：Develop an online Beam phase calibration method
BPM based Phase scan：Consume too much time
Environmental factors: Temperature and Humidity
RF Phase
Temp

## Slide 10
Transient beam based method
|
V
c
,
start
|
|
V
c
,
end
|
θ
start
θ
end
θ
start
θ
end
φ
b
|
V
c
|
V
c
Im
(
V
c
)
Re
(
V
c
)
Time
Time
Beam induced
transient
|
V
c
,
start
|
e
j
θ
start
|
V
c
,
end
|
e
j
θ
end
Beam
transient
I
b
Open loop operation
Beam induced transient in each cavity field can be measured by comparing the cavity field waveforms without/with beam

## Slide 11
Experiment conducted in ESS
Zoom
Zoom
Vc Vector
Beam Vectors
RF waveforms were recorded during phase scan in June 8(using BPMs, around 58mA and 5us in MEBT).
The test using RF waveforms(forward power, reflect power and pick up) to calculate beam phase.

## Slide 12
Experiment conducted in ESS
RF based method: (measured directly in feedback loop, no BPM): 29.3 deg (cavity field phase).
BPM Phase Scan Results: 2.04 in setpoint for 90 deg operation, 0.52 (29.8 deg) in cavity phase(pickup read in 2022-06-08).

## Slide 13: Future Work
Estimate the beam parameters by calibrated Feedforward signal Vf
Critical Problems：
1）During the beam commissioning the beam loading should be perfectly compensated
2）High Precision of feedforward signal

## Slide 14
The core idea of the modified ILC is to simplify the output as a constant value rather than a list of data, which can be easily implemented in FPGA.
An open loop beam loading based calibration for cavity phase method has been verified in ESS.
Summary

## Slide 15: Thanks for your attention