## Slide 1
Warm Linac interface meeting – Drift Tube Linac
Francesco Grespan – Paolo Mereu

## Slide 2: DTL layout

## Slide 3: Buildings and Site Infrastructure interfaces
DTL workshop requirements
Transport and installation in the tunnel TO BE DEFINED

## Slide 4: Survey & Alignment interfaces
Alignment of
Drift Tubes inside module (workshop)
Module to Module (workshop)
Tank to Tank (tunnel)
Needs
Module support or table and stable laser network in the workshop
Laser network and Alignment support (isostatic fine regulation to couple the modules)
Laser network in the tuner

## Slide 5: Survey & Alignment interfaces

## Slide 6: Conventional Power, Cables, Racks interfaces
Rack for Steerer power supply: 3Hor + 3Vert per tank
Rack for Movable tuners motor controller
Power for water skid: 5 pumps + 1 redundancy

## Slide 7: WP2 - Beam Physics interfaces

## Slide 8: WP2 - Beam Physics interfaces
In-air BERGOZ ACCT 55x91x22

## Slide 9: WP2 - Beam Physics interfaces
In-vacuum BERGOZ ACCT 55x91x22

## Slide 10: Proton Beam Instrumentation interfaces
Element/Tank | T1 | T1 | T1 | T2 | T2 | T2 | T3 | T3 | T3 | T4 | T4 | T4 | T5 | T5 | T5
Steerer X [DT] | 3 | 21 | 41 | 1 | 11 | 23 | 2 | 12 | 22 | 2 | 10 | 18 | 1 | 7 | 15
Steerer Y [DT] | 5 | 23 | 43 | 3 | 13 | 25 | 5 | 14 | 24 | 4 | 12 | 20 | 3 | 9 | 17
BPM [DT] | 17 | 37 | 59 | 9 | 21 | 33 | 10 | 20 | 28 | 8 | 16 | 24 | 5 | 13 | 21

## Slide 11: Radio Frequency (RFDS) interfaces
RF windows at ¼ L and ¾ L of each tank (Mega Industries design)

## Slide 12: Radio Frequency (LLRF) interfaces
9 RF Pick-ups per tank (N-connector)
3 movable tuners per tank (up to the motor controller)

## Slide 13: Vacuum interfaces
3 Vacuum manifolds

## Slide 14: Water Cooling interfaces
Cooling system data
Power dissipation: 70kW = 950kW × 1.25(margin) × 4ms × 14Hz
Cavity water temperature (inlet: 30°C, dT: 0.5°C)
Water distribution
Water Flow (≈100 mc/h)
1 water skids provided by LNL, with 5 three-way valves, 5 pumps.
2 pipes per tank (DN150)
DTL distribution
Modules: 2 series of 2 modules each
Tuners: 2 groups
Post couplers: 2 groups
DTs: all in parallel (?)
Steerer: all in parallel
End walls: 2
RF couplers: 2
Redundancy pump (Valves not represented)