## Slide 1: ESS LLRF System
2015-04-23
Anders J Johansson

## Slide 2: LLRF at ESS
LLRF: Low-Level Radio Frequency
Controls the phase and amplitude of the field in the cavities to within x degree / y %.
Starts at cavity field pickup connector on cavity/cryomodule.
Ends at input to the pre-amplifier.
Commands the slow tuners.

## Slide 3: LLRF system
LLRF system
:
PI
-
controller
Master Oscillator
Phase Reference Clk
352
.
21
MHz
Amplifier
(Klystron, Tetrode)
Pre
-
Amp
Load
Cavity
Circulator
PSU
(Modulator)
Power Grid
4
5
1
3
6
7
9
10
2
8
I
Pz Ctrl
Motor Ctrl
Slow Tuner
M
LLRF system
:
Motion control
LLRF system
:
Monitoring
&
Storing
1
…
10
Warning
/
Errors
U

## Slide 4: Design concept
Digital implementation of fast control in FPGA
Modular design for simple maintenace
Modular design for large volume procurement
Redundant design for availability
Downconversion at 352 MHz

## Slide 5: Control Architecture
1. Procedures
  such as tuning of a cavity, commissioning of a coupler
  Runs on any computer connected to EPICS
2. Algorithms
  such as updating the Feed-forward tables based on the measured error.
  Runs on CPU in crate
3. Functions
  such as PI-control and addition of FF-table.
  Runs in firmware on FPGA

## Slide 6: Warm Linac Rack layout illustration

## Slide 8
FPGA/ADC
RF/(VM)
FPGA/ADC
RF/VM
CPU
Timing
Timing (MRF)
MCH
EPICS, Supervision
Modulator V
Beam current
Vectormodulator out
X
Y
Z
Phase referense
Cavity Pickup
VM out
PreAmp Out
PowerAmp out
PowerAmp Refl
Cavity In
Cavity Refl
Fan Tray x 2
PSU x 2
Interlock (to LPS)
352.21 MHz MTCA.4 Warm Linac
CB control on backplane
Timing triggers
MCH supervision
External I/O
Ethernet on backplane
230 V AC
Phase referense
Cavity Pickup
VM out
PreAmp Out
PowerAmp out
PowerAmp Refl
Cavity In
Cavity Refl
LO-generation
LO/REF

## Slide 9: LLRF RF inputs Single coupler
Cavity pickup (Cavity)
LLRF out (LLRF Internal)
Pre-amp out (RFS)
Main Amplifier out (RFS)
Main Amplifier reflected (RFS)
Cavity forward (RFS)
Cavity reflected (RFS)
Phase reference in (Phase reference)

## Slide 10: LLRF RF inputs Two couplers
Cavity pickup (Cavity)
LLRF out (LLRF Internal)
Pre-amp out (RFS)
Main Amplifier out (RFS)
Main Amplifier reflected (RFS)
Splitter forward (RFS)
Splitter reflected (RFS)
Phase reference in (Phase reference)
Cavity forward 1 (RFS)
Cavity reflected 1 (RFS)
Cavity forward 2 (RFS)
Cavity reflected 2 (RFS)
Spare
Spare
Spare
Spare

## Slide 11: LLRF inputs Other
EPICS (ICS)
Ethernet for crate supervision (ICS)
Timing (ICS)
Beam current measurement (BI)
Modulator voltage (RFS)
Interlock (LPS in RFS)
230 V mains (?)

## Slide 12: LLRF output
LLRF output (RFS)
EPICS (ICS)
Tuning command (tune x Hz up/down) over EPICS.

## Slide 13: Motion Control Baseline interface
Cavity WPs are responsible for protecting the cavities against harmful commands
LLRF calculates necessary tuning adjustments
Adjustments are sent over EPICS to be executed.

## Slide 14
RFQ
Motion Controller / PID temperature ctrl
Cavity
TCP/IP
Control Box
ICS
EPICS
Water skid
RFS / LLRF

## Slide 15
DTL
M
M
M
Motion Controller
Connectors in tunnel
Cavity
TCP/IP
Control Box
ICS
EPICS
Limit switches / encoders
RFS / LLRF

## Slide 16
LLRF
Cavity WP
ICS

## Slide 17: Motion control LLRF comments
As the time constants are slow on the temperature tuning of RFQ and DTL, LLRF is helped by having detailed knowledge of the tuning process.
The LLRF architecture support extension to more RF-inputs if needed for tuning. (Multiple sensors in RFQ/DTL?)
Stepper motor controller standardisation handled by E2H2C.

## Slide 18: Components and Layout

## Slide 19: Baseline Layout
Crate for 1 buncher cavity
PSU
PSU
MCH
CPU
Timing
LLRF
ADC
FPGA
+RTM
1 2 3 4 5 6 7 8 9 10 11 12

## Slide 20: Baseline Layout
Crate for 1 352 MHz DTL cavity
PSU
PSU
MCH
CPU
Timing
LLRF
ADC
FPGA
+RTM
1 2 3 4 5 6 7 8 9 10 11 12
LLRF
ADC
FPGA
+RTM

## Slide 21: AMC for LLRF: Struck ADC
AMC: 10 Channel ADC + FPGA
AMC: Generic test interface