## Slide 2: ECDC for Spectroscopy
Spectroscopy STAP
PRESENTED BY Tobias richter

## Slide 3: Main Activities and Scope Overview
  instrument and technique specific controls interfaces
  devices controls integration - sample environment, detectors, motion control, choppers
  standardised and long-time maintainable software integration
  interface to detector backend, detector specific software event formation
  timing and timing verification
  downstream data integration to DRAM via NeXus files and live processing
Instrument Control System – Interface to ICS Deliver controls scope (for example timing system, network infrastructure, EPICS Infrastructure, IOCs, etc) to NSS Own the related requirements, milestones and priorities for activities in ICS/WP12 and NSS. Implement, evaluate, test and commission controls solutions.
Event Formation Perform near real-time processing of digitised detector signals and produce neutron event information.
Data Acquisition, Streaming and File Writing Reliably and accurately keep the scientific record of the experiments and measurements by monitoring all relevant parameters.
Engineering Interfaces Provide operator interfaces for low level commissioning and maintenance of neutron instrument equipment.
Scientific User Interface for Experiments Provide a workable solution for visiting scientists and ESS staff to efficiently control and monitor their experiments and measurements.
Data Curation (Catalogue) Index files produced from experimental runs and with their relevant metadata. Keep track of downstream processing activities.
Experiment Control and Data Curation
Experiment control
Stream events & meta data
Data reduction & visualization
Data analysis
Data management

## Slide 4: Scope Clarifications
Relationship to ICS/WP12:
ECDC prioritise their tasks and collaborate on a technical level. We feel responsible for the success of their work.
Exclusions
  Mechanical or electrical drawings, LBS, FBS
  Power consumption, instrument hardware space claims
  Network design or implementation
  Computing infrastructure, beamline workstations
  Timestamping at source (with agreed exceptions - ODIN)
Inclusions
  NeXus file writing
  Event formation – Interpretation of Detector Readout
  Detector slow control
  (Core) NICOS support
Subject to discussion

## Slide 5: ECDC Interfaces
Experimental Control and Data Curation
(ECDC)
Motion Control and Automation Group
TBL
DREAM
ODIN
LOKI
Control System Infrastructure
(ex ICS WP07)
Core technology Hardware (ICS WP04)
BIFROST
CSPEC
ESTIA
MAGIC
BEER
NMX
HEIMDAL
SKADI
FREIA
TREX
MIRACLES
VESPA
Software
(ICS WP03)
Neutron Chopper Group
Detector Group
Sample Environment
Sample Environment II
Data Systems and Technologies
Data Reduction, Analysis and Modelling
Neutron Instrument and Technologies Integration Support (ICS WP12)

## Slide 6: Current Staff and Profile
 | Afonso | Morten | Jenny | Jonas | Matt | Daniel | Tibor | George | Torsten | Anders | Stefanos
Event Formation |  | ● | ● |  |  |  |  | ○ |  |  | 
Timing |  | ○ |  | ● |  |  |  |  | ● | ● | 
Streaming | ○ |  | ○ |  | ● | ● |  | ○ |  |  | ○
NICOS |  |  |  | ● | ● | ○ | ○ | ○ |  | ○ | ○
Device Integration |  |  |  | ● | ● |  | ○ | ○ | ● | ● | 
Testing | ● | ○ |  | ○ |  | ● | ○ | ○ |  |  | ●
Deployment | ● | ○ |  |  |  | ● |  |  |  |  | 
Instrument Contact |  |  |  |  | ● | ○ |  |  |  |  | ●
11 Staff (+ Group Leader)
    6 in post at DMSC (green)
    2 due to start May & August (blue)
    3 in Lund (orange) associated with Motion, SE and Ymir
    budget exists for 1.5 more FTE until 2027
NSS + TD staff
    ICS NITIS (EPICS for NSS) at 5 staff
    close collaboration with Markus from NCG
    lost DetG slow controls contact in August 2022
Who is who in ECDC (NSS)
Experiment control (NICOS)
Data streaming and file writing
ECDC
Event formation
Testing, deployment and Infrastructure
Device integration

## Slide 7: Development, Integration, Testing and Verification
167 m2
Ymir Integration Platform (Instrument) in B02
  Main driver of progress across groups, through integration tests and demos
  Routinely used for engagement with instrument teams for feedback and evaluation
  Opportunity to run strawman experiments generating real data, like light tomography
  Exercises production networks, compute infrastructure and their interfaces, like user office proposal system

## Slide 8: ECDC Schedule – Milestones
Approach
  Ticking off important functionality as defined milestones on a set timeline gives us confidence in our planning abilities
  No benefit to have DAQ or experiment control on critical path
  New milestones until the end of 2024 under development
Issues
  Most ECDC deliverables depend heavily on external contributions (hardware, services, documentation, other engagement)
  Inability to follow an agreed timeline only gets attention when ECDC would delay something that “ESS cares about”
  Planning tools that provide benefits only once all work and resources are accounted for, will only be useful very late in the project (few subprojects currently have linkable activities for ECDC – instruments do not)
Notes: Comparing starts and finishes with plan is odd
Average delay of planned activities?

## Slide 9: Selected ECDC Milestones
  NICOS (experiment control) baseline for
    LoKI ✅
    DREAM ✅
    ODIN 🔸
    BIFROST 🔸
  NeXus File (Geometry) Templates ✅
  (Light) tomography
    Raw data ✅
    Manual reconstruction ✅
    Automated processing 🔸
  Hamamatsu Orca timing verification🔸
  Slow control for CAEN 5560 🔸
  Proposal system ready to schedule at Ymir ✅
  DMSC data storage ready with permissions 🔸
  Motion control available for demonstration for all standard classes🔸
  Staging computing equipment available to testign and integration 🔸
Upcoming:
  Detector timelines
  Better linking of milestones overall with instruments and within NSS/ESS
  Instrument commissioning planning
Past & Upcoming

## Slide 10: Main focus areas
2023
  Finalise most work on critical common infrastructure with verifications
    File writing
    Data streaming
    Overall experiment control
    Verification activities (downstream, timing)
  Complete scope for tranche 1 instruments
    NeXus templates
    NICOS interfaces
    Device integration & verification
  Detector and Camera integration
    event formation
    Slow control and calibration
  More detailed planning, if possible
2024
  Instrument tranche 1 rollout and cold commissioning
  Scope for tranche 2
  Detector and camera integration
  Sample environment
ECDC in the next couple of years

## Slide 11: Timing System
IPC2
IPC1
PTP EVR IOC
One Oscillator
EVG
EVR IOC
PCIe EVR2
Neutron Chopper
TTL Input
TDC
Setpoint
Sequencer
TTL Output
EVM Fanout (Repeater Hub)
PCIe EVR1
Motion controller
Optical fiber 14Hz & 88.0525 MHz
Master oscillator
1 Hz PPS System new second
PTP GrandMaster
Optical fiber 14Hz & 88.0525 MHz
88.0525 MHz
UTC time
EPICS forwarder
Medium accuracy PTP time stamped motion data
High accuracy EVR time stamped chopper data
Kafka cluster+NeXus+DMSC
GPS
IPC3
NTP IOC
NTP server
Low accuracy NTP time stamped meta data
Accuracy
NTP~10ms
PTP~10us
EVR~10ns

## Slide 12: Event mode data acquisition
Neutron events and motior positions on separate time axes
time
location
time
event

## Slide 13: Timing Verification for Motion Control
Paper in preparation for ICALEPCS 2023

## Slide 14: NeXus
Getting good engagement and feedback from scipp team (DMSC).
Issues and tasks on the roadmap:
  Complex geometries are large in size (DREAM)
  NeXus standard often ambiguous or incomplete
  Some missing definitions: scintillator screens, optics, guides, rheometer
  Alarms and connection status
  Some bugs in file writer and pipeline
Complete record of the experiments

## Slide 15: CAEN R5560 – BIFROST
  Hardware common for all tube/straw technologies
  ECDC leading effort to harmonise CAEN firmwares between instruments that need them to maximise commonalities without compromising tested functionality
    Development & deployment
    Data format
    Slow control
  Different FPGA firmware need per instrument
  Baseline NeXus detector geometries under discussion (BIFROST picture)
PSD tubes with CAEN R5560 – also LoKI as well as C-SPEC and MIRACLES (?)

## Slide 16: Detector Event Processing
Analog
Digital
Logical
Physical
(tof, r, j, q)
(tof, pixel)
(t, FEN, RING, ch, adc)
(V(t), A(t), Ohm)
EFU
Readout
Backend
Readout
Frontend
scipp
Deals with instrument configuration identifiers such as rings and front –end nodes + other digital and digitized values: grids, wires, strips, tubes, amplitudes or ADC values.
This step abstract all information on the left away and provides a 2D (3D) detector surface which can be used for commissio-ning, monitoring and calibration.
Conversion electronics ultimately measures charge, current or voltages.
Here, pixels are 'connected' with the physical instrument geometry: lengths, angles and detection volumes.
Series of Agreed Mappings

## Slide 17: Detector Readout Chain
Detector Group
ECDC
Instrument
Converter
Ring
Readout Master
Frontend
Assister
Event Formation Unit
For the data flow the ring & readout master are transparent.
The readout master provides timing and slow control to assister & frontends. Not shown.
The readout master is also agnostic to the slow control (thresholds, gains, offsets, operations modes, etc)
That means the following things need to be verified:
  Ring operation
  Timing synchronisation
  Data format & interpretation
  Frontend slow control
  + auxillary slow control (HV, gas, etc)
Used by most instruments – data path, simplified

## Slide 18: ODIN – Hamamatsu Orca
  Hardware at ESS
  Camera is working within EPICS area detetctor framework.
  Allows basic data acquisition and control of parameters (some items still TBD).
  Timing integration happens via connection to MRF event receiver. Verfication is ongoing to confirm
    Synchonisation to “ESS time”
    No drift or undue jitter
    Not dropping frames
Camera – non-event mode for imaging

## Slide 19: ODIN – Timepix3
Commercial event-mode detector
  Hardware at ESS & Basic functionality reproduced
  There are multiple operations modes and integration options that can meet the instrument team’s requirements
    Vendor software vs ESS control
    Standalone operations with MRF EVR vs ESS detector readout master integration
    Under evaluation
  LoskoVision-style acquisition/reduction similar to “standard” ESS live detector event formation mode

## Slide 20: Interface Specifications + Timelines
For the early instruments getting everything ready relatively soon should be a priority.
We need to establish a joint timeline for
  finalising designs
  setting up tests
  preparing slow control
  implementation & verification
  production
  delivery with FAT/SAT
  cold and hot commissioning
  calibration
Discovering tasks or issues late is not fun!
Interface definition status for a random selection of Instruments. See:
https://confluence.esss.lu.se/display/ECDC/Instrument+Status+Overview
Other information of interest:
  detector geometry
  Rates (global, local, peak, average)
  operation modes
  commissioning plans
  calibration procedures
  etc

## Slide 21: Detector Integration Overview
  BIFROST
    Good progress. Status as expected with respect to instrument schedule.
  C-SPEC & MIRACLES
    Expecting a solution similar to BIFROST, joining CAEN common effort
  T-REX
    Probably VMM based, no details known
  VESPA
    Nothing known yet
  Beam Monitors
    CDT electronics somewhat known
Event formation (coincidence building, location refinement, etc) in software requires intricate knowledge of frontends and data.
Main detector functionality and event formation are on a good way, where there is test data and agreements:
https://confluence.esss.lu.se/display/ECDC/Instrument+Status+Overview
Slow control (frontends and services) and calibration could do with a little bit more attention.
Focus on First Instruments (all with commercial detectors)

## Slide 22
Questions?