## Slide 1: Towards the development of a very cold neutron source
LENS-ELENA NEUTRON MODERATOR WORKSHOP | 17.04.2024 I Dalini D. maharaj
For the high brilliance neutron source (HBS)

## Slide 2: a very cold neutron source for the HBS
Outline
Overview of the High Brilliance Source
Motivation
Introduction to Moderator Materials
Concept Development
Initial Results
Future Work

## Slide 3: What is the HBS?
High Brilliance Neutron Source – A HiCANS facility
Linac Parameters
100mA, 70 MeV proton source
Multiplexer
Proton beam distributed among 3 target stations
Target Stations
Each target station operated at distinct frequency
Optimize thermal spectrum for each target-moderator combination
6-8 instruments per target station
Dedicated beam port for each instrument
  Can have its own cold source as needed

## Slide 4: What is the HBS?
High Brilliance Neutron Source – A HiCANS facility
Linac Parameters
100mA, 70 MeV proton source
Multiplexer
Proton beam distributed among 3 target stations
Target Stations
Each target station operated at distinct frequency
Optimize thermal spectrum for each target-moderator combination
6-8 instruments per target station
Dedicated beam port for each instrument
  Can have its own cold source as needed
High degree of flexibility makes the HBS adaptable
J. Baggemann, “Development of Neutron Extraction Plugs for HBS”, DENIM XII Jülich, 21st September 2023

## Slide 5: motivation
Access to longer length and time scales – large biological structures on the nanoscale
Significant improvement of gains in intensity and resolution for some neutron instruments
Can apply light optics methods to control neutron beams as refracting power ≈ λ2
1J.M Carpenter and B.J. Micklich, ANL (05/42) (2005).
Very Cold Neutrons for Materials Investigations
10 Å
0.81 meV
40 Å
0.05 meV
100 Å
0.008 meV
Range of very cold neutrons
10 - 100 Å

## Slide 6: motivation
Access to longer length and time scales – large biological structures on the nanoscale
Significant improvement of gains in intensity and resolution for some neutron instruments
Can apply light optics methods to control neutron beams as refracting power ≈ λ2
Previously difficult to extract VCN beams from conventional cold sources
Lower temperature cross sections not previously available
1J.M Carpenter and B.J. Micklich, ANL (05/42) (2005).
Very Cold Neutrons for Materials Investigations
10 Å
0.81 meV
40 Å
0.05 meV
100 Å
0.008 meV
Range of very cold neutrons
10 - 100 Å

## Slide 7: Why ONLY now?
2V. Santoro et al, HighNESS Conceptual Design Report arXiv:2309.17333v3 [physics.ins-det]
Neutron scattering kernels developed through the HighNESS project for many candidate moderator and reflector materials
Opportunity to explore VCN development for HBS – we are adaptable, after all

## Slide 8: producing very cold neutrons
Accessible low energy modes, ideally not restricted by a dispersion relation
Solid D2
Methane (in phase II)
Clathrates – THF-hydrates, methane hydrate
Cross section due to lattice drops precipitously at temperature scales well below Debye temperature
Neutrons can also excite vibrational modes in solid state materials

## Slide 9: Candidate very cold moderators
Solid D2
Methane (in phase II)
Clathrates – THF-hydrates, methane hydrate
Moderation by: rotational and translational modes (phonons)
Pros
Very low neutron absorption cross section and small nuclear mass
Operated at 5 K
Small upscattering cross section
Cons
Suffer broadening of pulse by a factor of five
Requires larger moderator volumes

## Slide 10: Candidate very cold moderators
Solid D2
Methane (in phase II)
Clathrates – THF-hydrates, methane hydrate
Y. Shin et al, Nuc. Ins. Meth Phys Res A 620 pp. 382–390 (2010).
Transition to phase II below 20.4 K
  Partially orientationally ordered state

## Slide 11: Candidate very cold moderators
Solid D2
Methane (in phase II)
Clathrates – THF-hydrates, methane hydrate
Transition to phase II below 20.4 K
  Partially orientationally ordered state
S. Grieger et al, J. Chem. Phys. 109 3161–3175 (1998).
Disordered sites - Oh
Weak CEF
No molecular field
Almost free quantum rotor!
Ordered sites - D2d
-Librational modes
-Rotational tunneling

## Slide 12: Candidate very cold moderators
Solid D2
Methane (in phase II)
Clathrates – THF-hydrates, methane hydrate
Transition to phase II below 20.4 K
  Partially orientationally ordered state
Y. Shin et al, Nuc. Ins. Meth Phys Res A 620 pp. 382–390 (2010).
¾ Disordered sites - Oh
Weak CEF
No molecular field
Almost free quantum rotor!
Free rotor contributes the most significantly to the scattering cross section
¼ Ordered sites - D2d
-Librate in minima of orientational potential
-Rotational tunneling

## Slide 13: Candidate very cold moderators
Inclusion compounds containing nanovoids
Very large unit cell; a ~ 17 Å
Cages can host guest molecules
  THF (TDF) - C4H8O (C4D8O)
  Oxygen - O2 (triplet GS with zero-field splitting of 0.4 meV)
  Methane - CH4 (discussed previously)
A. Falenty et al, Nature 516 pp. 231-233 (2014).
Solid D2
Methane
Clathrates – THF/TDF-hydrates, methane hydrate

## Slide 14: Candidate very cold moderators
Inclusion compounds containing nanovoids
Very large unit cell; a ~ 17 Å
Cages can host guest molecules
  THF (TDF) - C4H8O (C4D8O)
  Oxygen - O2 (triplet GS – E* = 0.4 meV)
  Methane - CH4 (discussed previously)
HighNESS - Cross sections developed for THF (TDF)-clathrates
A. Falenty et al, Nature 516 pp. 231-233 (2014).
V. Czamler et al, EPJ Web of Conferences 286 05004 (2023).
Solid D2
Methane
Clathrates – THF/TDF-hydrates, methane hydrate

## Slide 15: Candidate very cold moderators
Cages can host guest molecules
  THF (TDF) - C4H8O (C4D8O)
  Oxygen - O2 (triplet GS – E* = 0.4 meV)
  Methane - CH4 (discussed previously)
HighNESS - Cross sections developed for THF-clathrates
Methane clathrate advantage over solid methane?
V. Czamler et al, EPJ Web of Conferences 286 05004 (2023).
Y.C. Shin et al, Eur. Phys.J. Plus 136 882 (2021).
Solid D2
Methane
Clathrates – THF-hydrates, methane hydrate
17 April 2024

## Slide 16: CONCEPT DEVELOPMENT
Scope of Study
Goal - Optimize VCN moderator-reflector design for various instruments
  SANS
  TOF-INS
  NSE
Must demonstrate competitive advantage over cold parahydrogen source at low energies
Requirements and considerations
Compact design for Hi-CANS
Technically feasible
Optics – how can we use this to our advantage

## Slide 17: Concept development
I. Computational demands of simulations
II. Heat removal from moderator – important to maintain moderator at sufficiently low temperatures
Major Challenges and Considerations
Moderators
Material | Temperature (K)
L-parahydrogen | 14 K
L-orthohydrogen | 14 K
Solid methane | 20 K
Solid D2 | 5 K
Clathrate hydrates | 2.4 K!
Reflectors
Material | Temperature (K)
MgH2 | 20 K
Nanodiamond | 296 K

## Slide 18: CONCEPT DEVELOPMENT
Ta
Reflector
Thermal
Moderator
Neutron
Extraction
Cold parahydrogen
Moderator
Target
Starting point
  Low dimensional para-hydrogen source cold source developed for HBS
  Highly efficient cold neutron converter
  Already realized
Geometrical Description
H2 Scattering Cross Section at 20K

## Slide 19: CONCEPT DEVELOPMENT
Ta
Reflector
Thermal
Moderator
Neutron
Extraction
Cold parahydrogen
Moderator
Target
Geometrical Description
Starting point
  Low dimensional para-hydrogen source cold source developed for HBS
  Highly efficient cold neutron converter
  Already realized
Very Cold Neutrons
  Use efficiency of para source
  “Embed” appropriate moderator within

## Slide 20: CONCEPT DEVELOPMENT
Ta
Reflector
Thermal
Moderator
Neutron
Extraction
Cold parahydrogen
Moderator
Target
Geometrical Description
Neutron
Extraction
Cold parahydrogen
Moderator
Very cold neutron
moderator
Thermal
Moderator
Target
System

## Slide 21
1. “Artificial” rectangular monoenergetic 25 meV neutron source
Avoid lengthy computation times
2. Add a zero importance mask around extraction channel at surface of moderator
  Only see neutrons exiting extraction channel
CONCEPT DEVELOPMENT
Simulation Description
Neutron
extraction
Cold parahydrogen
moderator
Very cold neutron
moderator
Thermal
moderator
Target
system
Artificial
source
Zero importance mask
17 April 2024
Page 21

## Slide 22
Fix L, fix r
2r – diameter of neutron extraction channel
L – distance from extraction channel boundary to centre of point tally
θ – divergence
R – radius of fictitious sphere for point tally definition
(x,y,z) – centre of point tally
R = 1cm
(x,y,z)
Zero
Importance
2r
L = 50cm
CONCEPT DEVELOPMENT
Simulation Description – Point Tally Definition
17 April 2024
Page 22

## Slide 23
dy = +4.5
dy = 0.0
dy = -4.5
dY is displacement of VCN from centred position (dy = 0)
CONCEPT DEVELOPMENT
Preliminary Simulation Results
17 April 2024
Page 23

## Slide 24
CONCEPT DEVELOPMENT
Preliminary Simulation Results
Methane centred
Para Large
Para pencil + methane
Para pencil
17 April 2024
Page 24

## Slide 25: Further work
Holistic Optimization Study of Methane in Para
Optimize the geometry – keeping in mind
  Consider requirements of instruments – development of appropriate figures-of-merit
  Assess how optics might shape moderator design
Study methane at 5K – practical considerations
Assess feasibility of designs
Other VCN Materials
Asses performance of other candidate materials
  Is it practical to consider deuterated materials for compact source like HBS?
    If yes, must also consider engineering challenges with cooling large moderator volumes
  Compare performance against para + methane solution
17 April 2024

## Slide 26: references
[1] J.M Carpenter and B.J. Micklich, ANL (05/42) (2005).
[2] V. Santoro et al, HighNESS Conceptual Design Report. arXiv:2309.17333v3 [physics.ins-det].
[3] Y. Shin et al, Nuc. Ins. Meth Phys Res A 620 pp. 382–390 (2010).
[4] S. Grieger et al, J. Chem. Phys. 109 3161–3175 (1998).
[5] A. Falenty et al, Nature 516 pp. 231-233 (2014).
[6] V. Czamler et al, EPJ Web of Conferences 286 05004 (2023).
[7] Y.C. Shin et al, Eur. Phys.J. Plus 136 882 (2021).
17 April 2024

## Slide 27
HBS Team
J. Baggemann
Th. Brückel
J. Chen
T. Claudio-Weber
T. Cronert (†)
Q. Ding
P.-E. Doege
M. El Barbari
T. Gutberlet
J. Li
K. Lieutenant
Z. Ma
E. Mauerhofer
N. Ophoven
U. Rücker
N. Schmidt
A. Schwab
E. Vezhlev
J. Voigt
P. Zakalek
- Design, verification,
instrumentation
ZEA-1:
Y. Bessler
R. Hanslik
R. Achten
F. Löchte
M. Strothmann
- Engineering
IKP-4:
O. Felden
R. Gebel
A. Lehrach
M. Rimmler
R. Similon
- Nuclear physics
INM-5:
B. Neumaier
- Radio isotopes
S. Böhm
R. Nabbi
- Nuclear simul.
Ch.Haberstroh
M. Klaus
S. Eisenhut
C. Lange
- Liquid H2, AKR-2
H. Podlech
O. Meusel
- Accelerator
W. Barth
- Accelerator
/ HIM
@hbsneutron
https://hbs.fz-juelich.de/
J. Fenske
- Instrumentation