## Slide 2: Timepix3 integration at ESS
Status update
PRESENTED BY anders Pettersson
(Interim) WPM Experiment Control and Data Curation

## Slide 3: Some background
  In 2022 ECDC/NITIS recieved the hardware with an informal request to integrate.
  Integration was started witha a standard ESS approach
  Progress according to our expectations
  Feb 2024: Vendor software demo/workshop (by Detg)
  ECDC joining as observer
  Followed by an unfortunate meeting
  -> 2 approaches are now discussed

## Slide 4
Original integration process (path A)
2

## Slide 5: Timepix Architecture
Timing
EFU
Data transformation
Data Publishing
Camera
Data Source
Kafka
The current timepix architecture based on the Event Formation Unit (EFU) used for all event based ESS detector
  The event formation unit designed for data transformation from UDP stream of detector events and ESS timing source
  The EFU performs on-the-fly calculations to transform the incoming UDP data the Kafka fla- buffer schema
  EFU can perform additional timing corrections, reductions, clustering, depending on the data source requirements

## Slide 6: Major processing steps and challenges
Main challenges with the timepix data pipeline
Timepix and EVR (Time) data parsing
Global time calculation
Photon event clustering
Calculate Relative Time of Arrival
Notes: EFU recieve data, parse it , calculating relative time in relation to pulsetime

## Slide 7: Schematic of architecture
Aligning with ESS standars of streaming and timestamping
Tpix3
NIC1
NIC2
Data-T
Serval SW
UDP
Time
UDP
TTL
IPC
EFU
IPC
UDP

## Slide 8
Overall status update
Data parsing
EVR data parser done and optimized
Done and optimized
Global time calculation
TDC and EVR time pairing done
Pixel time to global time conversion done
Photon hit clustering
Fixed time and space gap clustering approach implemented
Done but not optimized
Done but not optimized
Events are identified by center of mass calculation based on photon events ToT
Relative Time of Arrival
Calculation performed after the identification on the global time
Handling of delayed timing based on frequency
Done and optimized
Timepix pixel and TDC data parsing optimized
All major steps are implemented and the current timepix solution is capable to process data from the camera together with ESS time.
From ECDC perspective the development project is ready for cold commissioning, but not ready to deliver full scale science.
We currently miss realistic data with ESS timing to perform a required demonstration and fit cold commissioning.
Notes: ToT Time over threshold
Need to do this for streaming (Vendor not)

## Slide 9
Global time calculation and RToA
This challenge requires to align the camera
  Pixel timestamp
  TDC timestamp
  EVR’s Pulse timestamps
Challenge:
Each of these timestamps has different bin size period of reset. Data arrival is not ordered and not realtime.
Technically achieved global time (real time in ns) for each pixel based on EVR time and calcalculate relative time of each event.
Achieved 2024 Feb
Notes: Relativ etim eofarrival

## Slide 10: Photon hit clustering
Center of mass calculation based on Time over Threshold ToT
Cluster building gaps are configurable
Achieved 2023 June
Early tests on processing non timestamped data (also not agreed as suitable data!). Plots from a wire setup. One without charege runnning through an done without.
2D hierarchical clustering
Notes: Time over Threshold

## Slide 11
Clustering algorithm with details
The current algorithm aims for simplicity
The algorithm currently collects photon events similar in time and space. We do not do reduction yet.
Our current steps:
  Sorting: Hits (pixels) are sorted in processing window according to their global ToA.
  Time Clustering: Hits with arrival time smaller then predefined time gap are clustered.
  2D clustering: In each time cluster sub sets based on 2D space distance between hits are created. These form an event set.
  Event creation: For each event set the event time based on first hit ToA, and the pixel ID according to a center of mass (CoM) are calculated where 2D position weighted with the time over threshold (ToT).
  Event RToA: Calculate relative time of arrival (RToA)
Sorting
Time Cluster
Event creation
Hierarchical 2D cluster
Calculate Event RToA

## Slide 12: Challanges on path A
Further development and optimisation
EFU data processing need to be optimized
Need to further develop in house competence on scintillators, image processing algorithms etc

## Slide 13: Development at ESS
Access to know-how
Shadowing experiments for data collection
Experiments performed for Instrument Development
Community
ESS is providing this as open source to the community
ESS have resource to world class physicist in neutron imaging and science
ESS has resources for world class data scientist and software engineers
Access to beam time

## Slide 14
Benefit of the current architectures
Streaming data pipeline for continuous data processing and utilize the most modern data processing architectures
We using Kafka an open source, scalable and industry standard data broker
No license dependencies are applied, gives us flexibility and lot’s of potential for optimization and improvements
Together with the previous point we are fully opensource to share and strengthen the neutron community around the most modern data processing system
Modern Data Architecture
Industry standard Data Analytics
Event formation software shared with all event based detectors. Software design according to SDLC standards, with fully automated CI/CD
Community in mind, fully opensource
Data processing cluster with detailed monitoring infrastructure. Data only stored on HA storage, all components are replaceable, with automatic deployment.
High availability operation with support in mind
Common product, SDCL, CI/CD
Open source, flexible and future proof
Notes: Streaming /modern- Easier then replasing a old specialized PC.future proof, klusters
Uisng Kafak- often analytical tools often rely on kafka
SDLC Software Development LifeCycle
CI Continous integration CD Continous Deployment
Common product – garantees small maintanance 8only chanege in 1 place, with best algorithm)
HA High availablility
No sw licences used

## Slide 15
Path B:
Including vendor software
2

## Slide 16: Plan B: Vendor software in data pipeline
Timepix and EVR data parsing
Global time calculation
Photon event clustering
Calculate Relative Time of Arrival
The vendor software’s scope is the photon neutron event identification. Which not aligned with the data pipeline at ESS.
A substantial Integration effort is required.
Vendor SW scope

## Slide 17: Schematic of architecture
Tpix3
NIC1
NIC2
Data-T
Serval SW
EFU
UDP
Time
UDP
TTL
IPC
Vendor SW
IPC
?
?
?
Delta t > 1-2 min
Feedback > 1-2 min
?
Push out 10Gb/s
Status/monitoring in NICOS
IN/OUT Vendor SW
Stable handling of files

## Slide 18: Plan B merits
Advanced neutron event identification
Vendor sw is further advanced in photon to neutron event identification method
According to the vendor its software is capable to perform multi core, parallel processing. (not documented, performance analysis not seen)
Vendor sw’s algorithm is optimized around different scintillator
High utilization of resources
Vendor sw’s algorithm can scale up image resolution higher then the camera delivers

## Slide 19: Plan B: Considerations
Currently not a full scale solution
Vendor sw software do not resolve ESS time calculation and provide the required RToA
Vendor sw do not provide streaming based data processing – workaround required to fit ESS infrastructure
It is not trivial to synchronize time information from vendor sw with ESS time!

## Slide 20: Plan B: Considerations
Limited scalability
Plan B requires intensive file writing into filesystem, multiple times during the processing steps
Sharing workload between multiple processing unit would requires high performance shared filesystem between the nodes
Current heavy IO and complex processing steps would require unique and expensive hardware

## Slide 21: Plan B: Considerations
Vendor dependency
This solution will be Blackbox for ESS, any problem or change on the software would require change request procedure.
(NDA would introduce legal risk for parallel in-house open source development)
Non standard EFU
The solution would not disclose EFU, which would still needed to perform timing calculation and data transformation for Kafka
This would introduce new interface instead of the existing ones.
Notes: SLA: Service Level Agreement
CR: Change Request

## Slide 22: Plan B: Considerations
Responsible, not tested
Vendor sw Blackbox setup (EFU interface is not scope of ECDC)
Responsibility for the setup/monitoring
This integration into ESS architecture is not tested bottlenecks are not fully identified
Required maintenance unknown
Responsibility for monitoring/maintenance

## Slide 23
Chapter slide or
a breaker slide
2

## Slide 24: Summary
  Path A
  Initial event formation tested
  Timstamping verified with ESS infrastructure
  Data streaming verified (not yet scaled up)
  Optimisation dependent on ESS/community
Path B
  Event formation approved by instrument scientist (but not timestaped with ESS time!)
  Timestamping not resolved
  Data streaming not resolved
  Optimisation/changes dependent on Vendor

## Slide 25: Short term plans
  Path A (ECDC)
  Plan for full demo of current project status (Path A)
  Present evaluation of experiment data (from ISIS Oct/Nov-23)
  Participate at ISIS Experiment (with t stamp)
  Capture/present data at ISIS experiment
Path B (Vendor/Instrument/
  Provide documented interface IN/OUT of vendor sw
  Define preliminary design for time synchronisation
  (Plan to have raw data collection, image reconstruction. Not live (Pairing of TDC)).
Path forwards
Access to ”true” reference data if possible
Evaluate status of both paths

## Slide 26: Lastly
ECDC/NITIS want to work with the instruments to find the best solution.
We all want the success of ODIN as part of ESS
ECDC also benefits of having two system for reference

## Slide 27: Thank you for listening