## Slide 1: Moderator optimisation for a spallation-driven ultracold-neutron source using superfluid helium
January 17, 2025 – The Fundamental Nuclear and Particle Physics at the ESS workshop
Wolfgang Schreyer
Oak Ridge National Laboratory

## Slide 2: A dedicated spallation target at TRIUMF
Beamline 1A
Fast kicker magnet
0 – 40μA for UCN
483MeV cyclotron
Spallation target

## Slide 3
What to optimize: UCN source parameters
TUCAN source optimization
TUCAN source cryostat and commissioning

## Slide 4: Heat load and production rate need to be carefully balanced
Heat load Q
Production
Rate P
Storage lifetime τ
Number of ultracold neutrons ~ Production rate P x Storage lifetime τ
CN-beam LHe source τ  τβ
Q ~ mW
(ILL)
Spallation LHe source τ ~ 20s
Q ~ 10W
(TUCAN)
sD2 source τ ~ 100ms
(PSI, LANL, NCSU, FRM-2)
Reactor LHe source τ ~ 10s
Q ~ 35W
(PNPI)
Improved cooling
Optimized moderators
UCN converter
CN source

## Slide 5: UCN density must be extracted
Time
UCN density
Pτsrc/Vsrc
Pτtot/Vtot
Vsrc
Vguide
Vexp
Valve
Valve opened
CN source

## Slide 6: Match production intervals to UCN experiment
NCSU, FRM-2, PNPI
Continuous UCN production and full heat load
TUCAN, ILL
Continuous UCN production during experiment fill, minimal heat load otherwise
PSI, LANL
Intermittent UCN production during experiment fill (Beam cycle time > τsrc), minimal heat load otherwise
Continuous (reactor) source
On-demand source
Intermittent (spallation) source
Time
Heat load
Time
Heat load
Time
Heat load
Fill
Fill
Fill
Fill
Fill
Fill

## Slide 7: Ultimate goal: maximize number of UCN that can be detected after experiment cycle
Ndet ~ P(E)τtot(E) Vexp/Vtot ε(E)
Deuterium sources: E > 108 neV
Vertical extraction: ε(E) ~ √E/(E + mgh)
Vsrc
Vguide
Vexp
Valve
g
CN source

## Slide 8: Optimal neutron temperature for a superfluid helium converter is 7.7K
Cold moderators considered for TUCAN:
Heavy water ice
Liquid deuterium
Liquid hydrogen
(Deuterated) solid methane
(Deuterated) solid mesitylene
P. Schmidt-Wellenburg et al, Nucl. Instr. Meth. Phys. Res. A, 611, 259-262 (2009)
E. Korobkina et al, Phys. Lett. A, 301, 462-469 (2002)

## Slide 9: TUCAN moderator geometry was refined over many iterations

## Slide 10: TUCAN moderator geometry was refined over many iterations
Vertical extraction
Horizontal extraction

## Slide 11: TUCAN moderator geometry was refined over many iterations
Effect of superfluid vessel material
Effect of cold moderator (individually optimized)

## Slide 12: TUCAN moderator geometry was refined over many iterations
Fully optimized model maximizing Pτsrc/Vtot
With engineering constraints

## Slide 13: Need to cool large volume of superfluid helium to ~1K at heat load of ~10W
Direct pumping
3He fridge
τsrc-1 ≈ τHe-1 + τwall-1 + τ3He-1 + τβ-1
τHe ~ Q-1..-1.5
τHe-1 ≈ 0.016 T7
Heat transport in He-II (Gorter-Mellink)
Interface resistance at heat exchanger
Pumping speed

## Slide 14: 3He cryostat built in Japan

## Slide 15
B4C-filled panels
Graphite
D2O
LD2
He-II
Target
Steel shielding
Steel
shielding
To nEDM
2nd UCN port
Concrete shielding
Concrete shielding
3He cryostat
LD2 cryostat
3He-4He heat exchanger
Superconducting polarizer
0
1
m
Switch

## Slide 16: 3He heat exchanger
60cm

## Slide 17: Multi-layer moderator vessels

## Slide 18: Heat exchanger and cryogenic UCN guide installed in cryostat
Moderators
3He heat exchanger
Experiment

## Slide 19: Nearly completed installation

## Slide 20: Successful TUCAN source commissioning
Phase 1 | Performance test of pumps | 2021 ✓
Phase 2A | 4K cooldown | Fall 2023 ✓
Phase 2B | 1K cooldown (natural helium only) | Winter 2023 ✓
Phase 3A | 3He system filled with natural helium | June 2024 ✓
Phase 3B | First cooldown with 3He | July 2024 ✓
Phase 5 | Condensation of 4He | October 2024 ✓
Phase 6A | First UCN production without LD2 | November 2024 ✘
Phase 4 | LD2 condensation | Spring 2025
Phase 6B | UCN production with LD2 | Summer 2025
Phase 7 | UCN production and extraction into experimental area | Fall 2025
0.85K @ 10W!
No superleaks!

## Slide 21: TUCAN source will be the strongest source in the world
Production rate: 1.5∙107 UCN/s @ 8.1W
Storage lifetime: ~20 s
Filled into nEDM cells: 14,000,000 (230/cm3)
Detected after nEDM cycle: 1,400,000 (23/cm3)
nEDM sensitivity 10-27 ecm achievable in 400 days
W. Schreyer et al, Nucl. Instrum. Meth. Phys. Res. A 927, 101-108 (2019)
S. Sidhu, W. Schreyer, et al, EPJ Web of Conferences 282, 01015 (2023)
C. M. Lavelle: Cryogenic Liquid He4 and Deuterated PMMA Scattering Laws for MCNP, AOS-20-0265

## Slide 22: New moderator concepts and improved cooling techniques are needed to scale further
Scaled 3He fridge?
Direct pumping
Cryocompressors
New moderator concepts
Improved cooling technologies
2∙109 UCN/s, 100W @ 1.6K
K.K.H. Leung et al, J. Appl. Phys. 126, 224901 (2019)
Neutron filter
Heat load -46%
Production -36%

## Slide 23: TUCAN source will be the strongest source in the world
Production rate: 1.5∙107 UCN/s @ 8.1W
Storage lifetime: ~20 s
Filled into nEDM cells: 14,000,000 (230/cm3)
Detected after nEDM cycle: 1,400,000 (23/cm3)
nEDM sensitivity 10-27 ecm achievable in 400 days
W. Schreyer et al, Nucl. Instrum. Meth. Phys. Res. A 927, 101-108 (2019)
S. Sidhu, W. Schreyer, et al, EPJ Web of Conferences 282, 01015 (2023)
C. M. Lavelle: Cryogenic Liquid He4 and Deuterated PMMA Scattering Laws for MCNP, AOS-20-0265