## Slide 1: NMX Updates and Demos
Neutron Macromolecular Crystallography
PRESENTED BY Aaron finke
2025-04-08

## Slide 2: The NMX Team
Who’s building NMX?
2025-04-08
Justin Bergmann
Commissioning Instrument Scientist
Aaron Finke
Instrument Data Scientist
Laïs Passine (ECDC)
Controls/MXCuBE
Esko Oksanen
Lead Instrument Scientist
Swati Aggarwal
Commissioning
Sample Scientist
Daniel Lundström
Lead Engineer
Zoë Fisher (DeMAX)
Deuteration Wizard

## Slide 3: NMX: Neutron Macromolecular Crystallography
Determination of precise hydrogen atom positions in protein crystals with an innovative detector technology and robot-based goniometry.
DMSC Deliverables: ESSNMX, eventually to a complete diffraction-to-refinement pipeline using a combination of software developed at DMSC and partner institutions.
CC Goals: Processing simulated NMX data, motion tests (NICOS)
HC Goals: Beam-to-data
A Quasi-Laue TOF instrument for Macromolecular Crystallography
2025-04-08
NMX moved from Tranche 2 to Tranche 1 in 2023

## Slide 4: NMX Instrument Update
2024-04-17

## Slide 5: Detector Testing
Progressing!
Three detector panels
Triple Gd-GEM
Active area 512.2 mm x 512.2 mm
400 µm effective pixel size
1200 x 1200 effective pixels
We have demonstrated complete detector “events”  EFU  filewriter  Nexus TOFRaw pipeline
  Next steps: tests at neutron sources (CERN in April, ILL in August)

## Slide 6: Data pipeline status
Neutron Macromolecular Crystallography
Instrument simulation
  Mcstas data modeling
  Saving of events to Nexus NXLaueTOF format
  Data Collection Strategy
Data reduction
  ESSNMX Data Reduction Pipeline
  Pyscale
Data analysis
  DIALS for Neutrons
  Phenix for Neutron MX
Data archiving
  Metadata (NXLaueTOF format)
  Piping to SciCat
2025-04-08
Done
Done-ish*
In Progress
To do
ESSNMX
Reduction Pipeline
* Ready for HC but still under development

## Slide 7: McStas NMX Simulations
Backend with Union
McStas
Small wavelength interval: 2.5 – 2.6 Å, full frame 1.7 Å
Mads Bertelsen
2025-04-08

## Slide 8: NMX McStas Simulations
Single_crystal component
  Used leucine with 4943 reflections
  Higher speed up for longer lists
  Perdeuterated pyrophosphatase with 1795256 reflections
1st order
0th order
Mads Bertelsen
2025-04-08

## Slide 9: NMX McStas Simulations
Single_crystal component
  To do:
    Model scattering from solvent
    Process simulated data in DIALS (in progress)
1st order
0th order
Mads Bertelsen
2025-04-08

## Slide 10: MXCuBE
The Data Collection GUI for NMX
Use MXCuBE Web at NMX for a more friendly UI.
MXCuBE is a multi-facility data collection GUI used at many MX synchrotron beamlines around the world.
NMX will be the first neutron facility to use MXCuBE. Joined the collaboration in 2024.
Have MXCuBE as the main interface for the user + NICOS also present for prototyping, calibration and backup.
View of NMX experimental hutch
MXCuBE Web
2025-04-08

## Slide 11: Demo Neutron Single-Crystal MX Workflow
NMX
Instrument simulation
Data catalogue
Data reduction
Data analysis
Reduced data files
Data catalogue
simulated detector data
Samples:
Rubredoxin
Loading NeXus file
Grouping detector data
Binning TOF histogram
“nxs” format
Fully automated workflow, from events -> h,k,l, I, I/sig(I)
2025-04-08

## Slide 12: Demo: Web-based interface
Considerations:
NMX users by and large will not have a working knowledge of Python
  Maybe they will know command line/Linux but not always
Automated processing should yield results in formats/statistics users understand
Since processing takes time, real-time results pending can be useful.
Web-based results interface app written in Flask/JS
Data reduction for NMX with ESSNMX/DIALS
ESSNMX
Reduction Pipeline
2025-04-08