## Slide 1: Instrument simulations with SIMRES Advanced features and use cases
Jan Šaroun, Nuclear Physics Institute CAS, Řež, Czech Republic

## Slide 2: About SIMRES
History: since early 1990th, initially for 3-axis spectrometers (ResTrax)
Today: general purpose neutron ray-tracing
Desktop application (interactive virtual instrument)
Not so versatile (new components difficult to implement)
Integrated variance reduction methods = very fast (depending on configuration)
  Optional reverse tracing: start at the sample …
Complementary: includes components and features not available in McStas
Differences vs McStas

## Slide 3: About SIMRES
History: since early 1990th, initially for 3-axis spectrometers (ResTrax)
Today: general purpose neutron ray-tracing
Computing time to 1% accuracy for various BEER@ESS operation modes
Project-driven development:
Powder and engineering diffractometers (monochromatic and ToF)
Neutron transport optics, crystal monochromators
Strain-scanning, beam 1x3 mm2
Imaging, slit 10x10 mm2
Diffration beam 2x5 mm2
Full white beam
Desktop application (interactive virtual instrument)
Not so versatile (new components difficult to implement)
Integrated variance reduction methods = very fast (depending on configuration)
  Optional reverse tracing: start at the sample …
Complementary: includes components and features not available in McStas
Differences vs McStas

## Slide 4: CRYSTAL: Elastically bent crystals
Used as monochromators and analyzers
Single reflecting plane
Quasiclassical neutron trajectories in uniformely bent single crystals
P. Lukáš, J. Kulda, Phys. stat. sol. (b) 166,41 (1989)
Fails near the perfect crystal limit
Si 111, l=2.1 Å
OK for monochromators etc.
Hyperbola - can be replaced by lines for R <~ 10 m
Assumes uniform deformation:
Today:
CRYSTAL models bent mosaic crystals and their 3D focusing arrays.
Bent perfect or flat mosaic crystals are special cases handled by the same algorithm
Recently implemented in McStas
Daniel L. Christensen: ICNS2025 presentation
Sandwich of bent Si wafers
Arranged in a focusing array
e.g. monochromator at SALSA@ILL

## Slide 5: XTAL: Extended bent single crystal model
Bent perfect single crystals (Si, Ge, …)
Multiple reflections (crystallographic data provided for Si, Ge, C, Al2O3, MgF2, …)
gradient of
Choose a wavelength range
Find all Ghkl where Dlhkl fits in this range
Select one Ghkl or transmitted beam (G000 )
Optional: include multiple reflections:
list all possible paths to hkl …
How it works:
NOTE: rec. lattice varies with position in the crystal

## Slide 6: XTAL: Extended bent single crystal model
Fast algorithm – aims at a single final hkl reflection
All competing reflections are considered for beam attenuation
Aplication:
Studies of multiple reflection effects
monochromators, analyzers (including focusing arrays)
… or a stack of bent wafers
111
112
Experimentally verified: P. Mikula et al., Phys. Met. Metall. 123 (2022) 354-1360
Simulation of “forbidden“ reflection Si 222
(222) = (331) + (111)
solid state benders
SALSA@ILL monochromator
Si004
Transmitted
spectrum
Beam attenuated by ~30 contributing reflections
Spectrum after monochromator

## Slide 7: XTAL: Extended bent single crystal model
Example: Bi-spectral switch for BEER@ESS
stack of 160 Si single-crystal blades
coated with m=3 NiTi supermirror
?
Problem: residual elastic deformation of Si
ESS moderator
Spectrum at the sample was predicted by both McStas and SIMRES models of BEER:
What we observed in the test at IMAT@ISIS:
expected
measured

## Slide 8: XTAL: Extended bent single crystal model
measured
simulated
SIMRES/XTAL: beam extinction by diffraction in a stack of bent Si blades (without NiTi)
McStas: simulation of the IMAT experiment with a new solid state bender component (under development, derived from Guide_multichannel.comp)
Total transmission probability for bending <R> = 2.5 m
Details of the IMAT experiment presented at ICNS 2025:
J. Šaroun, J. Fenske, G. Nowak, C. Durniak, S. Britto, W. Kockelmann, D. Raspino, P. Beran, Z. Tasi, Z. Ludanyi Poster B1/441
Example: Bi-spectral switch for BEER@ESS

## Slide 9: Binding to McStas running McStas as a part of SIMRES instrument model
SIMRES instrument model
Sample replaced by event monitor
McStas simulation
MCPL_input
MCPL_output
Access to variety of McStas components
Advanced sample models
Neutron-optical components not available in SIMRES
Unions: e.g. complex samples and sample environment …

## Slide 10: Binding to McStas
g-Fe
a-Fe
Example:
Residual stress mapping, simulation of pseudo-strains
McStas UNION section
SIMRES
secondary
beam
SIMRES
HK4@NPI
primary beam
peak positions vary also for a stress-free material = pseudo-strain
scan
3 cm
slit
2x3 mm2
g-Fe 111
a-Fe 110

## Slide 11: Binding to McStas
Example:
Residual stress mapping, simulation of pseudo-strains
Peak shift
Peak intensity
Correction for measured residual strain
(similar magnitude !)
Finding the position of the interface
Assess texture or chemical gradients
Simulations are used to:

## Slide 12: Event monitors
source
sample
monitors
last component
a “successful neutron” triggers event storage
Registered events are kept in the memory until next simulation
=> visualize and export in any projection and binning
Usage
Instrument optimization
Sample monitors: provide sampling distribution for data analysis
trigger

## Slide 13: Sampling distribution for data analysis
event list from sample monitors: (r, ki, kf, w)
Use case: treatment of pseudo-strains
complete instrument resolution function
measured variable:
as analysed by the detection system
Simulation with an ideal powder diffraction sample:
single diffraction plane,
no beam attenuation
+
=
Peak profile
“as measured”
Sample properties
Convolution sum can be evaluated by external tools:

## Slide 14: STRESSFIT: Python package for treatment of pseudo-strains
https://github.com/NPLtools/stressfit
The MC convolution is used in the cost function for deconvolution of measured residual strain distributions
Diffraction geometry
“As measured” strain distributions
Deconvoluted intrinsic strain
Test on synthetic data for BEER and HK4 instruments:

## Slide 15: Concluding remarks
Availability: https://github.com/saroun/simres
Maintenance, bug fixes, minor upgrades + support continues …
Re-use in McStas:
Implementation of some of the SIMRES components in McStas (help welcome)
So far:
Monochromator_bent, NPI_tof_dhkl_detector, NPI_tof_theta_monitor, Guide_multichannel, bispectral_switch (under development) …
Future:
Major refactoring would be desired but not likely to happen …
Complex development/compilation toolchain
  Core: Fortran+C, CLI: Java, GUI: Java+Java3D, Lazarus Pascal
  => Move to: Fortran/C + Python ?
Manpower …

## Slide 16: Thank you for attention