## Slide 2: Introducing Effects of Surface Physics in McStas Union
PRESENTED BY Mads Bertelsen

## Slide 3: Introduction
McStas instrument structure
Component sequence
Source
Guide_bunker
Chopper
Guide_1
Guide_2
Guide_3
Sample
Analyzer
Detector

## Slide 4: Union components
  Geometry constructed from simple shapes
  Each assigned a material
  All shapes given a priority value
  Can overlap
  In overlap, largest priority value decides material
Geometry
Boxes, cylinders, cones, spheres
2.1
7.7

## Slide 5: Union components
  Assemble materials from scattering processes
Geometry
Incoherent_process
Powder_process
Incoherent_process
Single_crystal_process
Incoherent_process
Single_crystal_process
NCrystal_process
Inelastic sample
Al
Sample
Vacuum

## Slide 6: Union components
Using the Union components
Typical sample component
Union components
Single_crystal.comp
Geometry
Raytracing
Absorption
Scattering
- Incoherent
- Single crystal Bragg
Multiple scattering loop
Incoherent_process.comp
Incoherent scattering
Single_crystal_process.comp
Single crystal scattering
Union_make_material.comp
Union_box.comp
Union_master.comp
Raytracing
Absorption
Sampling scattering physics
Multiple scattering
Union_init.comp
Union_stop.comp
Union_cylinder.comp

## Slide 7: Union components
  Lets make a colimator
  Absorbing blades limit divergence
Simple example - colimator
Air
Cd
McStas

## Slide 8: Union components
  Lets make a colimator
  Absorbing blades limit divergence
  Add a Be block, now its a filter
Simple example - filter
Air
Cd
Be
McStas

## Slide 9: Use cases
  Samples
  Sample holder
  Air
  Sample environment
  Colimators
  Filters
  Beam monitors
  Monochromators
  Detectors
  Instrument backends
Photo by Pia Ray Jensen

## Slide 10: Union components
  Bulk scattering, scattering properties independent of position in material
  Gravity not simulated
  Polarization not supported
  No physics when rays cross an interface
Assumptions

## Slide 11: Interface physics update
  Code from Refractor.comp by E. Farhi, B. Cubitt
  Scattering length density provided with material definitions
  Refraction calculation require SLD for both materials
  Snells law with fall of
Refraction
n1 sin(theta1) = n2 sin(theta2)
n = sqrt(1.0-(lambda*lambda*SLD/PI))
n1
n2

## Slide 12: Interface physics update
Simple example - filter
Air
Cd
Be
No refraction
Refraction

## Slide 13: Interface physics update
Simple example - filter

## Slide 14: Interface physics update
Surface processes
  Surface process components
    Gets normal vector, initial wavevector and weight
    Returns final wavevector and weight
  Allows
    Reflectivity curve
    Thin absorbing paints
    …
  Can be attached to geometry faces
    Each outside face
    ... and one for all cuts in inside of material

## Slide 15: Interface physics update
B: Surface process
A: Surface process
Geometry A
Geometry B
Surface stacks
  Surface process components
    Gets normal vector, initial wavevector and weight
    Returns final wavevector and weight
  Allows
    Reflectivity curve
    Thin absorbing paints
    …
  Can be attached to geometry faces
    Each outside face
    ... and one for all cuts in inside of material

## Slide 16: Interface physics update
  Surface process components
    Gets normal vector, initial wavevector and weight
    Returns final wavevector and weight
  Allows
    Reflectivity curve
    Thin absorbing paints
    …
  Can be attached to geometry faces
    Each outside face
    ... and one for all cuts in inside of material
    Several processes can be combined into a stack
Surface stacks
B: Surface process 2
A: Surface process 1
B: Surface process 1
Geometry A
Geometry B

## Slide 17: Interface physics demo
Super-mirror
Fe
Ni
Al
Bi single crystal
Beam
McStas

## Slide 18: Interface physics demo
McStas

## Slide 19: Interface physics demo
McStas

## Slide 20: Interface physics use-case
Surface physics relevant for
  Optics
    Guides
    Focusing optics
    Refractive optics
    .. in sample environments
  Reflectometry
    Sample
    Substrate

## Slide 21: Conclusion
  Union components constitutes a powerful tool in McStas to simulate complex systems
  Newly added interface physics expands their use case to optics, reflectometry and more
  Remaining limitations:
    No simulation of gravity
    Lack support for polarization

## Slide 22: Thanks for your attention!