## Slide 2: McStas instrument simulations
Mads Bertelsen
PRESENTED BY Mads Bertelsen

## Slide 3: McStas
  Monte Carlo ray-tracing simulation
  Specialized for neutron scattering
  Started 1998 at RISØ, DK
  2 Full time developers at DMSC
Overview
Peter Willendrup
Mads Bertelsen

## Slide 4: McStas
  Large component library
  Beamline components / Samples / …
  McStas instruments is a sequence of components
Components

## Slide 5: McStas
  NCrystal scattering kernel library
    Single crystals, powders, gasses, …
    Stand-alone or as plugin, for example GEANT-4
    Plugs into McStas as:
      Sample component / Union process
NCrystal in McStas
Elastic neutron scattering models for Ncrystal, Thomas Kittelmann and Xiao-Xiao Cai, (2021)
Bragg scattering in Pyrolytic graphite
Thomas Kittelmann
https://github.com/mctools/ncrystal/wiki
https://github.com/mctools/ncrystal-notebooks

## Slide 6: McStas
  Accepted and trusted in community
  More than 400 citations of main papers
  Used to design many ESS instruments
Community
McStas (i): Introduction, use, and basic principles for ray-tracing simulations,
P. K. Willendrup and K. Lefmann, Journal of Neutron Research (2019)

## Slide 7: McStas
History of schools
+ e-learning + Local schools + University courses

## Slide 8: McStas
Map of usage

## Slide 9: McStas
  Can replicate real instruments well
  Powder diffractometers in Israel
Verification
KANDI-II 2.47 Å wavelength
Si
Gr2GaC
KARL Si sample
PG 2.421 Å
Cu 0.98 Å
Verification of the McStas code using two double axis neutron diffractometer,
D. Potashnikov, A. Pesach, O. Rivin, O. Ozeri, Z. Yungrais, M. Bertelsen and E. N. Caspi,
NIMA (2024)
Foil intensity measurements

## Slide 10: McStas
Cases
Design
K. H. Andersen et. al. The instrument suite of the European Spallation Source, Nucl. Instrum. Methods Phys. Res. A, vol. 957, 163402 (2020)
“For all instruments, their design has been optimised and their performance thoroughly evaluated using both analytical calculations and Monte-Carlo ray-tracing simulations …”
Preparation
G. Simutis, J. Küspert, Q. Wang, J. Choi, D. Bucher, M. Boehm, F. Bourdarot, M. Bertelsen C. N. Wang, T. Kurosawa, N. Momono, M. Oda, M. Månsson, Y. Sassa, M. Janoschek, N. B. Christensen, J. Chang, D. G. Mazzone,
Commun Phys 5, 296 (2022)
Virtual experiment
Instrument
Cryostat
Sample holder
Sample
14 meV setting
5 meV setting
H. Jacobsen, S. L. Holm, M.-E. Lăcătuşu, A. T. Rømer, M. Bertelsen, M. Boehm, R. Toft-Petersen, J.-C. Grivel, S. B. Emery, L. Udby, B. O. Wells, K. Lefmann,
Phys. Rev. Lett. 120, 037003 (2018)
Explanation
Investigation of instrument resolution effects on surprising result from measurements, eliminating possible explanations.
Simulated scan of double peak in q
Confirmation of hypothesis, excludes resolution effects

## Slide 11: McStas
  User can assemble sample materials
  Multiple scattering in complex geometry
Union components
Incoherent_process
Powder_process
Incoherent_process
Single_crystal_process
Incoherent_process
Single_crystal_process
Phonon_simple_process
Inelastic sample
Al
Sample

## Slide 12: McStas
Magnet project
Using McStas Union components to simulate a magnet sample environment and predicting background with machine learning,
Petroula Karacosta, Master thesis with Kim Lefmann, University of Copenhagen
  Describe geometry and materials
  Good student project

## Slide 13: McStas
User interface
  C meta-language instrument file
  Help and plotting from mcgui
McStas instrument file
DEFINE INSTRUMENT example(theta)
DECLARE
// C-code – declare variables
double two_theta;
INITIALIZE
// C-code - perform initial calculations
two_theta = 2.0*theta;
TRACE
// McStas component sequence
Monochromator = Monochromator_flat(
yheight=0.1, zdepth=0.05, Q=1.78)
AT (0,0,2.0) RELATIVE source
ROTATED (0, theta, 0) RELATIVE source
FINALLY
// C-code – perform calculations after simulation

## Slide 14: McStas
User interface
Instrument file
Simulated instrument
z
y
COMPONENT A(par=2)
AT (0, 0, 0.5)
ROTATED (-10, 0, 0)
COMPONENT B(width=0.3)
AT (0, 0, 4.0)
ROTATED (10, 0, 0)
COMPONENT C(length=2.5)
AT (0, 0, 11.5)
ROTATED (-12, 0, 0)
x

## Slide 15: McStas
COMPONENT B(width=0.3)
AT (0, 0, 4.0)
ROTATED (-10, 0, 0)
COMPONENT C(length=2.5)
AT (0, 0, 11.5)
ROTATED (12, 0, 0)
COMPONENT A(par=2)
AT (0, 0, 0.5)
ROTATED (10, 0, 0)
Execution of simulation
Instrument file
c file
Executable
McStas
compiler
Users
c - compiler
  Assemble from component library
  Place components in a sequence
  Place them in simulated space
  Execute through terminal or mcgui
Simulated instrument

## Slide 16: McStas
McStasScript overview
  Python McStas API
    Build instrument object
    Execute simulation
    Receive data as Python objects
  Open source
  https://github.com/PaNOSC-ViNYL/McStasScript
  Comprehensive test suite
Local components
Produced data
Generate instrument file
c file
Executable
McStas
compiler
Users
c - compiler
McStasScript
Instrument file

## Slide 17: To Python slides for demo!