## Slide 1: Accelerator Components and Technologies
Christine Darve
Nordic Particle Accelerator School, NPAS2015
http://www.eit.lth.se/index.php?ciuid=922&L=1
Lund University
August 19, 2015

## Slide 2: Outline
  Types of Particle Accelerators
  Accelerator Characteristics
  RF Cavity
  Superconductivity and Superfluidity
  Examples of the Particle Accelerators:
    The European Spallation Source (SRF cavities R&D)
    The LHC (low-beta magnets environment and Controls)
    The Tevatron (accelerator complex and technologies)

## Slide 3: Acknowledgements & references
Acknowledgement to D. McGinnis, M. Vretenar and P. Lebrun
US-Particle Accelerator School, http://uspas.fnal.gov/materials/materials-table.shtml
CERN Accelerator School http://cas.web.cern.ch/cas
A few books
RF Linear Accelerators, T.P. Wangler, Wiley, 2008
RF Superconductivity for Accelerator, H. Padamsee, J. Knobloch, T. Hays, Wiley, 2011
An introduction to particle accelerators, E.J.N. Wilson, Oxford Univ. Press, 2001
An introduction to the physics of high-energy accelerators, D.A. Edwards & M.J. Syphers, Wiley, 1993
The principles of circular accelerators and storage rings, P.J. Bryant & K. Johnsen, Cambridge Univ. Press, 1993

## Slide 4: Type of Particle Accelerators
>1980 -Tevatron @ Fermilab
980 GeV
>2008 - LHC @ CERN
7-14 TeV
80 keV
Ernest Lawrence
(1901 - 1958)
Livingston’s diagram
Each generation built on the accomplishments of the previous ones raising the level of technology ever higher

## Slide 5: High power H/D beams around the world
Notes: Accelerator-based for interdisciplinary research, nuclear research, fundamental physics, spallation sources.
e.g. SNS, MYRRHA, C-ADS
FNAL, CERN
IPHI
SPIRAL- radioactive ion

## Slide 6: Type of Particle Accelerators Used for ?
Discovery science: e.g. High Energy Physics
Materials research/manufacturing: e.g. light sources, spallation source, Accelerator Driven Systems (ADS)
National security
Medical Applications:
e.g. Neutron and Proton Therapies
MRI and NMR
Today: > 35,000 accelerators are in operation around the world
X-ray scanning
iThemba LABS
FNAL
SLS
.. and “has been”

## Slide 7: Outline
  Types of Particle Accelerators
  Accelerator Characteristics
  RF Cavity
  Superconductivity and Superfluidity
  Examples of the Particle Accelerators:
    The European Spallation Source (SRF cavities R&D)
    The LHC (low-beta magnets environment and Controls)
    The Tevatron (accelerator complex and technologies)

## Slide 8: Accelerator Characteristics ElectroMagnetism - Lorentz
Electric Fields to accelerate charged particles
RF accelerator components
Magnetic Fields to bend, steer, (de)focus
 Magnet components
 | Electron | Proton
Rest mass [Kg] | 9.11E-31 | 1.67E-27
Rest mass [MeV] | 0.511 | 938
V~0.95 c [MeV] | 1.1 | 2000
ratio | 1 | 1836
Notes: Einstein ? Newton ?

## Slide 9: Accelerator Characteristics ElectroMagnetism - Maxwell

## Slide 10: Accelerator Characteristics DC to AC Accelerators
    Linear Accelerators (LINAC): Large space charge
    DC and AC components: Cockroft-Walton and Van de Graff, RFQ, DTL, RF cavities
Each Linear Accelerator starts by a source followed by DC accelerator components
Need to switch to AC due to the accumulation of high voltage causing sparking
So we need to use Radio-Frequency sources
As an effect, the beam is bunched
 Principle of the Drift Tube Linac:

## Slide 11: Accelerator Characteristics
    ESS LINAC is 600m long (350m of acceleration) and reaches an energy of 2 GeV
    Assuming we need a 7 TeV machine (LHC), the Linac should be 1,225 km long !
    Linac over and over ?
     Synchrotron Accelerators:
    Space charge effect becomes small
    * Cover range where particle velocity is nearly cst.
    e.g. LHC, Tevatron
Linac 2 GeV
11

## Slide 12: Accelerator Characteristics Family of Linac component
RF cavity
EM fields enclosed in a cavity with resonant frequency matching that of RF generator
Drift Tube Linac
RF Quadrupole
At low energy proton, the RFQ permits:
        1. Bunching of the beam
        2. Focusing quadrupole
        3. Accelerating
Every cell is different, focusing quadrupoles in each drift tube
If f >10 MHz, the DTL acts like an antenna and radiates energy instead of using it for the acceleration

## Slide 13: Outline
  Types of Particle Accelerators
  Accelerator Characteristics
  RF Cavity
  Superconductivity and Superfluidity
  Examples of the Particle Accelerators:
    The European Spallation Source (SRF cavities R&D)
    The LHC (low-beta magnets environment and Controls)
    The Tevatron (accelerator complex and technologies)

## Slide 14: RF Cavity
Beam
RF Input
Power Amplifier (Klystrons)
Power Coupler
Gap
FNAL Booster Cavity
Waveguide

## Slide 15: RF Cavity

## Slide 16: RF Cavity Cavity Field Pattern
For the fundamental mode at one instant in time:
Electric Field
Magnetic Field
Out
In
Wall Current

## Slide 17: RF Cavity Cavities Modes
Fundamental and High Order Modes (HOM)

## Slide 18: RF Cavity RLC Model for Cavity Mode
Position:
Amplitude:
Width
Function of geometry and cavity material
Function of geometry
Around each mode frequency, we can describe the cavity as a simple RLC circuit.
Req is inversely proportional to the energy lost
Leq is proportional to the magnetic stored energy
Ceq is proportional to the electric stored energy

## Slide 19: RF Cavity RLC Parameters for a Transmission Line Cavity
For the fundamental mode of the transmission line cavity:
The transfer impedance of the cavity is:

## Slide 20: RF Accelerator
Vgap
Leq
Req
Ceq
Rgen
Igen
Zo
The cavity is attached to the power amplifier by a transmission line.
The internal impedance of the power amplifier is usually matched to the transmission line impedance connecting the power amplifier to the cavity.
  As in the case of a Klystron protected by an isolator
  As in the case of an infinitesimally short transmission line

## Slide 21: SRF Cavities Performances
Accelerating gradient
Peak Surface fields
Power Dissipation
Cavity Quality
Shunt Impedance
Few limitations of performance:
Thermal Breakdown, alias quench
Field Emission: Electron induced by an electrostatic field
Multipacting: electron avalanche
Limit power loss in the cavity wall:
By using low-resistant material or superconductors
By rounding the shape to optimize the field distribution
Limit shape edge to prevent field emission
Good vacuum to limit breakdown

## Slide 22: Cavity gradients

## Slide 23: Cavity Q
If the cavity walls are lossless, then the boundary conditions for a given mode can only be satisfied at a single frequency.
If the cavity walls have some loss, then the boundary conditions can be satisfied over a range of frequencies.
The cavity Q factor is a convenient way the power lost in a cavity.
The Q factor is defined as:

## Slide 24: Cavities and Cryomodules
RF cavities housed in cryomodules, which keep the RF cavities working in a superconducting state, without losing energy to electrical resistance

## Slide 25: Outline
  Types of Particle Accelerators
  Accelerator Characteristics
  RF Cavity
  Superconductivity and Superfluidity
  Examples of the Particle Accelerators:
    The European Spallation Source (SRF cavities R&D)
    The LHC (low-beta magnets environment and Controls)
    The Tevatron (accelerator complex and technologies)

## Slide 26: Superconductivity and Superfluidity
Superconductivity became a key-technology for particle accelerator. Superconductivity allows :
  To operate high-field, high current density magnet operating above the saturation of iron,
  To build high-field, low-loss RF Cavities (low wall resistance)
  Reducing overall electrical consumption of the machines

## Slide 27: Superconductivity and Superfluidity

## Slide 28: Superconducting Magnets
In a superconducting magnet, the field is given by the current distribution in the windings (Biot & Savart’s law).
When present, the iron only acts as a flux return yoke

## Slide 29: Superfluidity of Helium
Helium II - Quantum fluid
Exceptional heat transfer
Specific heat transition at 2.17 K - Tl
Enormous heat conductivity at moderate flux (3,000 x OFHC copper at 1.9K)
> Thermo-mechanical - fountain effect
LHC operation
Tevatron operation
Helium (25 %) is the most common element in Universe after Hydrogen (73 %)
Two isotopes: 3He (fermion) & 4He (boson)
Notes: Few DT along the cell
very large specific heat (typically 105 times that of the conductor per unit mass, 2 × 103 times per unit volume), combined with the enormous heat conductivity at moderate flux (3000 times that of cryogenic-grade OFHC copper, peaking at
1.9 K)
The amount of energy needed to raise the temperature of a kilogram of helium by one degree (the specific heat, Cp) shown in Figure 6 is very large for both He I and Helium II.
As an example, Copper has a Cp of 0.03 J/kg - K at 2 K, while the Cp of Al at the same temperature is approximately 0.11 J/kg - K. The specific heat of Helium II just below Tl at 1 bar is of the order of 12,400 J/kg - K, dropping to approximately 2,900 J/kg - K in the normal state.

## Slide 30: Superfluidity of Helium The two-fluid model for helium II
Normal-fluid fraction:
excited states atom (phonons & rotons)
 like a conventional viscous fluid
finite density , rn
finite viscosity, 
entropy, s
Macroscopic quantum physic system simplification
The two-fluid model is only a phenomenological model !
Superfluid fraction:
- atoms that have undergone BEC
 like an ideal inviscid liquid resulting in the absence of classical turbulence.
finite density, rs
NO viscosity
carry NO entropy
irrotational behavior for an inviscid fluid
but vortices can be generated in the superfluid component
Quantized vortices
Counter-flow turbulence

## Slide 31: Thermal conductivity of helium II
High flux regime
dT/dx ~ q3
Low flux regime dT/dx ~ q
Heat transport regimes at 1.9 K
Laminar
Turbulent
Mutual- friction regime
No bulk flow
Heat flux
Counter-flow mechanics
e.g. d > 1mm, q > 10mW/cm2
In mutual friction regime:
AGM Gorter-Mellink mutual friction parameter
Thermal resistivity function
Internal convection of the super-fluid and normal-fluid components
Notes: D1~ 10 micron for 10-4K/m
Cu (@3.6 K) = 1.2 W/cm2 ; He I (@3.6 K) = 3.6 e-6 W/cm2
Cu (@1.9 K) = 1.6 W/cm2 ; He II (@ 1.9 K) = 24 W/cm2
Heater changes super fluid
into normal. More super
flows through plug
increasing pressure in
container, and fluid squirts
out top in a fountain

## Slide 32: Outline
  Types of Particle Accelerators
  Accelerator Characteristics
  RF Cavity
  Superconductivity and Superfluidity
  Examples of the Particle Accelerators:
    The European Spallation Source (SRF cavities R&D)
    The LHC (low-beta magnets environment and Controls)
    The Tevatron (accelerator complex and technologies)

## Slide 33: The European Spallation Source

## Slide 34: The European Spallation Source
Japan 2008:
JPARC (<1MW)
Europe 2019: The European Spallation Source (<5 MW)
USA 2006:
SNS (<1.4 MW)
Will bring new insights to the grand challenges of science and innovation
Collaborative project: more than 17 countries
2014: Start of construction phase of the world's most powerful linear proton accelerator
2019: Provide the world's most advanced tools for studying materials with neutrons
(~ 450 employees; > 2500 users / year)
Lund, Sweden
Philosophie de “Pré-vert”: Greenfield
1 GeV, 26 mA in linac, 627 ns long pulse, 60 Hz
2.86 ms long pulse !
Notes: Promote science, competitivity and complementarity of Life Science as operated in the USA and Japan.
USERS
Build capacity and partnership (in Europe) around science and innovation
Green-field – new investment – pre-vert
Complementarity of scientific tool: LS and NS
Each builds on the previous and prepares for the next
regional and European impact
Intensity frontiers
Beam-to-target : 2006—2019

## Slide 35
High time average and peak flux
Berkeley 37-inch cyclotron
350 mCi Ra-Be source
Chadwick
1930
1970
1980
1990
2000
2010
2020
105
1010
1015
1020
1
ISIS
Particle driven pulsed
ZING-P
ZING-P’
KENS
WNR
IPNS
ILL
X-10
CP-2
Fission reactors
HFBR
HFIR
NRU
MTR
NRX
CP-1
1940
1950
1960
Effective thermal neutron flux n/cm2-s
(Updated from Neutron Scattering, K. Skold and D. L. Price, eds., Academic Press, 1986)
FRM-II
SINQ
SNS
J-PARC
LANSCE
OPAL
PIK
2030
CARR
CSNS
Dhruva
IBR-II
NIST
RSG
LVR
JRR-3
Particle steady state
Pulsed reactor
HANARO
HIFAR
SAFARI-1
SALAM
ETERR-2
MARIA
HOR
JEEP II
ORPHEE
Reactor Sources
Spallation Sources
ESS

## Slide 36
Fission and Spallation
Spallation is a non-elastic nuclear interaction induced by a high-energy particle producing numerous secondary particles

## Slide 37: Target Station includes systems that address nuclear hazards
~ 130 m long
Accelerator – Target interface
Target monolith, incl. Moderator & Reflector Systems, and Target Systems
Fluid Systems
High bay
Remote Handling Systems
Remote Handling Systems including hot cells and associated equipment for maintenance and storage of irradiated components
Target Safety System including credited controls to protect public and environment from radioactive hazard
Fluid Systems including He and H2O coolant loops, ventilation, filtering, etc.
Spain was one of the first countries to send a Letter of Intent committing to the construction of the European Spallation Source, and a close collaboration has followed. In November 2014, ESS-Bilbao was chosen as the in-kind partner for the ESS target system

## Slide 38: Target station converts protons to “slow” neutrons
Functions:
Convert protons to usable neutrons
Heat removal
Confinement and shielding
Unique features:
  Rotating target
  He-cooled W target
  High brightness moderators
Diameter ~ 11 m; Height ~ 8 m
Mass ~ 7000 tonnes (mainly steel)
The tungsten wheel concept:
The target wheel will measure 2.5 meters in diameter, is estimated to weight 4 tonnes, and is divided into 36 radial sectors
Target Wheel
Moderator & reflector plugs
Monolith Vessel
Target Monolith
Proton Beam Window
Notes: Explan spallation:
Moderation
Why choice of Solid tungsten
Low radioactive inventory

## Slide 39: ESS long pulse potential
Possibilities of pulse shaping
time (ms)
Brightness (n/cm2/s/ster/Å)
7
5
x1014
ISIS TS1
128 kW
ISIS TS2
32 kW
SNS
1.4 MW
JPARC
300 kW
ILL 57 MW
ESS 5 MW
2015 design
thermal moderator
0
1
2
3
3
4
1
2
6
λ=1.5 Å
ESS 5 MW
2013 design (TDR)
4
8

## Slide 40: Accelerator Technical performances
Design Drivers:
High Average Beam Power
5 MW
High Peak Beam Power
125 MW
High Availability
> 95%
Key parameters:
    -2.86 ms pulses
    -2 GeV
    -62.5 mA peak
    -14 Hz
    -Protons (H+)
    -Low losses
    -Minimize energy use
    -Flexible design for mitigation & future upgrades
Spokes
Medium β
High β
DTL
MEBT
RFQ
LEBT
Source
HEBT & Contingency
Target
2.4 m
4.6 m
3.8 m
39 m
56 m
77 m
179 m
75 keV
3.6 MeV
90 MeV
216 MeV
571 MeV
2000 MeV
352.21 MHz
704.42 MHz
The scope contingency for the accelerator project consists of the RF sources and installation costs (after 2019) for the high beta-part of the linac
The fully equipped cryomodule for the high-beta linac are IK contributions and are not part of the scope contingency. The infrastructures needed for the construction of these are only available during ESS construction.
Spoke
M-b
H-b
NC FE

## Slide 41: Linac redesign to meet ESS cost objective
Chart: Beam Beta
Beam power (MW) | 5
Beam current (mA) | 62.5
Linac energy (GeV) | 2
Beam pulse length (ms) | 2.86
Repetition rate (Hz) | 14
 | Num. of CMs | Num. of cavities
Spoke | 13 | 26
Medium b (6-cell) | 9 | 36
High b (5-cell) | 21 | 84
WP4
WP5
[SRF2013 – “The ESS Superconducting Linear Accelerator”, C. Darve, M. Eshraqi, M. Lindroos, D. McGinnis, S. Molloy, P. Bosland and S. Bousson]
Spokes
Medium β
High β
DTL
MEBT
RFQ
LEBT
Source
HEBT & Contingency
Target
2.4 m
4.6 m
3.8 m
39 m
56 m
77 m
179 m
75 keV
3.6 MeV
90 MeV
216 MeV
571 MeV
2000 MeV
352.21 MHz
704.42 MHz
Notes: 400 m/ 600 m tunnel = SRF

## Slide 42: Front End Section
Ion Source
  Microwave Discharge Ion Source
  Proton peak current ~75 mA
  Total drain current ~100 mA
  Output Energy 75 keV
  Provided by INFN-LNS, Catania
  Experience from TRIPS ion sources
LEBT (Low Energy Beam Transport)
  Dual solenoid layout
  Functions:
    Transport and match input the RFQ
    Clean the beam pulse from the rise/fall time of the source with a slow chopper
    Provide different level of beam current with an iris
  Provided by INFN-LNS, Catania
  Design close to the IFMIF LEBT
IFMIF source and LEBT at CEA-Saclay
Extraction system of the ESS ion source
(Courtesy L. Celona)
Prototype proton source operational, and under further development, in Catania. Output energy 75 keV.

## Slide 43: Front End Section
RFQ
  352 MHz 4-vanes RFQ
  5 segments of ~90 cm
  Functions:
    Accelerates
    Bunches the pulse in a train of bunches
    Focuses in the 3 planes
    Provide different level of beam current with an iris
  Foreseen transmission > 90 % for 70 mA input beam
  Provided by CEA-Saclay
MEBT
  Fully instrumented MEBT ~ 4.5 m
  Functions:
    Transport and match into the DTL
    Characterize the beam
    Fast chopping of the beam with rise/fall time ~ 10 ns
  Provided by ESS-Bilbao
MEBT layout (Courtesy B. Cheymol)
Design exists for ESS RFQ similar to 5 m long IPHI RFQ at Saclay. Energy 75 keV->3.6 MeV.
Design work at ESS Bilbao for MEBT with instrumentation, chopping and collimation.

## Slide 44: Front End Section
DTL (Drift Tube Linac)
  352 MHz
  5 tanks
  Length ~ 40 m
  Output energy: ~90 MeV
  Provided by INFN-LNL, Legnaro
Six klystrons
  352 MHz
  with a maximum saturated power of 2.8 MW
  and a duty factor of 4% are required for the Front End
DTL 3D view (Courtesy P. Mereu)
DTL design work at ESS and in Legnaro, 3.6 ->90 MeV.
Picture from CERN Linac4 DTL.

## Slide 45: Super-Conducting Linac
4 Elliptical Cavities per Cryomodule
2 Spoke Cavities per Cryomodule
Power coupler
Cold tuning System
Ti. Helium tank
Segmented SRF linac with RT focusing elements
Notes: 2 spoke – 3 gap
4 cavity – SNS like
Segmented SRF linac with RT focusing elements

## Slide 46: Spoke cavity string and cryomodule package
Diameter
1350 mm
2900 mm

## Slide 47: Cavity Cryomodule - Generic
Similar medium and high-beta cavity cryomodules
    Common design: Small length difference between medium and high-beta cavities
    Distance between power couplers
    Vacuum vessels, thermal shield, supports, alignment system.
Only minor differences:
  Length of the inter-cavity bellows, details in cryo piping, beam pipe bellows
  Tuner piezo frames
  Penetration of the antenna for Qext adjustment
Similar to SNS in size and purpose : re-use the same concepts

## Slide 48
50K Thermal shield
Lateral port
(CTS, alignment)
Tie rods (TA6V)
Positioning jacks
(3 at 120°)
Power coupler
Waveguide transition
Guide rail and wheel
Space frame
Vacuum vessel
(stainless steel - 1200 mm diam.)
Two phase He pipe
Positioning optical devices
Access traps to the tuners
He. safety valve
Cryogenic line interface
Elliptical Cryomodule Components

## Slide 49: Elliptical Cryomodule Components
Power coupler
Cold tuning System
Ti Helium tank
5-cell elliptical cavity
Space frame
6600 mm
Diameter
1200 mm

## Slide 50: Cryomodule Interfaces
Cryogenic distridution
Most AD internal Work Packages (beam optics, RF, cryo, vacuum, test stands, electrical, cooling, installation)
External WPs cryomodule, cavity and designers and potential In-Kind collaborators
Control command (Control Box, PLC, LLRF, MPS, EPICS)
Data-logging ICS teams
ESS ES&H
Conventional Facility
ESS system engineer, QA
Survey experts
Transport
Cryogenic distribution
Radio-Frequency
Beam Vacuum
Beam Diagnostic
Beam Optics
Control system
Previous Linac version for comparison 

## Slide 51: Cold Tuning System
2 piezo stacks
Stepper motor and planetary gearbox (1/100e) at cold and in vacuum
Slow tuner
Main purpose : Compensation of large frequency shifts with a low speed
Actuator used : Stepper motor
Fast tuner
Main purpose : Compensation of small frequency shifts with a high speed
Actuator used : Piezoelectric actuators
Type V ; 5-cell prototype
+/- 3 mm range on cavity
Elliptical CTS
Spoke CTS
&

## Slide 52: Lorentz De-tuning
Because of the enormous gradients in superconducting cavities,
  the radiation pressure deforms the cavities
We expect over 400 Hz of detuning in the ESS cavities.
  Unloaded cavity bandwidth = 0.07 Hz
  Loaded cavity bandwidth = 1 kHz
The mechanical time constant of the cavities is about 1 ms compared to the pulse length of 3 ms
  Static pre-detuning as done in SNS will not be sufficient
  Dynamic de-tuning compensation using piezo-electric tuners is a must!
  Or else pay for the extra RF power required

## Slide 53: Fundamental Power Coupler
Antenna
Vacuum
Outer conductor
(LHe-cooled)
Doorknob
Inner conductor
(water-cooled)
Al2O3
ceramic disc
RF input
Short circuit
WR2300
Elliptical:
1.1 MW
Spoke:
335 kW

## Slide 54: ESS Requirements and RF Parameters
 | Medium | High
Geometrical beta | 0.67 | 0.86
Frequency (MHz) | 704.42 | 
Number of cells | 6 | 5
Operating temperature (K) | 2 | 
Epk max (MV/m) | 45 | 45
Nominal Accelerating gradient (MV/m) | 16.7 | 19.9
Q0 at nominal gradient | > 5e9 | 
Qext | 7.5 105 | 7.6 105
Iris diameter (mm) | 94 | 120
Cell to cell coupling k (%) | 1.22 | 1.8
p,5p/6 (or 4p/5) mode sep. (MHz) | 0.54 | 1.2
Epk/Eacc | 2.36 | 2.2
Bpk/Eacc (mT/(MV/m)) | 4.79 | 4.3
Maximum. r/Q (W) | 394 | 477
Optimum b | 0.705 | 0.92
G (W) | 196.63 | 241
RF peak power (kW) | 1100 | 
Elliptical cavities
Spoke cavities
Frequency (MHz) | 352,2
Optimum beta | 0,50
Operating temperature (K) | 2
Nominal Accelerating gradient (MV/m) | 9
Lacc (bopt.x nb gaps x l/2) (m) | 0,639
Bpk (mT) | 79 (max)
Epk (MV/m) | 39 (max)
Bpk/Eacc (mT/MV/m) | <8,75
Epk/Eacc | <4,38
Beam tube diameter (mm) | 50
RF peak power (kW) | 335
G (W) | 130
Max R/Q (W) | 427
Qext | 2,85 105
Q0 at nominal gardient | 1,5 109

## Slide 55: SRF Cavities Development
Ti He vessel
Hydroformed Ti bellows
(+/- 3mm range)
Power coupler port
 Stiffeners on the Spoke bars
(vacuum pressure)
Stiffeners (LFD compensation)
Elliptical cavities
Spoke cavity
High beta:
5 cells – beta=0.86
Length 1316,91mm
Medium beta:
6 cells – beta=0.67
Length 1259,40mm
NbTi flange
(w/bore holes for alignment & assembly tool)
+Al hex. gaskets
418 mm
550 mm
994 mm
 No HOM power couplers

## Slide 56: Medium-β Elliptical Cavities
KL reduction using compensation rings for medium and high-beta
Nominal wall thickness [mm] | 3.6
Cavity stiffness Kcav [kN/mm] | 2.59
Tuning sensitivity Df/Dz [kHz/mm] | 197
KL with fixed ends [Hz/(MV/m)²] | -0.36
KL with free ends [Hz/(MV/m)²] | -8.9
Pressure sensitivity KP [Hz/mbar] (fixed ends) | 4.85
Kext (tank + tuner)≈30 kN/mm
KL≈-1 Hz/(MV/m)2
Df ≈ 325 Hz @ 18 MV/m (1/3 of cavity bandwidth )
Lorentz detuning
RF/mechanical design

## Slide 57
Cavity Prototypes
The 3 spoke cavities prototypes:
named: Romea, Giulietta and Germaine
View of the cavity inside: the spoke bars
Romea
Giulietta
Germaine

## Slide 58: Spoke cavity Performances (Jan-June 2015)
Eacc_max=15.3 MV/m achieved with “Romea”
Several MP barriers but easily processed.
Qo > 1.6 1010
Strong FE at max gradient
Limitation is the cooling capacity (unstable conditions, cavity in vertical position)
Spoke cavity exceeding ESS requirements in vertical test on both Eacc and Qo

## Slide 60: Elliptical Cavity Preparation
Vertical Electropolishing system@ CEA
High beta cavity fabrication (Zanon and RI)
    Study of the tooling in progress @ CEA
    Example of the tooling for the assembling of the coupler on the cavity in clean room

## Slide 61: High b Elliptical Cavity Activities in Clean Room

## Slide 62: Magnetic shield
Limit contribution of the trapped flux to the surface resistance to 4 nW
Limit the external static field to Bext = 14 mG.
→ Required shielding efficiency equal to 35.
Achievable with 1.5 mm,
µr =20000 shielding material
Courtesy of J. Plouin/ CEA

## Slide 63
Cavity fabrication
Cryomodule components fabrication
Cavity string assembling in clean room
Validation test of the cavity in vertical cryostat
Validation test of the cryomodule
Cryomodule on beam line
Power coupler fabrication
Coupler RF processing
Cryomodule assembling
Tools fabrication
Chemical treatment
High pressure rinsing
In clean room (ISO5 or ISO4)
Assembling in clean room
Transport
Qualified cavity storage
Cryomodule reception and storage
Cryomodule storage
Processed couplers storage
Courtesy of Pierre Bosland CEA/IRFU
Space frame
Beam valves and extremity flange
TA6V rods in X pattern to keep the beam axis at the same position during cool down
Magnetic shield
Tuning system
Cryomodule life-cycle
63
Notes: QA control

## Slide 64: Elliptical Assembly Procedure
Cavity string assembly in clean room
Cold mass assembly (outside the clean room)
Thermal shield
Spaceframe
Vacuum
vessel
Design concept of the tooling: most of parts will be used for both types of elliptical cryomodules
Build on existing knowledge (SNS, XFEL)
Develop Training and “Fabrication file”
Pre-industrialization
Industrialization
Notes: Only minor differences:
  Length of the inter-cavity bellows, details in cryo piping, beam pipe bellows
  Tuner piezo frames
  Penetration of the antenna for Qext adjustment

## Slide 65: Infrastructure in Saclay
IS0 5
52,69 m2
IS0 7 27,5 m2
Water cleaning
High Pressure Rinsing HPR
    The clean room inauguration
     May 13th 2014
    Clean room for the M-ECCTD (and H-ECCTD)
    Possible IKC for the assembly by industry at Saclay (XFEL cryomodules assembly)
    Uses the current infrastructure at Saclay
    Benefits from the experience of the XFEL cryomodule assembly (ALSYOM)
Notes: Only minor differences:
  Length of the inter-cavity bellows, details in cryo piping, beam pipe bellows
  Tuner piezo frames
  Penetration of the antenna for Qext adjustment

## Slide 66: Spoke assembling in clean room/IPNO
Courtesy of D. Reynet / IPNO

## Slide 67: Process and Instrumentation
Instrumentation function
  Monitoring
  Control
  Interlock
  Alarms
Operating Modes under definition

## Slide 68: Control integration

## Slide 69: Spoke linac (352 MHz) RF System Layout
26 Double Spoke cavities
Power range 280-330 kW
Combination of two tetrodes
Other options:
Solid State Amplifiers
Large power supply (330 kVA) to supply 8 stations (16 tetrodes)

## Slide 70: Elliptical (704 MHz) RF System Layout
One cavity per klystron
4 klystrons per modulator
16 klystrons per tunnel penetration
Tunnel

## Slide 71: Elliptical (704 MHz) RF System Layout
4.5 Cells of 8 klystrons for Medium Beta
10,5 Cells of 8 klystrons (IOTs) for High Beta
WR1150 Distribution
Klystrons
Modulator
Racks and Controls

## Slide 72: Outline
  Types of Particle Accelerators
  Accelerator Characteristics
  RF Cavity
  Superconductivity and Superfluidity
  Examples of the Particle Accelerators:
    The European Spallation Source (SRF cavities R&D)
    The LHC (low-beta magnets environment and Controls)
    The Tevatron (accelerator complex and technologies)

## Slide 73: CERN and the Large Hadron Collider
Searching for the Higgs boson !
data : 20 km of CDs stacked per year

## Slide 74: Key technologies of the LHC accelerator
Superconducting magnets
  1,250 ton of NbTi superconducting materials
  7,600 km of superconducting “Rutherford” cables
  9,600 magnets (incl.1,232 dipoles, 392 quadruples)
Superfluid helium cryogenics (< 2 K) and vacuum techniques
  Pressurized and saturated superfluid helium, in two-phase flow
  Cryostats and thermal insulation
  Efficient and large capacity helium refrigerators
  Cryogen storage and mgt (120 ton of He)
Pressurized He II bath containing magnet
Two Phase He II
heat exchanger
Notes: Field reproducibility/precision ~ 10-3
Field homogeneity ~ 10-4

## Slide 75: LHC Magnets

## Slide 76: LHC Magnets
 | Inner Cable | Outer Cable
Number of strands | 28 | 36
Strand diameter | 1.065 mm | 0.825 mm
Filament diameter | 7 µm | 6 µm
Number of filaments | ~ 8900 | ~ 6520
Cable width | 15.1 mm | 15.1 mm
Mid-thickness | 1.900 mm | 1.480 mm
Keystone angle | 1.25 ° | 0.90 °
Transposition length | 115 mm | 100 mm
Ratio Cu/Sc | ≥ 1.6 | ≥ 1.9
7,600 km of cable made of 270,000 km of strand (6 earth circumferences)
 filaments : 6 times back and forth to the Sun + 150 trips to the moon

## Slide 77: The low-beta magnets at the LHC
77
 Critical system for LHC performance
American contribution to the LHC machine
IP2
IP8
+ D1
IP5
IP1
Q=Q_Arc x 10
Inner Triplet for final beam focusing/defocusing

## Slide 78: The low-beta magnets at the LHC
Air flow m/s
Escape path
Underground views : 80-120 m below ground level
One way
Tunnel restriction
Experimental Hall
Looking toward IP

## Slide 79
Interface with QRL
xx9xx
Low-beta system
xx8xx
TT8xx: Pt100, CernoxTM
PT8xx: based on passive strain gauge
EH8xx: cryo-electrical heaters
TT821
EH821
Type of instrumentation : cryo-magnets
Notes: 5 mK at 2 K

## Slide 80: Electrical feed-boxes
CV8xx: control valve
LT8xx: liquid helium level gauge
(based on superconducting wire)
*HTS leads
*Vapor cooled leads

## Slide 81: General architecture of the cryogenic system
50 m x 50 m
up to 100 m
30 m x 30 m
3’000 m

## Slide 82: 18 kW @ 4.5 K helium refrigerators
33 kW @ 50 K to 75 K
23 kW @ 4.6 K to 20 K
41 g/s liquefaction
Air Liquide
Linde
Warm compressors

## Slide 83: 2.4 kW @ 1.9 K refrigeration units
Cartridge 1st stage
Axial-centrifugal impeller
Air Liquide
IHI - Linde
Cold compressor key technology

## Slide 84: Cryogen management (helium, nitrogen)
Cryogen storage
Courtesy of Laurent Tavian

## Slide 85: Outline
  Types of Particle Accelerators
  Accelerator Characteristics
  RF Cavity
  Superconductivity and Superfluidity
  Examples of the Particle Accelerators:
    The European Spallation Source (SRF cavities R&D)
    The LHC (low-beta magnets environment and Controls)
    The Tevatron (historical accelerator complex and technologies)

## Slide 86
Unified control system for the entire complex
400 MeV Linac
8 GeV Booster Synchrotron
120 GeV Main Injector Synchrotron
1 TeV Tevatron Synchrotron
antiproton source – target/debuncher/accumulator
antiproton “Recycler” storage ring
fixed target lines
Simultaneous operation of
Tevatron proton-antiproton collider (storage ring)
Antiproton production and storage (~0.5 Hz)
120 GeV fixed target to Meson lab (~0.1 Hz)
120 GeV fixed target to NUMI/MINOS (~0.5 Hz)
8 GeV fixed target to MiniBoone (~5 Hz)
Booster RF
Cockcroft_Walton

## Slide 87
f
Fermilab Accelerator Division

## Slide 88
f
Fermilab Accelerator Division

## Slide 89
f
Fermilab Accelerator Division

## Slide 90: Tevatron magnet cross-section
+ coils made of NbTi alloy wire
+ wire size is 8 mm
+11 million wire-turns in a coil
+ 42,500 miles of wire per magnet
6.5 km of superconducting magnets operating @ 3.6 Kelvin:
+777 dipoles
+216 quads
+204 correction elements

## Slide 91: One typical cooling loop for the Tevatron

## Slide 92: Central Helium Liquefier - CHL
The Central Helium Liquefier consists of:
Four parallel reciprocating 4,000 HP helium compressors (6.8 MW total power)
Two Claude cycle cold boxes (6,400 liters/hr, peak at 9000 liters/hr)
15 helium gas storage tanks (1,500 m3, 1.7 MPa, at RT)
One Nitrogen Reliquefier (4,680 liters/hr)
600,000 liters of LN2 storage
Purification system

## Slide 93: Summary
Accelerator Components requires:
State-of-the-art material performance
Challenging design
Unique technologies
Lots of materials available at:
US-Particle Accelerator School, http://uspas.fnal.gov/materials/materials-table.shtml
CERN Accelerator School http://cas.web.cern.ch/cas
Joint Universities Accelerator School
The domain of Particle Accelerator needs YOU !!!