## Slide 1
Sverker Werin
MAX IV laboratory, Lund university
Production of synchrotron radiation

## Slide 2
Light to investigate the world
Building
Human
Fly
Cell
Virus
DNA
Atom
Atom nucleus
1 nm
1 um
1 mm
1 m
1 km
Radio waves
Microwaves
IR light
Visible light
UV light
X-ray
Wavelength

## Slide 3: First discovery of SR 1947
"On April 24, Langmuir and I were running the machine … we asked the technician to observe with a mirror around the protective concrete wall. ” (Herb Pollock)
General Electric Research Laboratory, Schenectady, NY, US

## Slide 4
Light sources – electric field
www.nature.com

## Slide 5
Light sources – electric field
www.nature.com

Near field
Far field

## Slide 6
No questions?

## Slide 7
Dipole radiation (antenna)

## Slide 8
Dipole radiation (relativistic)

## Slide 9
Dipole radiation (relativistic)

## Slide 10
1/g=1/energy
Dipole radiation (relativistic)

## Slide 11: What is the wavelength of this signal?
30
60
15
45
Quick duty
Please talk!

## Slide 12
~1/energy
Radiation
time

## Slide 13
Light and waves
Wavelenght=> colour
Light wave

## Slide 14
Fouriertransform
Wavelength
Energy
X
Which colour/wavelength?

## Slide 15
Filter
?
Filter the light

## Slide 16
Filter the light
When did the light get colour?

## Slide 17
Heisenberg’s uncertainty relation
Fourier transform
… and in ”fancy” language

## Slide 18
http://www.shintakelab.com/en/enEducationalSoft.htm
Radiation 2D by T. Shintake

## Slide 19
Bending magnet radiation
Energy
Wavelength
In the synchrotron

## Slide 20
Example (MAX II)
Energy 1.5 MeV (g3000)
R 3.5 m
lcritical 0.54 nm
Ecritical 2.3 KeV
Bending magnet
Energy lost by one e- over one turn

## Slide 21
Liénard-Weichert fields
near
far

## Slide 22
No questions?

## Slide 23: Polarisation
E field in direction of acceleration  polarisation
Changes with observation plane

## Slide 24: Time structure
RF system
500 MHz
100 MHz
Storage ring 100-300 ps
MAX IV SPF 100 fs
Slicing 50 fs
Free Electron Laser 20 fs
Multi bunch Single bunch Uneven fill patterns

## Slide 25
By: Goscinny.
Idea: PSI.
10 ns, plenty of time!

## Slide 26: Flux and brilliance
Peak brilliance
During the peak of a bunch
Average brilliance
Forever or during a macro pulse from the accelerator
What counts
To compare
E0
0.1%BW
Light
Electrons

## Slide 27: Think of a gaussian light beam…
w0
w(z)
f
E-field or intensity?
Spherical or cartesian?
(factors of 2 and )
Fundamental feature of light! (=nothing to do about it ;-)
Define a quality factor:
Today’s challenge for development

## Slide 28: …and then of an electron beam.
x
x’
Emittance
The goal for the accelerator designer is to make the electron beam ”smaller” than the light diffraction:
But, increasingly difficult for shorter and shorter wavelengths.
Chart: Diffraction limit
| 0.99471839432434583 | 0.49735919716217292 | 0.24867959858108646 | 0.12433979929054323 | 6.2169899645271615E-2 | 3.1084949822635807E-2 | 1.5542474911317904E-2 | 7.7712374556589518E-3 | 3.8856187278294759E-3 | 1.942809363914738E-3
Photon energy (keV) | 0.0124 | 0.0248 | 0.0496 | 0.0992 | 0.1984 | 0.3968 | 0.7936 | 1.5872 | 3.1744 | 6.3488 | 12.6976 | 25.3952 | 50.7904 | 101.5808

## Slide 29: Flux and brilliance
Peak brilliance
During the peak of a bunch
Average brilliance
Forever or during a macro pulse from the accelerator
What counts
To compare
E0
0.1%BW
Light
Electrons

## Slide 30
In the synchrotron (revisited)

## Slide 31
In the synchrotron (revisited)
Insertion devices Undulator/ Wiggler
Periodic magnetic structures

## Slide 32: Insertion devices
Superconducting multi pole wiggler in MAX II
Undulator in MAX II

## Slide 33: A wiggler
Shorter wavelength / higher photon energy
3 or many strong magnets
Flux is the sum (no interference)

## Slide 34
K = undulator parameter, typically between 1 and 4
lundulator = period length for magnets, typically 2-3 cm
Many weak magnets
Interference peaks
Harmonics
Helical polarisation exists
Undulator

## Slide 35
Interference in the undulator

## Slide 36
Interference in the undulator

## Slide 37
1 st harmonic
3 rd harmonic
Interference in the undulator

## Slide 38
K = undulator parameter, typically between 1 and 4
lundulator = period length for magnets, typically 2-3 cm
Many weak magnets
Interference peaks
Harmonics
Helical polarisation exists
Undulator

## Slide 39: Linewidth, energy and angular spread

## Slide 40
MAX II SC MPW (Super Conducting Multi Pole Wiggler)
Period = 0.06 m
K = 20
B = 3.5 T
R = 1.4 m
critical = 0.22 nm ( 5.6 KeV)
undulator = 670 nm (1.8 eV)
Why wiggler, why undulator?

## Slide 41
MAX II undulator
Period = 0.06 m
K = 4
B = 0.7 T
R = 7.2 m
critical = 1.1 nm ( 1.1 KeV)
undulator = 30 nm (41 eV)
Why wiggler, why undulator? (p 2)

## Slide 42: Software
http://ftp.esrf.eu/pub/scisoft/xop2.3/
http://radiant.harima.riken.go.jp/spectra/

## Slide 43
A beam line

## Slide 44
Inuti ringbyggnaden

## Slide 45
Photo electrons

## Slide 46
Photo electrons

## Slide 47
Absorption
?

## Slide 48
Scattering

## Slide 49
Geometry and chemicals bonds with the help of photon spectroscopy
Clean rhodium crystal surface
With a small amount of oxygen
Rhodium

## Slide 50: The Ribosome structure and function
2009 years Nobelprice in Chemistry
Venkatraman Ramakrishnan, Thomas A. Steitz och Ada E. Yonath

## Slide 51: Solar cells and batteries
J. Schnadt et al.
Bonding of dye molecules
Probing charge transfer times
< 2.5 fs
Grätzel type solar cell
Rechargeable Li batteries

## Slide 52
Archimedes’ original text
Archimedes used ink which contained large amount of iron.
By using X-rays at different wavelengths (close to the Fe Ka edge) one could see where the iron was.
Forgery – and new discoveries…
STANFORD SCIENTISTS USE X-RAYS TO SEE 2,000-YEAR-OLD DOCUMENT

## Slide 53: ... the greatest invention since sliced bread!!!
Petrified embryo of animals

## Slide 55: Let us start dreaming…
What happens if we combine them?
X-ray image
Hologram, 3D image
Movie of moving objects
http://eartholographics.blogspot.se
http://www.netanimations.net
http://www.mnh.si.edu
http://dev.nsta.org
See atoms and molecules

## Slide 56
Synchrotron light
Incoherent
”Long” pulses (100 ps)
High average power
Ring
Electrons
Undulators
Free electron laser
Coherent
Short pulses (10 fs)
High peak power (GW)
Linear accelerator
Electrons
Undulators

## Slide 57: In principle it is fairly simple!
Make the electron beam slightly better:
Reduce the emittance 50 times
Reduce the pulse lengdth 1000 times
Accelerate a little more
Fix a little higher stability and filter
…
25 - 100 m

## Slide 58
Still no questions?

## Slide 59
E= cos(wt+f1) + cos(wt+f2) + ….
I=E2 = cos2(wt+f1) + cos2(wt+f2) + ….
…+ cos(wt+f1)cos(wt+f2) +… =
= Nelectrons cos2(wt+f1)
Nelectrons = 108
Emission of light and coherence
A bunch of electrons

## Slide 60
E= cos(wt+f1) + cos(wt+f1+2p) + ….
I=E2 = cos2(wt+f1) + cos2(wt+f1+2p) + ….
…+ cos(wt+f1)cos(wt+f1+2p) +… =
= N2magnets cos2(wt+f1)
Nmagnets = 100
Emission of light and coherence
A single electron in an undulator

## Slide 61
E= cos(wt+f1) + cos(wt+f1+2p) + ….
I=E2 = cos2(wt+f1) + cos2(wt+f1+2p) + ….
…+ cos(wt+f1)cos(wt+f1+2p) +… =
= N2magnets Nelectrons cos2(wt+f1)
Nmagnets, undulator = 100
Nelectrons = 108
MAX II
MAX IV
Emission of light and coherence
A bunch of electrons in an undulator

## Slide 62
E= cos(wt+f1) + cos(wt+f1+2p) + ….
I=E2 = cos2(wt+f1) + cos2(wt+f1+2p) + ….
…+ cos(wt+f1)cos(wt+f1+2p) +… =
= N2magnets N2electrons cos2(wt+f1)
Nmagnets, undulator = 100
Nelectrons = 108
Micro bunching
Emission of light and coherence
A micro bunched beam in an undulator
Also valid for harmonics!
It can’t be true!
Chart: Brilliance
| 1892 | 1962 | 2000 | 2015
 | 20000000 | 1000000000000
 | 1000000000000 | 1e+24
 | 1e+24 | 3e+34
x1020

## Slide 63: In principle it is fairly simple!
Make the electron beam slightly better:
Reduce the emittanse 50 times
Reduce the pulse lengdth 1000 times
Accelerate a little more
Fix a little higher stability and filter
…
25 - 100 m

## Slide 64: How to make the bunching?
Make an energy modulation
Transform it into a density modulation
Energy modulation
Density modulation
Coherent radiation in harmonics
10 um
1 Å
1 cm
1 km

## Slide 65: Light interacting with an electron beam
Undulator

## Slide 66
Energy exchange
E-field
vx
lg
Some e- gain energy
Some e- loose energy
S = 0
e-

## Slide 67
Bunching
lg
Detour & lower v
Shortcut & higher v
e-
-DE
+DE
Bunched e- with distance of light wavelength

## Slide 68
Saturation
vx
lg
Overbunching

## Slide 69
Amplification
E-field
vx
lg
All e- loose energy
E-field gains energy
S ≠ 0
Phase shift (Frequency slightly off resonance)

## Slide 70
SASE (Self Amplified Stimulated Emission)
From noice
No mirrors ( X-rays)
Tunable
”Spiky” (t and l)
L
P

## Slide 71: Noise in SASE

## Slide 72
Resonator FEL
IR 5-250 mm
UV  200 nm
Tunable: magnet / e- energy
Mirrors limit
Storage ring: high rep. Rate, ”stable”
Linac: high peak power, ”unstable”

## Slide 73
SEEDING
Remove instabilities
CHG with gain HGHG
laser
Monochromator

## Slide 74: LCLS, Stanford
1.5 Å
SASE

## Slide 75
Thanks for listening!