## Slide 1
Single-crystal orientation terminal for NTDS
China Spallation Neutron Source
Neutron Technology Development Team
Presenter: Yuhua Ma
mayuhuaw2016@foxmail.com

## Slide 2
Outline
Research Background
Summary and Outlook
Physical Design

## Slide 3
Research Background
(1) High-energy inelastic spectrometer: 2026
(2) Polarized inelastic spectrometer: 2029
(3) Cold neutron direct geometric inelastic spectrometer: 2029
(4) Elastic diffuse neutron spectrometer: 2029
(5) Single-crystal neutron diffraction spectrometer: 2029
Testing conditions met: First half of 2026
Reciprocal vector and direction
Check single crystal quality
Single crystal directional cutting
Single crystal property/scattering test under special environment
Future developments (Laue lines, single-crystal stress, etc.)
1
Main functions
2
3
4
5
Spectrometer Requirements
Existing design meets
Future Expansion

## Slide 4
Physical Design
Physical Design
Device Overview
single crystal orientation neutron imaging device
Beamline Characteristics:
Cold neutron energy region(1~100meV)
Adjustable energy spectrum
Low divergence(FWHM=±0.405°)
Time-of-flight (TOF) type
Key Components：
Decoupled and Poisoned Hydrogen Moderator
Chopper assembly
Bent guide and straight guide
Beam spot size control
Detection System
The device is located at Beam Line 8A of the CSNS.
Terminal 1
Single-crystal orientation

## Slide 5
Wavelength Range | 1.5~6.5Å
Orientation Accuracy | ＜0.5°
Detector | Coverage angle: 20°~60°; Spatial resolution: < 200 μm
Design Specifications
Scattering geometry
Overall Physical Design
Physical Design
Physical Design
Device Overview
Detection System
Mode | Diffraction Pattern | Beam Spot | Detector | Q Range | Count | Summary
Back scattering | Hyperbolas or straight lines, similar to X-rays | Not adjustable | Central hole required, complex structure | High | Low | Advantages: Simple analysis, high resolution; Disadvantages: Increased cost due to detector hole; beam spot size limited
Forward scattering | Ellipses or parabolas, different from X-rays | 0.1~25 mm | Simple structure | Low | High | Advantages: Simple detector structure, adjustable beam spot; Disadvantages: Significant sample absorption
Incident mode selection forward scattering geometry

## Slide 6
Physical Design
Continuous wavelength beam irradiation
Adjustable beam spot size
Adjustable diffraction angle coverage
L/D: 0~500
Realize Laue diffraction and neutron imaging simultaneously
Scintillator screen CCD-based neutron imaging detection
Physical Design
Physical Design
Device Overview
Detection System

## Slide 7
Experimental Procedure
Physical Design
Physical Design
Device Overview
Detection System
Experiment Switching and Preparation
Measurement of initial diffraction
Electric Orientation
Manual Orientation
Experiment ended
Beam Shutter close
Check equipment status, set chopper, slit, etc.
Adjust sample holder position for rough positioning.
Initiating the experiment;
Laue diffraction
Calculate the diffraction center, adjust the sample stage, and record the rotation direction and angle.
Return the sample stage to original position, manually adjust the sample holder, and repeat the adjustment until the center of the diffraction spot is found when the sample stage is in its initial position.
Remove the sample holder (containing the sample).
Test complete.
Beam Shutter open
Beam Shutter open/close
Beam Shutter close

## Slide 8
Overall Design
Detection System
Key Specifications:
FOV: 22cm × 22cm
Spatial Resolution: < 200um
380mm
311mm
614mm
Shielding and Light Avoidance
Boron-aluminum alloy、 Lead
Neutron and gamma shielding
Camera sealing ring
Light avoidance
Darkbox sealing plate step design
Physical Design
Physical Design
Device Overview
Detection System

## Slide 9
Neutron Scintillator Screen
6LiF/ZnS(Cu)—high light output (~10000 photons/n), good uniformity, stable performance; size and spatial resolution meet design requirements
Main parameters: 220 mm×220 mm, thickness 100 μm, ⁶LiF/ZnS (1:2), emission wavelength 530 nm (green light)
Scintillator
Substrate
Incident
nutron
Detection surface
Flashing fluorescence
Geant4 simulation:
screen thickness 100 μm
beam spot size σ = 54 μm
CCD Camera
Camera Model | Pixel Size | Readout Noise | Dark Current Noise | Readout Rate | ADC bit | Quantum Efficiency@530nm
PI SOPHIA 2048B | 2048x2048x15μm | 3.5 e-@200kHz | 0.00025 e-/p/s | 0.9 fps | 16 | >90%
Physical Design
Physical Design
Device Overview
Detection System

## Slide 10
Outlook: Facility Planning and Scientific Application
2
Scientific objective
A scheme for measuring the orientation of single crystals using Laue diffraction experiments was proposed, and the complete physical design of the neutron detector was completed.
It is expected to be completed by the end of 2026. Upon completion, it will enable the measurement of the microstructure of single crystals, support the development of other spectrometers, and provide a key means to reveal the mechanisms of matter evolution.
Dedicated to the research of single-crystal orientation and neutron imaging methodologies and experimental techniques, this research aims to achieve the correlation measurement of material microstructure and macroscopic morphology, providing a research platform for revealing the service and evolution mechanisms of materials under extreme conditions.
1
Implementation scheme design
3
Construction Planning
Laue diffraction spectrum indexing and crystal rotation calibration;
Development of NTDS single-crystal orientation data processing software;
Development of automated experimental techniques, including automatic crystal rotation and automatic measurement of diffraction spots.

## Slide 11
THANKS
Please offer your comments and corrections!
Welcome to apply for using beams and for cooperation!