## Slide 1: Multiple time sampling for Monte Carlo ray-tracing instrument simulations
Mads Bertelsen, Peter Willendrup
ICANS 2026
PRESENTED BY Mads Bertelsen

## Slide 2: Instrument simulations
  Can always be improved
    Add capabilities
    User experience
    Increase computational speed
Simulation team @ DMSC
Peter Willendrup
Mads Bertelsen
Thomas Kittelmann
Torben
Nielsen
McStas
Supported – continuously developed for 28 years
Modular – build instrument from large component library
Flexible – edit or create components locally
Community driven – components & instruments contributed
Fast – a laptop is typically sufficient

## Slide 3: McStas optimization
  We are often asked: “Can we simulate this in real time?”
  Real source intensity
    Single 2 MW ESS pulse: ~1010 thermalized neutrons entering the guide
    Instruments with flux on sample ~1010 n/s/cm2
  McStas speed
    ESS instrument simulation on laptop: ~2 105 rays per second
    Just need 105 laptops?
Monte Carlo performance
We need to improve! Today we present a new optimization trick

## Slide 4: McStas optimization
  Limiting phase-space
  Focusing
  Weight – Reflection / Absorption
  Weight – Sampling interesting events
Performance tricks

## Slide 5: McStas optimization
  Limiting phase-space
  Focusing
  Weight – Reflection / Absorption
  Weight – Sampling interesting events
Performance tricks
Only start with these wavelengths

## Slide 6: McStas optimization
  Limiting phase-space
  Focusing
  Weight – Reflection / Absorption
  Weight – Sampling interesting events
Performance tricks

## Slide 7: McStas optimization
  Limiting phase-space
  Focusing
  Weight – Reflection / Absorption
  Weight – Sampling interesting events
Performance tricks
Reduce ray weight p instead of removing the ray

## Slide 8: McStas optimization
  Limiting phase-space
  Focusing
  Weight – Reflection / Absorption
  Weight – Sampling interesting events
Performance tricks
Sample
Detector
Reality – Low scattering probability

## Slide 9: McStas optimization
  Limiting phase-space
  Focusing
  Weight – Reflection / Absorption
  Weight – Sampling interesting events
Performance tricks
Sample
Detector
Reality – Low scattering probability
Simulation – Modified scattering probability
Actual intensities recovered with weight transformation

## Slide 10: McStas optimization
  Limiting phase-space
  Focusing
  Weight – Reflection / Absorption
  Weight – Sampling interesting events
Performance tricks
Even with these tricks, choppers are a problem

## Slide 11: McStas optimization
  Rays that do not hit a chopper opening are discarded
  Wasted compute
Performance tricks

## Slide 12: McStas optimization
ODIN as test case
  10 choppers
  Several chopper operating modes
  3/6 frame Wavelength Frame Multiplication (WFM )
  Variable distance between WFM choppers

## Slide 13: McStas optimization
Current performance on ODIN (no sample)
  2.5 105 rays/s without choppers
  Same for band pass only
    Wavelength range chosen well
  WFM mode 104 /s and lower

## Slide 14: McStas optimization
Current performance on ODIN (no sample)
  Normalized to no chopper case
  Bandpass ~same number
  WFM much lower
    Many rays removed by choppers

## Slide 15: McStas optimization
Multiple time sampling
Ray parameters
Position, Velocity, Weight, Time, Spin
Current McStas – one time sampled

## Slide 16: McStas optimization
Multiple time sampling
Current McStas – one time sampled
Prototype – multiple times sampled from ESS Butterfly
and t_offset[100], p_t[100]
Ray parameters
Position, Velocity, Weight, Time, Spin

## Slide 17: McStas optimization
  ESS pulse time sampling
  Has to include tail
  Makes sense to use more times
Multiple time sampling

## Slide 18: McStas optimization
Multiple time sampling
  ESS pulse time sampling
  Has to include tail
  Makes sense to use more times
  Sampling strategy
    Step 1: position, direction, wavelength
    Step 2: multiple time sampling
  Number of time samples
    Up to a given number, user parameter
    Adaptive, given number on chosen monitor to avoid over-sampling

## Slide 19: McStas optimization
  Code updates necessary
    Components that ABSORB based on time (Choppers)
    Components that read time (Monitors)
  Components that unpack rays no longer support GROUP
    Multi slit choppers: Go from DiskChopper GROUP to MultiDiskChopper
  Need careful introduction to package
Multiple time sampling

## Slide 20: McStas optimization
Multiple time sampling performance
  Return to ODIN performance

## Slide 21: McStas optimization
Multiple time sampling performance
  Return to ODIN performance
  No choppers
    Can get more time information
  Only Band pass
    Same as without choppers
  WFM
    Significantly improved performance

## Slide 22: McStas optimization
Multiple time sampling performance
  Return to ODIN performance
  No choppers
    Can get more time information
  Only Band pass
    Same as without choppers
  WFM
    Significantly improved performance

## Slide 23: McStas optimization
Multiple time sampling performance
  Return to ODIN performance
  No choppers
    Can get more time information
  Only Band pass
    Same as without choppers
  WFM
    Significantly improved performance
    Gains between 5x and 35x

## Slide 24: McStas optimization
  ODIN Case
    White beam not using time information ~ 3% performance loss
    Parked choppers or BP using time information ~ 3-5x gain
    WFM mode ~ 5x-35x gain
Performance across ESS instruments
Case | Expected performance gain
Single frame instruments | 2-5x (if time focusing used as baseline)
WFM or complex chopper solutions | Significant, like ODIN
Monochromating choppers | Large

## Slide 25: McStas optimization
Multiple time sampling performance

## Slide 26: McStas optimization
Multiple time sampling performance

## Slide 27: McStas optimization
Multiple time sampling performance
Example data at maximum 500 sampled times

## Slide 28: McStas optimization
Multiple time sampling performance
Example data at maximum 500 sampled times

## Slide 29: McStas optimization
Multiple time sampling performance
Example data at maximum 500 sampled times

## Slide 30: McStas optimization
Multiple time sampling performance
2563 s vs 25.7 s
Example data at maximum 500 sampled times

## Slide 31: McStas optimization
Multiple time sampling performance
2563 s vs 48.5 s
Example data at maximum 500 sampled times

## Slide 32: McStas optimization
  Some additional considerations necessary before release
    Need to be carefully implemented to be backwards compatible
    Components where time impacts position or velocity need to be marked
      Doppler monochromator
      Others?
  Similar system would also be possible for spin
Outlook

## Slide 33: McStas optimization
  Used to get % gains when optimizing, not gain factors
  We see up to 120x gain at CSPEC (when time information used)
    Or in another way, reducing computation time by 99.2 %
  The gains are mainly where performance was problematic (high resolution tof)
    Simulation performance flatter with changing resolution
  These performance gains are independent on other speed ups
    time focusing / porting code to GPU’s
  Not in released McStas yet, prototype on github branch
  Simple to implement, can probably be used in other packages too
Conclusion

## Slide 34: Thanks for your attention