## Slide 1: SKADI
Small-Angle Scattering at ESS
PRESENTED BY Sebastian Jaksch

## Slide 2: Science Case

## Slide 3: Instrument Overview
Chopper System
Sample Exposure System
Sample area, shielding
Roughly 3x3 m open space, top and side accessible
Neutron detector system
Two independent detector banks movable, one fixed for low angles at 20 m
Beam filtering system
V-cavity polarizer, gradient spin flipper
Beam extraction Sysystem
NBOA, BBG, Reflector
Beam geometry conditioning
Collimation and apertures
20, 14, 8 and 4 m plus slit VSANS
Heavy shutter
Neutron Detector
1 m2 active area on two banks (6x6 mm2 resolution) and low angle detector (3x3 mm2 resolution) at start,
2 m2 full scope
Hutch
Space for two teams and instrument workshop

## Slide 4: Simulated Performance Data
Technical Specification |  | Standard mode 14 Hz | 
Instrument class | Polarized SANS | Bandwidth | 5 Å
Moderator | Cold | Wavelength range | 3 – 21 Å
Q range | 10-4 – 1 Å-1 | Momentum resolution | ΔQ/Q = 2 – 7%
Flux at sample (2 MW) | 3.6 x 108 ns-1cm-2 | Pulse skipping mode 7 Hz | 
Detector type | Li-scintillator, pixelated | Bandwidth | 10 Å
Detector coverage (current) | 1 m2 | Wavelength range | 3 – 21 Å
Detector coverage (full scope) | 2 m2 | Momentum resolution | ΔQ/Q = 1 – 7%

## Slide 5: Sample Handling
Two exchangable sample tables with kinetic mounts
Up to 990 kg loads
Optical table on top
Huber axes and hexapods available

## Slide 6: Sample Handling
Sample stack on top made from aluminium profiles
Simple to reproduce for custom sample environment
Power supply and connectors directly in the table for setup off-instrument

## Slide 7: Background Minimization
Guidelines for low background instruments
Absorb early: Collimation shielding directly around the neutron guide inside the bunker
Do not scatter back onto the detector: Get lost box behind detector

## Slide 8: Background Minimization

## Slide 9: Detector
Pixelated scintillation detector
6x6 mm2 or 3x3 mm2 resolution
Direct beam capable
Starting with 50% coverage
Better than microsecond TOF resolution

## Slide 10: Detector

## Slide 11: Simulation Preparation
Preparing for rollout
Users will be able to test different instrument configurations
Allows for pretesting of experiment time and optimized resolution in desired Q-range

## Slide 12: Early Science Workshop
https://indico.ess.eu/event/3938/

## Slide 13: Thanks to ….
Romuald Hanslik, FZJ
Sylvain Désert, formerly LLB now ESS
Tadeusz Kozielewski, FZJ
Ralf Engels, FZJ
Tamires Gallo, ESS
Annika Stellhorn, ESS
Henrich Frielinghaus, FZJ
… And you, for your attention !