## Slide 1
ICANS XXV
Recovery From a Sticky
Position
Presenter - Dan Coates
ISIS Target Design Group
Group Leader – Ste Gallimore
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 2
1 Isis target stations
.
2 The failure
3 Tooling design
4 Preparation
Agenda
5 The task
6 The cause & future
Notes: To replace photo with one of your own. 1) Send the geometric shape overlay to the back – Right-Click > Send to Back > Send to Back. 2) Replace image – use the guides provided to correctly position it. 3) Send your image to the back so that the geometric overlay re-appears over the image. Please remove or amend the image credit if you are using a different image to the one provided.

## Slide 3
ISIS SPALLATION SOURCE
160µA - 40Hz
40µA – 10Hz
800MeV – 50Hz
ISIS FACILITY

## Slide 4
TARGET STATION 1 TROLLEY LAYOUT
TARGET, REFLECTOR, AND MODERATORS (TRAM)
THIS IS THE AREA THAT IS THE FOCUS OF THIS PRESENTATION.
FORWARD SHIELD PLUG
VOID VESSEL DOOR & INFLATABLE SEAL
SHIELD GAP, USED FOR TRANSPORTING COMPONENTS INTO REMOTE HANDLING CELL
REAR SHIELD PLUG
CRYO TROLLEY, H2 & CH4 COLD BOXES
WATER SERVICES
ISIS Target Station 2 is of a similar layout!
40 years old
Low Millage, travels 30m, 3x per year, Total 3.6Km, (2.25 miles).
No service history, All retired.
300 tons
Trolley designed for regular methane moderator replacement (2 per year)
Company that supplied the bogies, ceased trading in the late 80’s
Driven from the tail by a chain, gearbox and motor.

## Slide 5
ISIS TARGET STATION 1 SECTION
TARGET SERVICES AREA
REMOTE HANDLING CELL
TARGET STATION MONOLITH
WASTE ROUTE, 1M X 1M TRAP DOOR TO TUNNEL
VOID VESSEL, He ATMOSPHERE
TROLLEY MOVEMENT
ISIS Target Station 2 is of a similar layout, but with a retractable void vessel!

## Slide 6
Target Station
Remote Handing Cell
Distance stuck
From home
Location of
Collision
TROLLEY
DRIVE
DIRECTION
Target Station
Tunnel
Target trolley gets stuck
1st July 2025

## Slide 7
Trolley 1.5m from fully forward
Trolley stuck
Trolley drive overload trips, chain jumps.
14 tons to move trolley
2 hours to get trolley fully back
Target trolley recovery

## Slide 8
North side Hudson trolley
New rubbing marks
Swarf
Damage spotted
Missing paint

## Slide 9
North side Hudson trolley
New rubbing marks
Swarf
Damage to forward tunnel cladding

## Slide 10
Target station tunnel looking towards
the remote handling cell
Inside the TSA
Target station tunnel looking towards
the void vessel

## Slide 11
Location of the damage is within the tunnel to the target station.
No visibility.
Poor lighting.
Out of reach of the manipulators.
No crane coverage.
1mm thick stainless cladding.
Stud welded to wall, number and location of ?
Challenging cut profile. Corners!
Location of the damaged cladding

## Slide 12
The Remote Handling Cell is for operational maintenance. It is not used for PIE. Radioactivity must be kept low for personnel entry.
However, we have done:-
Drilling & Tapping.
Bandsaw cutting of old TRaM frame.
Cropping of moderators.
All these tasks were carried out within reach of the crane and manipulators.
The removal of the cladding would need to be carried out remotely with the TRaM assembly occupying the cell. Personnel access not permitted with the Tram in the cell.
Only a small area with 1T crane coverage available to assemble kit to reach 1.5m down the tunnel.
Can only use two of the four manipulator arms, TRaM obstructs two of the arms.
Position of the TRaM
Space to assemble tooling
Cell entry trap door
Damaged Cladding
Limit of manipulator reach
Remote handling cell limits
Target storage well

## Slide 13
Cladding removal design considerations
Borrow a robotic arm from an external active handling supplier? - Tight time frame, difficult to
decontaminate and release back to supplier.
Plasma Cutting & Laser cutting? No spark arresting on the ventilation system.
Cutting by nibbler? - gap between cladding and wall unknown.
Remaining option was to cut cladding by grinding.
Grinder types, power, wheel sizes, wheel material types, carbide cutting / grinding wheel / diamond wheels.
  Tool holding, positioning, changing wheels.
  Control, how were we going to move into position, remote control, control via manipulators, motor drives?
  Location, build a frame to mount tooling, use the existing rails?
  Concerns, with gyro effects from grinder, wheel failure, vibration, dragging the trolley and tool wear. Mock up & trials to prove the design and procedures.
  Access, Tooling to fit through to 1m x 1m hatch!.

## Slide 14
Remote traverse 24V DC motors.
Trolley drive 24V DC motor.
Rear drive trolley
Cutting trolley
Lathe, Quick change tool post
Angle Grinder
Consisting of 2 trolley units to mount on the existing cell rails.
Each trolley is shipped in and coupled within the cell.
Utilising readily available off the shelf components, leadscrews, bearings, universal joints, motors, vee belt, angle grinders, slideways, and quick- change tool post.
PWM DC motor drive, fine control, maintains torque.
Multiple angle grinders prepared. 4”, 9”. Different wheel types. Arranged in various orientation.
Cutting trolley design

## Slide 15
Cutting trolley design
Trolley in the forward position to cut beyond the damaged area maintaining control access to manipulators
Trolley in the retracted position to provide access for tool changes and assembly.
Cutting range

## Slide 16
As the components arrived, they were assembled and tested.
Modifications carried out to improve reliability, performance, and for easier remote handling to reduce loading on the manipulators.
Mock ups and testing

## Slide 17
Deciding on grinder sizes
Testing discs
Test cuts

## Slide 18
Rear trolley
Front trolley
3 x grinders - vertical, horizontal & tilted.
Camera holder
Grinder power supply
& controls
Produce procedures for installation and cutting
Gained confidence that we can carry out the repair
Proven final design

## Slide 19
Robot split into 5 packages
3 x Units remotely craned into RHC
1 x TSA, trolley motor power supply
1 x manipulator rooms, remote traverse motor power supply.
Henry hitches a lift
The kit is prepared for posting
Into the remote handling cell

## Slide 20
Equipment posted into the cell and assembled
A week of transferring equipment into the remote handling cell.
Assembly of trolleys
Feeding through cables.

## Slide 21
Took 7 people to operate the robot
Based in three different room
First 3 cuts – 9" grinder
Cuts 4 and 5 – 5" vertical grinder
Cut 6 – 5" horizontal grinder
Cutting begins

## Slide 22
Unable to practice due to lack of information on how the stainless was mounted to the wall.
The unknown & frustration
Guessing the location of the studs.

## Slide 23
Modified pry bar
(Extended by 3m with crane loop)
Lots more grinding
After a week of cutting & prying, Success!
The target trolley was able to be driven forward.
Rescheduled user cycle was able to begin on time.
The design, mock ups, and repair was completed within a 2 month window.
It’s free!

## Slide 24
The target trolley has a history of getting stuck. There was a collision in 2010. Solved by correcting a tilt.
It always seem to occur on the northside.
Building subsidence.
120T trolley bogie wear.
Trolley being pushed from a single central point causing skew.
Cause of the collision?
Trolley bogie X4
Single point push pivot

## Slide 25
A team effort!
This difficult task that was completed within a very tight time frame. This was only possible due to the dedication of technical staff with various skill set contributing their efforts by reprioritising their work.

## Slide 26
Daniel.coates@stfc.ac.uk
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.