## Slide 1: ICANS XXV - 13–17 apr 2026, Clarion Hotel Malmö Live
A. Pietropaolo - on behalf of the SORGENTINA project team
ENEA, Nuclear Department, Frascati, Italy
antonino.pietropaolo@enea.it
SORGENTINA
a multipurpose accelerator-driven fusion neutron source

## Slide 2: Overview
Scientific premises
SORGENTINA project
The main components of the so-called thermomechanical demonstrator
Tests
Remarks & Conclusions

## Slide 3: Scientific premises Main focus
99mTc radiotracer for Single Photon Emission Computed Tomography
99mTc is effective in imaging diagnostics
Short Half-Life: T1/2 ~ 6 h
Optimal g-ray emission: Eg = 140 keV
99mTc covers about 85% of diagnostic radioisotope market with more than 30 million SPECT procedures per year worldwide.
It is mostly obtained from the b- decay from the parent nuclide 99Mo (namely the ‘’ vector’’ because of its long half-life of about 3 days)

## Slide 4: Scientific premises 99Mo/99mTc supply chain – gold standard
Direct fission to 99Mo is not very probable
Individual Fission Yield = 1.8E-3%
Cumulative Fission Yield = 6%
99Mo is thus produced by the main reaction paths: 235U + n 236U  99Zr + 134Te + 3n
and
235U + n  236U  99Y + 134I + 3n 99Zr and 99Y then decay by b emission to 99Mo.

## Slide 5: Scientific premises 99Mo/99mTc supply chain – alternative solutions
A series of 99mTc production methods (direct or by means of 99Mo precursor) have been identified as short-, mid- and long-term alternative solutions to the reactor based technique:
Thermal neutrons
98Mo(n,)99Mo
Fast Neutrons
100Mo(n,2n)99Mo
Gamma-ray beam
100Mo (g,n)99Mo
Accelerated charged-particle beams
96Zr(a,n)99Mo or 100Mo(p,2n)99mTc
In 2015
process tested at
FNG (ENEA-Frascati)
D + T  n + a + 17.1 MeV
En = 14.1 MeV
FNG
300 W accelerator-driven
14 MeV fusion neutron source
Yn ~ 5×1010 s-1

## Slide 6: Scientific premises 99Mo/99mTc supply chain – alternative solutions
2017
2025
2035
SORGENTINA

## Slide 7: SORGENTINA project Main goal of the project
  Design of a 14 MeV fusion neutron source 250 kW power neutron emission rate of about 1014 s-1;
  Production of medical radioisotope (mainly 99Mo and 64Cu) but also other applications with fast and thermalised neutrons for fusion technology and beyond.
  Need to proceed step by step as this is a
  first of the kind fusion neutron source
ENEA 25% RER 75%
5 M€
Thermomechanical
Demonstrator
Funding scheme
Project started on Jenuary 2020
Experiments on moderators @ FNG facility

## Slide 8: SORGENTINA project location
ENEA Brasimone Research Centre
Brasimone Lake
SORGENTINA Building

## Slide 9: SORGENTINA project The main components of the Termomechanical Demonstator (TMD)
11
ROTATINMG TARGET
2020-2021 (SARS-COV2): design/discussions
2022: call for tender
2023: contract (De Pretto Industries, Italy)
2024: realization
2025: testing (more tests needed)
ION SOURCE & ACCELERATOR
2020-2021 (SARS-COV2): discussions and conceptual design
2022: call for tender and contract (MUONS Inc., US)
2023-2025: realization
2026: testing (ongoing)
condenser
evaporator
Target acts as a heat pipe
Liquid-Vapor phase transition for power exhaust
D/T (50/50) plasma chamber
Multiapertures extraction grids
Drift tube
330 rpm

## Slide 10: SORGENTINA project The rotating target prototype
11
Evaporator
Condenser
Rotating target
Bearings
Stator
Spray manifolds
Electric engine
E-M inductor
What we were thinking about
What we have in our hands
simulate of the average power from the ion beam distributed by the target rotation
aluminium

## Slide 11: SORGENTINA project The rotating target prototype
Tests with EM inductor limitied @ 50 kW
Mechanical problems
to be solved as soon

## Slide 12: SORGENTINA project The ion source & accelerator
Is there a way to describe what is a
‘’competitive dialogue’’
as a procedure for an international call for tender?
Call for tender
Participants &
Contracting authority
MUONS Inc. US had the contract

## Slide 13: SORGENTINA project The ion source & accelerator
Parameter | Value
Ion energy | 300 keV
Ion current | 830 mA
composition | D+/T+ (50/50)
Beam gemetry rectangular spot | 20 cm - H 8 cm - W
Operation | CW
Hydrogen only for this phase of the project

## Slide 14: SORGENTINA project The ion source & accelerator
~0.9 A extracted and accelerated up to 50 keV;
91 apertures, 4-mm diameter arranged in a hexagonal pattern inside a diameter of 6 cm;
Electron suppressor grid;
Grids are made in oxygen free copper with a 10 mm layer of Mo;
Water channels are inside the electrode holders.

## Slide 15
5 electrodes to bring the beam energy from 50 keV to 300 keV;
Ceramic insulators among the electrodes.

## Slide 16: SORGENTINA project The ion source & accelertator: tests at Richarson Lab (US)
Single Aperture beam measurement on September 19th, 2024
H+, 16.7 mA @ 28 kV
More: February 2025, 91-hole grids, 100 mA of H+ extracted @25 kV

## Slide 17: SORGENTINA project Device installation at Brasimone Research Centre
Ion source 300 kV deck
Ion beam dump
Accelerator
Ion source
Ion beam dump
HV decks
Six 50 kV 900 mA power supplies are in series to get 300 kV;
Individual power taps at ground, 50kV, 100kV, 150kV, 200kV, 250kV, 300 kV;
4 sets of supplies are each powered by an alternator that is driven by an electromotor (3x150 kW, 1x11 kW) using an isolated drive shaft.
Vacuum, high voltage, control system tests done in Brasimone in February 2026
Full test in H+ @ 250 kW with beam dump @ ENEA Brasimone in May

## Slide 18: SORGENTINA project Next steps
The TMD phase will end on July 2026 (5 M€ funded). The next steps we need to do are:
Assessment of the primary cooling system using the inductor up to 250 kW power;
Study about rotating sealing systems:
  Ferrofluidic
  Polymeric
  polymeric + ferrofluidic
Joining vacuum chamber hosting the rotating target with the ion source & accelerator
Test in operando of the Ti sputtering system (already tested at laboratory scale in ENEA) to be hosted inside the vacuum chamber housing the rotating target
Titanium for H (then D/T) implantation:
TiDx (1.4 < x < 1.8) as from experimental campaing on FNG

## Slide 19: SORGENTINA project
Scientific Responsible
TASK-1: Civil works
TASK-2: Target
TASK-3: Accelerator
TASK-4: Neutronics
TASK-5: Tritium
TASK-7: Safety
TASK-6: Radiochemistry
TASK-8: Radiation Protection
TASK-9: Titanium facility
ENEA- RER MoU responsible
Planning and Quaility Manager
Essential for the funded phase
In the perspective of new funds
The SORGENTINA project team
Nadia Voukelatou, Alessia Santucci, Agostina Orefice, Antonietta Rizzo, Marco Lamberti,
Nicola Fonnesu, Pietro Zito, Ivan Panov Spassovski, Fabio Moro, Davide Flammini, Vincenzo Narcisi,
Valerio Sermenghi, Salvatore Scaglione, Danilo Zola, Danilo Dongiovanni, Nicholas Terranova,
Jean-Francois Ciparisse, Alberto Ubaldini, Camillo Sartorio, Andrea Evangelista, Paolo Del Prete, Pietro Agostini, Demis Santoli, Bruno Mastroianni, Ranieri Marinari, Marco Capogni, Mauro Capone, Alessandro Del Nevo,
Gian Marco Contessa (now ISS), Alessio Del Dotto (now INFN)
Researchers/technicians & adminstrative staff from different ENEA’s Laboratories/Departments
and thus different but synergic competences
About 10 publications about the first activities of the project
We are waiting to finalise all the remaining tests to publish more

## Slide 20: SORGENTINA project
…hopefully for the moment
Thank you for attention
and possibly see you with more results at ICANS XXVI