## Slide 1: The Path to 2.0 MW and Beyond at the SNS
April 16, 2026
Nicholas Evans
ICANS XXV, Malmö, Sweden
Notes: Image - 2021-P09584: Aerial overview of the Spallation Neutron Source, SNS, and the future location for the SNS Second Target Station, September 30, 2021. This image has been reviewed by an ORNL Releasing Official and is approved for public release, September 26, 2022.

## Slide 2: Outline
The Proton Power Upgrade (PPU)
Commissioning PPU
Operation beyond 1.4 MW
Challenges
Preparing for Second Target Station operations

## Slide 3: Spallation Neutron Source Today
Currently the highest power proton accelerator 1.4 MW 1.9 MW
Produce neutrons for materials science research via spallation on a liquid mercury target
Over 1 ms, 1000 pulses of negative hydrogen ions, each 700 ns long are accelerated to 1.3 GeV or 0.91c
Negative hydrogen (H-) ions stripped, resulting protons accumulated in the ring increasing the intensity by a factor of ~1000
Accumulated 700 ns long pulse of 1.5 E14 protons is extracted to target 60 times a second – roughly 32 kJ per pulse
DTL 87 MeV
CCL 186 MeV
SCL 387 MeV
SCL1000 MeV
After Upgrade 1300 MeV
RFQ 2.5 MeV

## Slide 4: Proton Power Upgrade (PPU) Overview
PPU doubles Spallation Neutron Source (SNS) power capability from 1.4 MW to 2.8 MW
  30% beam energy increase, 50% beam current increase
2 MW to First Target Station
Linac
Accumulator Ring
First Target Station (FTS)
Future Second Target Station (STS)
PPU scope

## Slide 5: PPU specifications & Key Performance Parameters
Key Performance Parameter | Threshold | Objective
Beam power on target (MW) | 1.7 at 1.25 GeV | 2.0 at 1.3 GeV
Beam energy (GeV) | 1.25 | 1.3
Target operation without failure (hours) | 1250 at 1.7 MW | 1250 at 2.0 MW
Stored beam intensity in ring (protons per pulse, ppp) | 1.60  1014 at 1.25 GeV | 2.24  1014 at 1.3 GeV
Major Specification | Original Spec. | Parameters Current Run | PPU full capability | PPU FTS operation
Beam power (MW) | 1.4 | 1.9 | 2.8 | 2.0
Beam energy (GeV) | 1.0 | 1.3 | 1.3 | 1.3
Beam current, macro-pulse average (mA) | 26 | 26 | 38 | 27
Macro-pulse length (ms) | 1 | 1 | 1 | 1
Energy per pulse (kJ) | 23.3 | 32 | 47 | 33
Repetition rate (Hz) | 60 | 60 | 60 | 60
All threshold values have been demonstrated Energy objective complete

## Slide 6: Phased Power Ramp-up: Philosophy and Execution
1/1/2022
7/1/2022
1/1/2023
7/1/2023
1/1/2024
7/1/2024
Increase neutron flux to users as quickly as possible
Push the power early to identify issues with new and existing equipment
1250 Hours at 1.7 MW achieved Oct. 7th 2024
1st Phase
2nd Phase
RID Window

## Slide 7: Power ramp-up – Phase 1
Energy
  1.12 GeV linac output energy
  1.05 GeV for operation (limited by injection dump septum magnet)
Issue
  During beam power ramp-up beyond 1.4 MW, instability of Cryogenic Moderator System (CMS) process control in one of loops during beam on/off transient
  Beam power was limited at 1.45 MW
Resolution
  New controls implemented, providing feed forward control for helium return heater
  Later improvement for > 1.7 MW through better feedback to CMS
    Supported by modeling and machine learning
Power ramp-up to 1.55 MW by increasing beam current
1.45 MW
1.7 MW
Loop 1 valve stable
20 – 80 %
CMS loop control at 1.45 MW as it was
CMS loop control at 1.7 MW after controls improvement
Notes: The control valve that supplies cold helium to the He/H2 heat exchanger
feed forward “kicking” of helium return heater

## Slide 8: Power ramp-up – Phase 2
Energy
  1.18 GeV linac (reduced gradients for some existing high beta cavities for higher beam loading as planned, and with 2 cavities off)
  1.05 GeV for operation (limited by injection dump septum magnet)
Issue
  New LLRF not reliably receiving pulse-to-pulse beam information
    Adaptive feed forward (AFF) was not properly functioning at beam rep. rates except 60 Hz – lower rep rates were worse
    This was noticed occasionally during phase 1 but the addition of phase-2 cavities and attempt for higher beam-loading highlighted issue
Resolution
  Software update corrected the issue, and got reliable beam information for LLRF AFF
Power ramp-up to 1.7 MW by increasing beam current (charge per pulse equivalent to 2.1 MW at 1.3 GeV)
Phase 2
Phase 1

## Slide 9: The Long Outage – All PPU Equipment is Installed
1/1/2022
7/1/2022
1/1/2023
7/1/2023
1/1/2024
7/1/2024
Aug. 2023 we shut down to install the final cryomodules, HPRF, upgrade the ring injection region, and make a penetration into the tunnel for the Second Target Station Stub
The rest of the talk will focus on the final push to 1.7MW at 1.3 GeV
1/1/2022
7/1/2022
1/1/2023
7/1/2023
1/1/2024
7/1/2024

## Slide 10: Injection Region Commissioning – New Magnets
Three new magnets designed and built at Fermilab to SNS specification to allow transport of 1.3 GeV beam through injection region of ring

## Slide 11: Ring Installation - Before
Chicane 2
Chicane 3
Dump Dipole

## Slide 12: Ring Installation - After
Chicane 2
Chicane 3
Dump Dipole

## Slide 13: Ring Injection Dump Imaging System (RID-IS)
RID-IS is based on Target Imaging System - Optical system in the tunnel (left) images luminescent coating on dump vacuum window (right)
PPU-designed, installed system for tuning

## Slide 14: Injection Dump Imaging System – First Light
Newly installed imaging system allowed for quick tune up of the injection dump
Application combines information from RID-IS and BPMs
Can’t use BPMs when both waste beams are present because trajectories are very different
BPM-only setup requires ‘simulating’ H0 trajectory by changing magnet currents, then verifying wirescan that can see both beams – time consuming
Discoloration at the center of the window is from previous run. Almost no light from the center of the window
Image of window externally illuminated
First image of beam on the dump

## Slide 15: Ring Injection Dump Imaging System
Both waste beams on the dump face with
~0.1μC per pulse (6E11 particles) on the dump, about 200 turns (of 1000) in the ring
“H minus” waste beam
Dead spot in coating
“H naught” waste beam
Uncoated area acts as fiducials for image alignment
Boundary of coated area
Image of window externally illuminated
ELOG: 12-JUN-2024 12:45 by Sarah Cousineau

## Slide 16: Injection Region Commissioning – Beam in Ring Highlights
BCM Signal showing first 1.3 GeV beam circulating in the ring for several hundred turns.
RID Imaging system showing full charge to the dump. Shadow of the foil can be seen – beam optics flips image of foil on window face.
Foil Shadow
With camera exposure adjusted two waste beams are clearly visible for 1.5 μC to the dump.

## Slide 17: RID Issues Since Install/Commissioning
RID window was replaced with coated window in Spring 2023 – must be done remotely because of high radiation near dump
Sealing surface showed damage from original helicoflex seal
A new design was created in short order which worked initially, but since then we have a small leak
RID volume is backfilled with He which is leaking into the beamline causing issues with ion pumps – considering vacuum in RID, analysis is underway
Slowly getting worse
Sealing surface

## Slide 18: RID Issues – Operational Impact
Leak is temperature dependent not an issue when running at high power
When we turn beam off for maintenance vacuum pressure shoots up
A range of measures to deal with issue:
  More turbo pumps
  Temperature set point of RID window cooling water increased when power is reduced
  Gate valve closed to isolate dump when off for long periods
Pressure rise when beam is off

## Slide 19: RID Issues – A More Permanent Fix
Polishing tool design
Window in cradle, with rollers and rails
New rollers
Installed rollers
Previous change out was very difficult due to damage from moisture
Need a new design for:
  carriage and rollers – rails can’t be removed
  remote tooling to polish the sealing surface
  new clamp
Work is underway, replacement planned for FY27

## Slide 20: Ramp to High Power Operation
With a decent tune throughout, only minor tweaking was left to reduce losses
Ramp to 1.7 MW began on June 12th, 2024
Everything going well until ring vacuum alarms started coming in at 870 kW on June 22nd, 2024!
Beam Power (W)
1.7E6 W
870 kW

## Slide 21: PPU Design
As part of PPU catcher was redesigned
Redesign of chicane 2 chamber and electron catcher allows easier replacement of –catcher
Catcher not brazed to chamber
Carbon-carbon geometry is identical to old catcher
Thermocouples were planned but not installed

## Slide 22: Vacuum Issues – What’s going on?
Vacuum group noticed water leaking from electron catcher - always a bad sign.
Cooling passage is in a vacuum-tight shroud.
How is water getting to vacuum?
Did we hit the copper and damage it?
Probably not this looks like sputtered carbon.
Leak check verified source of leak

## Slide 23: Electron Catcher – Leak Fixed
Leak was repaired, insufficient flow ID’ed as cause, flow increased
Imaging system quickly assembled and installed to view catcher during operation
No issues since
New design is underway
Illuminated view of electron catcher in-situ
Imaging system view of catcher during operation after leak repair. Electrons are hitting the right spot.
5
1
4
3
2
Leaking joint identified

## Slide 24: Catcher Damage 1 year later

## Slide 25: Original Catcher after 14 years for Comparison
In raking light you can see the channel dug by electrons

## Slide 26: Damage to copper tells an interesting story
Damaged copper has been covered by more carbon – suggesting reflected electrons might be under control after tunnel has been dug in carbon wedge
Compare to carbon etched away exposing copper in early operation (right)

## Slide 27: Ramp to High Power
Beam Power (W)
1.7E6 W
Start of 1.3 GeV commissioning
Full charge beam stored in ring
Electron Catcher Repairs
Target Gas Separation Issues
1250 Hrs at 1.7 MW, 1.3 GeV
Commissioning is ‘complete’
Production Run Starts
Time for loss tuning eaten by repairs

## Slide 28: SNS relies almost exclusively on high power pulsed klystrons for RF. Since 2019, there has been an increased volatility in the scientific klystron market, severely affecting the quality of the supply.
The SNS has three open klystron contracts, all starting in 2019:
5MW
3MW
700kW
Klystron Type | Usable Units | Refurbishment Status
5 MW | 0 / 3 | 1 under test at SNS
3 MW | 0 / 4 | 1 under refurbishment
700 kW | 4 / 28 removed | 3 under refurbishment
High Power RF – A Long-Term Problem

## Slide 29
Recent Experience: Klystron Fabrication & Operational Challenges
5 MW Klystrons
Cathode micro-discharge: instantaneous 5A spike in beam current
High perveance → low peak output power
All 3 klystrons: persistent cathode micro-discharge; prohibited operation on 2/3
Removed from CCL-1 (Aug 2024) after vacuum degradation; returned to vendor
3 MW Klystrons
Vacuum ion pump pressure vs. time — spike triggered DTL-3 removal (May 2024)
Persistent leaks → structural support redesign required
Incorrect cathode radius → low perveance & low output power
Removed from DTL-3 (May 2024); returned to vendor
700 kW Klystrons
SCL-25 fault log: repeated Cathode 5 Over Current faults (Aug 2024)
4 of 28 klystrons pulled from HV for repeated cathode arcing
3 of 4 removed units returned to vendor
Stable operation elusive even at lower power levels

## Slide 30: On the way to 2.0 MW
Since PPU commissioning we’ve been ramping power by 100kW per run
2.0 MW is expected in late April 2026
July 2024 – PPU Commissioning
1250 Hrs at 1.7 MW, 1.3 GeV
April 7, 2026

## Slide 31: How are we doing two years later?
Electron catcher recovery impacted tune up– but we used operation to bring losses back in line with expectations. Except…
  ring activation is higher than expected (very localized spot ~1700 mrem/hr at a foot!)
Even at 1.9 MW accelerator is operating well with no major issues due to high power operation

## Slide 32: A Plan for 2.8 MW – Preparing for the Second Target Station
We have a detailed plan toward a 2.0 MW, 45pps demonstration on the first target in June 2027
✅
✅

## Slide 33: ORAI Investigates Potential Beyond 2.8 MW
The Oak Ridge Accelerator Institute (ORAI) led by Fulvia Pilat is developing:
a conceptual design to support new applications at the SNS
a prototype multi-purpose, low-power test station in an existing SNS dump beamline
Low-power (<7kW) target to be added to existing injection dump line
Potential siting options for a third (100 kW+) target

## Slide 34: Summary
Spreading out installation and operation of new equipment proved a useful strategy to minimize the impact of new issues
Leaning on well-established machine settings wherever possible streamlined startup
Final commissioning push to 1.7 MW at 1.3 GeV was a huge success – one major hiccup with electron catcher, but recovery was quick
A lingering puzzle with injection losses
Dealing with a leak in the RID, a consumable electron catcher, and klystron sourcing issues
We’re inching closer to 2.0 MW, 60 Hz operation on the first target, and preparing for Second Target Station era with 2.0 MW, 45 pps on the First Target Station

## Slide 35: Thanks
Thanks to the PPU team, and the dedicated SNS staff for an amazing, sustained effort throughout the project
Special thanks to accelerator physics, beam instrumentation and operations for commissioning effort
Special thanks to our partners at Fermi National Accelerator Lab and Jefferson Lab
Thanks to Sang-Ho Kim, John Moss, Melissa Harvey, Vasiliy Morozov, Fulvia Pilat, and Charles Peters for providing slides
Thanks to the organizers for inviting me

## Slide 36: Backup Slides

## Slide 37: 1.7 MW at 1.05 GeV – equivalent to 2.1 MW at 1.3 GeV

## Slide 38
p+
H0
H-
H- beam
from Linac
Thin primary
stripping Foil
Thick secondary
stripping Foil
To Injection Dump
To the Ring
From the Ring
2e-
Foil stripping
H- → p+ + 2e-
p+
From the Ring
p+
To the Ring
H- beam
Notes: This is more detailed scheme of ring injection area.
Right now we can do experiment over here for a small pencil beam.
The H- beam is injected from linac into the ring through the corner of the thin foil.

## Slide 39: PPU commissioned 28 new complex RF systems in the high-beta portion of the superconducting Linac across three accelerator outage periods. The new systems ultimately power 28 new superconducting cavities.
700kW 805MHz klystrons x 28
LLRF Control Systems x 28
DI Water System for component cooling
High-Voltage Convertor Modulators x 3
Controls and Network
Scope - RF

## Slide 40: Scope – Superconducting Linac
PPU07 – Slot 25 installation
PPU CMs from end of linac Slot 32
PPU01
PPU02
PPU03
PPU04
PPU05
PPU06
PPU07
32 cavities and couplers procured and tested
  30 cavities field emission free
  2 cavities with limited field emission
  All cavities and couplers met specification
Eight cryomodules delivered from JLab to SNS
  All cryomodules met specification
  Seven are installed and operating with beam
  Cryomodule 8 is a spare
Unloading PPU07
Testing PPU CM in the SNS test cave

## Slide 41: Injection Region changes
New geometry meant injection region tuned from scratch
3 of 4 chicane magnets steer 2 waste beam trajectories, and recirculating beam – this drives injection region tuning
New combined function dump dipole for waste beam transport
Move chicane #1 upstream ~30cm
Chicanes #2, #3 replaced
Injection region after upgrade
p Beam
H- Beam
p Beam
Waste Beams

## Slide 42: Commissioning Timeline

## Slide 43: DTL, CCL and SCL Commissioning – Beam to Linac Dump
7 new high-beta cryomodules added to the end of the linac – 4 installed in previous outages, 3 new for 1.3 GeV operation
Commissioning of beam started Friday June, 7th
  Operation authorized to begin – 11:06
  Warm linac (DTL&CCL) tuning complete – 13:50
  Super conducting linac setup complete, 1.33 GeV beam to linac dump – 17:31
6 hours and 25 minutes to tune linac to a world record energy!
Machine setup from previous run provided a good starting point

## Slide 44: Injection Region Commissioning – Beam to Injection Dump
Initial tuning was done at 1.05 GeV to leverage existing machine settings – transport line from linac to ring was identical to last run
All of the new magnets must be tuned up from scratch

## Slide 45: Injection Region Commissioning – Beam in Ring
1.05 GeV Ring Commissioning Begins Saturday June 8th
  First pulses in Injection Dump – 9:54
  First beam stored in the ring, send to extraction dump – function of newly installed magnets verified - 16:27
1.3 GeV Ring Commissioning Begins Tuesday June 11th
  First 1.3 GeV beam to extraction dump – 16:33
Full charge pulse stored in ring on Wednesday June 12th
  Accelerator ready for low-loss tuning and then beam to target
Took a break for several days to allow fault studies, and target strain measurements before resuming accelerator tune up

## Slide 46: Injection Region Commissioning – Beam in Ring
Only remaining magnet to tune in the injection region was chicane #1 – we were quickly able to get beam circulating
With a good tune in the ring new magnets were all set within 3% of design values.
Start of commissioning to full charge in ring: ~80 hrs in the control room (5 days, 16 hr/day)

## Slide 47: Beam to Target
First beam on target June 18th, 2024
To reduce failure of components due to higher voltage at 1.3 GeV we now run all 14 at slightly lower voltage (instead of 13 + spare)
No issues were encountered with this new mode
Magnets in transport line to target scaled from existing 1.05 GeV machine settings with no issues