## Slide 1: The short- and long-lived method for water activation in spallation neutron systems
April 7, 2026
Ahmad M. Ibrahim, Franz X. Gallmeier, Tucker C. McClanahan, Don Montierth, Igor Remec

## Slide 2: Outline
Shielding of water loop components outside of core vessel
Methods used
Comparing methods
  Radioisotope concentrations
  Decay source spectra and shielding requirements
  Experimental validation
Conclusion

## Slide 3: Cooling water activated inside core vessel
Primary components inside the core vessel:
  The STS target, the proton beam window (PBW), the moderators, the beryllium reflector surrounding each moderator, the target viewing periscope, the collimators, and the core vessel shielding.
Cooling water activated by primary irradiation from protons, neutrons, other particles
Unique challenges caused by spallation and high-energy interactions
Cooling water carries radioisotopes out of the well-shielded core vessel

## Slide 4: Water flow carries radioisotopes to regions not directly exposed to primary radiation
Secondary components outside of core vessel are not exposed to primary radiation:
  Pipes, tanks, filters, and pumps
Adjacent accessible areas must be adequately shielded
Goal: combine water activation with flow calculations to shield secondary components
ORNL SNS STS target systems and downstream utilities
Core vessel
High bay

## Slide 5: Methods used
True calculation, dilution method, and short- and long-lived method

## Slide 6: Fully detailed calculation has thousands of steps
Core vessel
Secondary comp.
Times to use in calculations
Typical values
True calculation requires 45,000 × 2 + 1 activation steps per year
Very difficult

## Slide 7: Dilution method and short- and long-lived method
Total source
Constant irradiation in the core vessel with 100% availability during total operation time
Radioisotope’s activity density is corrected by irradiation volume to total loop volume
Irradiate all with a smaller source
Irradiation time = total operation time
Decay time =
Dilution method
Short- and long-lived method
Core vessel
Total operation time
Secondary comp.
Loop volume irradiated with smaller source,
Secondary comp.
Total source
One final irradiation step with and decay step with for only
Core vessel
Secondary comp.
Long-lived comp.
Short-lived comp.

## Slide 8: Comparing the dilution and short- and long-lived methods
Isotopic concentrations and source spectra

## Slide 9: Source and irradiation scenario
 | Dilution method | Short- and long-lived method | 
 |  | Long | Short
Source (proton/sec) | 3.4E+15 | 5.4E+12 | 3.4E+15
Irradiation scenario | 2 years of 5,000 h beam-on and 3,760 h beam-off | 2 years of 5,000 h beam-on and 3,760 h beam-off | N/A
 | 5,000 h irradiation | 5,000 h irradiation | 
Irradiation volume |  |  | 
Radioisotope's activity density |  |  | 
 | Dilution method | Short- and long-lived method | 
 |  | Long | Short
Source (proton/sec) |  |  | 
Irradiation scenario | 2 years of 5,000 h beam-on and 3,760 h beam-off | 2 years of 5,000 h beam-on and 3,760 h beam-off | N/A
 | 5,000 h irradiation | 5,000 h irradiation | 
Irradiation volume |  |  | 
Radioisotope's activity density |  |  | 
Core vessel
Total operation time
Secondary comp.
Core vessel
Secondary comp.

## Slide 10: Comparing isotopic activity densities at 1 Sec
Radionuclide | Half Life (s) | Half-life to loop time | Activity Density (Ci/cm3) |  | Percentage difference
 |  |  | Dilution | Short- and long-lived | 
H3 | 3.9E+8 | 9.9E+5 | 7.2E-6 | 6.1E-6 | 14%
Be7 | 4.6E+6 | 1.2E+4 | 1.0E-5 | 1.3E-5 | -28%
C11 | 1.2E+3 | 3.1 | 6.8E-6 | 7.0E-6 | -3%
O15 | 1.2E+2 | 0.31 | 6.1E-5 | 1.5E-4 | -140%
O14 | 7.1E+1 | 0.18 | 6.0E-6 | 2.4E-5 | -298%
N16 | 7.1E+0 | 0.018 | 1.8E-5 | 6.9E-4 | -3714%
N17 | 4.2E+0 | 0.011 | 9.6E-9 | 6.1E-7 | -6277%
Radionuclide | Half Life (s) |  | Activity Density (Ci/cm3) |  | Percentage difference
 |  |  | Dilution | Short- and long-lived | 
H3 | 3.9E+8 | 9.9E+5 | 7.2E-6 | 6.1E-6 | 14%
Be7 | 4.6E+6 | 1.2E+4 | 1.0E-5 | 1.3E-5 | -28%
C11 | 1.2E+3 | 3.1 | 6.8E-6 | 7.0E-6 | -3%
O15 | 1.2E+2 | 0.31 | 6.1E-5 | 1.5E-4 | -140%
O14 | 7.1E+1 | 0.18 | 6.0E-6 | 2.4E-5 | -298%
N16 | 7.1E+0 | 0.018 | 1.8E-5 | 6.9E-4 | -3714%
N17 | 4.2E+0 | 0.011 | 9.6E-9 | 6.1E-7 | -6277%
Differences increases with decreasing except for H3 and Be7
Differences are large for radioisotopes with short half lives
  Dilution method assumes equilibrium and then correct activities with
  Short- and long-lived method does not assume equilibrium because

## Slide 11: Comparing radioisotope concentration and decay spectra vs transit/decay time
Dominated by N16 before delay tank
O14 plays a role throughout the loop
emitters (O15 and C11) remain

## Slide 12: What causes differences in H3?
H3 inventory in spallation systems water is affected by secondary reactions.
  is produced by spallation of Oxygen
H3 activity densities calculated by Dilution and S&L-lived methods over 20 years of STS operation
cross-section from https://www.oecd-nea.org/janisweb
Dilution method assumes He3 is being constantly irradiated inside the core vessel for 100% of operation time even though it is only irradiated for of the time
5,330 barns thermal cross-section
Notes: Because of secondary reactions.
For Tritium, its inventory in spallation reactions is affected by two interactions, not one.
The first is the spallation reaction of Oxygen that creates tritium. This tritium decays to He-3. He-3 undergoes n,p reactions to regenerate the tritium again.
Method A overestimates the production of tritium by this secondary reaction.

## Slide 13: What causes differences in Be7?
Be7 inventory in spallation systems water is affected by burnup.
  is produced by spallation of Oxygen
Be7 activity densities calculated by Dilution and S&L-lived methods over 20 years of STS operation
cross-section from https://www.oecd-nea.org/janisweb
Dilution method assumes Be3 is being constantly being burnt inside the core vessel for 100% of operation time even though it is only irradiated for of the time
~50,000 barns thermal cross-section
Notes: The opposite happens to Be-7.
Be-7 is generated by the spallation reactions of Oxygen. However, because of its extremely high n,p cross-section, it gets burned as it stays in the irradiation region.
Method A assumes that it stays in the irradiation region more than it does, so it underestimate its inventory.

## Slide 14: Comparing the dilution and short- and long-lived methods
Decay source spectra and shielding requirement

## Slide 15: Source spectra and dose rates
Dose rate is ~100% caused by N16 for short decay times
Differences in dose rates at these times is equivalent to N16 between the two methods
Decay photon spectra calculated using dilution and S&L-lived methods
Dose rate inside a concrete shield surrounding an infinite pipe
Notes: Looking at the decay photon source spectrum and the decay dose rate, we can see that the most significant difference is around the 6 and 7 MeV, corresponding to the two gammas that the N-16 emits. In this case that we ran, the difference was a factor of 38.
We ran a simulation for an infinite pipe covered with regular concrete for shielding, and here are the dose rate profiles inside the concrete.
When I multiplied the dose rates calculated by Method A by the factor of 38, the two profiles agreed very well.

## Slide 16: Comparing the dilution and short- and long-lived methods
Experimental validation

## Slide 17: Well shielded Total Loss Monitor (TLM) near the proton beam window return pipe
Most reliable reading, not affected by interreferences
TLM ~3 cm from the wall of a 1.5” pipe with 0.065” walls
Notes: We have many radiation monitors installed near components of the cooling water circuit at the SNS.
This is the monitor installed close to the proton beam window return pipe.

## Slide 18: Control System Studio’s reading at SNS
At ~1.4 MW power, TLM reading ~97 Rem/hr
From https://status.sns.ornl.gov/
1.4 MW power
~97 Rem.hr
Notes: We monitored the reading of this radiation monitor over several days. Its reading was about 97 rem/hr at 1.4 MW operation power of the SNS.

## Slide 19: Dose rate calculated by Method A and Method B vs TLM measurement
Dose rate in the air surrounding PBW return pipe
At ~1.4 MW power, TLM reading ~97 Rem/hr
Calculation or measurement | Dose rate (Rem/h) | % difference with measurement
Measurement | 97 | 0%
Dilution | 7 | 92.8%
S&L-lived | 79 | 19.6%
S&L-lived calculates a much closer dose rate to measurement
Notes: Method A calculated 7 Rem/hr. Method B calculated 79 Rem/hr.
This shows that Method B is much closer to measurements.

## Slide 20: Conclusion
Coolant water transports radioactive nuclides from the irradiation regions inside the core vessel to secondary components that are not directly exposed to the primary radiation field.
We developed the short- and long-lived method to accurately model all radioisotopes regardless of whether their half-lives are short or long compared to the loop circulation time.
We recommend this method for shielding analysis of activated water loops in the design of the STS and similar spallation systems.