## Slide 1: AARE Activation Library Developments
April 16, 2026
Franz Gallmeier
ORNL, NScD/NTD

## Slide 2: Layout
AARE introduction
Motivation
AARE development roadmap
CINDER library development overview
Decay information updates
Cross section updates
Fission fragment yield updates
Forging of the libraries
Overview of library contents

## Slide 3: The AARE workflow
Workflow geared around MCNP analyses of accelerator driven systems
Generate radionuclide inventory information
Generate decay gamma sources
Perform decay gamma dose rate analyses
RSICC Packages
  CINDER_1.05 (2008)
  AARE_1.0 (2018)
MCNP6/MCNPX
AARE Activation Script:
Loop over cells:
Prepare materials, fluxes
Prepare transmutation inputs
Execute transmutation
mcnp_inp
outp
histp
CINDER2008
ORIHET3
SP-FISPACT
aare_activation_inp
orihet3_out
fispact_out
TAB4
?
AARE_Gamma Source Script:
Read decay gamma sources
Prepare MCNP format source definition
aare_gamma_source_inp
MCNP_sdef
MCNP6/MCNPX
result
table_by_...
spectra_...
cell_dir_vol_list
mcnp_inp

## Slide 4: Motivation for Updates
MCNP evolved from MCNP5 -> MCNPX -> MCNP6
  Neutron cross section libraries extended to 150 and 200 MeV with mix-and-match using models where no data are available
  Charged particle cross section libraries introduced
Nuclear data developments:
  Progress in evaluated data: ENDF/B-VI -> ENDF/B-VII -> ENDF/B-VIII also JEFF, JENDL, KAERI …
  Nuclear reaction modeling provides large-volume libraries
Make use of these developments to improve predictive capability

## Slide 5: AARE2 Development Roadmap
New activation libraries
Modernized CINDER code
Update MCNP RNUCS tally
Converting workflows to Python
Develop mesh-based activation
Develop plotting

## Slide 6: Here we cover CINDER Library Developments
Update decay data basis
Update activation cross section data
Generate new charged-particle-induced and gamma-induced cross section libraries
Extend the fission fragment distributions
Merge all parts into a complete library

## Slide 7: Decay libraries provide:
nuclide spin, parity, energy-level, half-life
decay schemes
decay products and their energy distributions when provided

## Slide 8: Update decay library
ENDF/B-VIII.0 as the basis, which gives the largest coverage among the evaluated data libraries
  for 3742 nuclides
Supplemented by data from various other sources
Summing up to 5711 nuclides from 4084 in CINDER2008

## Slide 9: Cross section data libraries provide:
Cross section data bases of pointwise data in ENDF-6 format
Reaction cross sections for 200 explicit reaction channels to 30 MeV energy
Radionuclide production cross sections above 30 MeV energy
Fission cross sections

## Slide 10: New Activation cross sections for CINDER libraries
Extending neutron libraries to 150 MeV energy
Develop charged-particle-induced and gamma-induced activation libraries
Starting out with TENDL cross section libraries (TENDL-2021, TENDL-2023, latest release TENDL-2025 not used yet)
TENDL offers cross sections to 200 MeV energy for
  2850 nuclides
  Neutrons, protons, deuterons, tritons, helions, alphas, gammas
Supplemented by other sources to cover low mass nuclei for which TENDL uses ENDF/B-VIII with lower upper energy

## Slide 11: Library preparation steps
Using NJOY2016 process pointwise library data into multigroup representations
  of 339 groups for neutrons
  of 47 groups for charged particles and gammas
  Flat weighting spectrum for group collapsing
TENDL2023 data for 2835 nuclides
Neutron library supplemented by
  16 nuclides from TENDL2021
  3 nuclides from ENDF/B-VIII.1
  7 nuclides from JENDL5
  9 nuclides from IEAF2001
Proton library supplemented by 4 nuclides from JENDL5

## Slide 12: Fission Fragment Yields
Listing of fission fragment nuclides with abundance per fission event

## Slide 13: Fission fragment yields
No fission fragment libraries for charged particle and gamma induced reactions exist.
By extending the data range to 150 MeV considerably increases the number of nuclides with fission channels.
The fission fragment distributions exhibit a strong dependence with incident particle energy.
A new approach needed to be taken.

## Slide 14: Fission fragment yield calculations (1)
The TALYS2.0 code used for producing the TENDL libraries can be applied to perform fission fragment yield analyses with
  BROSA model (fully functional with phenomenological model)
  GEF model (insufficiently only first chance fission followed and requires evaporation of pre-evaporation fission fragment distributions).
Modifications to TALYS2.0 developed:
  by updating GEF model from 2016 version to 2023 version,
  by building a library of fission fragment deexcitation information for 4200 possible pre-evaporation fission fragments for a list of excitation energies from 1-100 MeV.
  expand TALYS2.0 by generating pre-evaporation fission fragment distributions from multi-chance fission branches and applying the deexcitaion library for producing post-evaporation (final) fission fragment distributions.

## Slide 15: Generate Fission Fragment libraries
Perform TALYS2.0 analyses for all CINDER radionuclides with fission channel for neutron-, charged-particle-, and gamma- initiated reactions (about 800 per sub-library) and for all energy groups.
Perform TALS2.0 analyses for 90 spontaneous fission nuclides of the CINDER library by running cases of low-energy incident gammas.

## Slide 16: The Creation of the CINDER Libraries
The Library_Maker_Tool of the AARE package was updated to merge all the decay, cross section, and fission fragment yield data into independent sub-libraries for neutrons … gammas.
Upgrades applied for:
  Merging explicit reaction channel and radionuclide production data to unified cross sections;
  Adding energy-dependent fission fragment yield blocks to each fissile radionuclide, and a block of fission Q-values;
  Adding the nuclide-specific spontaneous fission yield data;
  Adding the mapping of reaction outcomes from TENDL and other sources to CINDER (impacted mostly metastable states).

## Slide 17: Neutron library comparison: Cinder2025 vs Cinder2008
5711 nuclides
250 stable nuclides (black)
2752 nuclides with cross section (blue+red)
858 fission nuclides (red)
Cinder2025
Cinder2008
4084 nuclides
248 stable nuclides (black)
819 nuclides with cross section (blue+red)
103 fission nuclides (red)

## Slide 18: Decay information sources: Cinder2025 vs Cinder2008
Cinder2025
Cinder2008
  3742 ENDF/B-8.0 (cyan)
  59 JEFF33 (magenta)
  1 JENDL5 (red)
  80 NDS (blue)
  52 ENSDF (green)
  1768 Moeller 2019 (grey)
  2864 ENDF/B-7.0 (cyan)
  JEFF31 (magenta)
  278 EAF (red)
  219 ENDF/B-6.0 (pink)
  106 NDS (blue)
  9 XDL (coral)
  181 Moeller 1997 (grey)

## Slide 19: Nuclide production coverage: Cinder2025 vs Cinder2008
Cinder2025
Cinder2008
  3647 nuclides produced by reactions
  1808 nuclides produced by reactions

## Slide 20: Fission fragment coverage: Cinder2025 vs Cinder2008
Cinder2025
Cinder2008
  4205 nuclides produced by fission
  1325 nuclides produced by fission

## Slide 21: Fission fragment distributions

## Slide 22: Cinder2008 vs Cinder2025 XS comparison: neutron ->Al27
For stable nuclides best parameter nuclide structure data set exist in TALYS
The cross sections compare well using these input data
Higher upper energy opens many more channels: 15 Cinder08 vs 107 Cinder25

## Slide 23: Cinder2025 Cross sections: proton ->Al27
96 nuclide production data sets exit for protons on aluminum

## Slide 24: Summary
New activation libraries consisting of decay, production cross section, and fission yield data were generated extending the cross section energy to 150 MeV, and extending projectiles from neutrons to light ions and gammas to adapt activation and residual dose analyses to the upgrades of MCNP6.
LANL is developing an upgraded CINDER code, CINDER2025, which was used for first tests of the neutron library.