## Slide 2: ESS Proton Beam Window (PBW)
From manufacturing to site commissioning
PRESENTED BY sara Ghatnekar Nilsson
Anders Andersson, Stig Jörstad, Adrien Besson, Javier Garitaonandía, Fernando Sordo

## Slide 3: Agenda
1 Why does ESS need a Proton Beam Window?
2 Introduction
3 Manufacturing
4 Beam diagnostics
5 Factory Acceptance Test, vacuum compatibility
6 Factory Acceptance Test, mechanical integration
7 Installation at ESS
8 Site Acceptance Test – vacuum tests after installation
9 The end

## Slide 4: Why does ESS need a PBW?
PBW
Monolith Vessel
≈10-5 mbar
Accelerator side
≈10-7 mbar
PBW Vessel
≈10-2 mbar
The Proton Beam Window forms the mechanical boundary between the Accelerator and the Target environments.
The Accelerator side vacuum requirement is <10-4 mbar.
The Target side vacuum requirement is <1 mbar.
So, what vacuum levels does ESS have today before Beam on Target?

## Slide 5: Introduction
The PBW is an In-kind delivery from ESS-Bilbao, Spain.
The design was done in collaboration between ESS-Bilbao and ESS since 2016.
The components to be presented today
Manufacturers:
Leading Metal Mechanic Solutions S.L.
Thune Eureka S.A.
Nortemecánica S.A.

## Slide 6: Manufacturing, PBW
PBW milled out from Al T6061-T6 block. Cooling channel done by Electro Discharge Machining.
165 mm
85 mm
Weight: 128 kg
Manufacturing started in 2023
PBW system = PBW+frame+flanges+pipes+inflatable seals

## Slide 7: Manufacturing, PBW
3 fiducials made by FZ Jülich GmbH.
The PBW was E-beam welded to the frame by FZ Jülich.
View from Acc side
2 mm water cooling channel
View from Target side

## Slide 8: Manufacturing, PBW frame and flanges
Complete PBW system with inflatable seals on flanges, and hoses for vacuum, cooling water and instrument air.
Inflatable seals procured from Mewasa

## Slide 9: Manufacturing, Pipe box
Pipe box housing tubing for instrument air, water, vacuum and signal cables.
4200 mm
Total weight of PBW+Pipe box = 450 kg

## Slide 10: Manufacturing, Shielding plug
Shielding plug made of stainless steel with a weight of ≈15 tonnes.
Stainless steel plates put together by threaded rods.
3500 mm
⌀ 980 mm

## Slide 11: Beam diagnostics
The APTM monitors the fraction of the proton beam that is outside the intended envelope.
Connected to MPS.
Aperture Monitor (APTM)
View from Acc side
View from Target side
View from Acc side
128x52mm

## Slide 12: Beam diagnostics
The Target side of the PBW is coated with Al2O3 mixed with Cr2O3 by flame spraying.
The luminescence light is captured by mirrors inside the Monolith Vessel. Connected to MPS.
Luminescence coating
Un-coated
Coated
Pressure test (7 bar(g)) was done after coating to ensure the structural integrity of the PBW.
Coating thickness ≈180 mm

## Slide 13: FAT, vacuum compatibility
All media tubes and the inflatable seals were tested and approved.
Performed in Oct 2024 at Zamudio, Spain.

## Slide 14: FAT, mechanical integration
The experience from the FAT was that the margins were too tight. Therefore the Shielding plug was optimised by machining some chamfers (Nortemecánica).
Performed in Nov 2024 at Nortemecánica.
The components

## Slide 15: PBW Port Block and PBW Vessel
Installed at ESS in Feb 2022

## Slide 16: Installation of PBW at ESS
Installed in Feb 2025

## Slide 17: Installation of Shielding plug at ESS

## Slide 18: SAT - Vacuum test after installation
The inflatable seals were pressurised with 2 bar (g).
After installation, the PBW Vessel was evacuated and then filled with He.
Leak rates, both on the Acc side and the Target side, were measured and were approved.

## Slide 19: The end