## Slide 1: The Proton Beam Transport Line for the Second Target Station (STS) at the Spallation Neutron Source (SNS) Michael Allitt, Larry Boyd, Austin Chaires, James McLaurin, Alex Baron, Andrei Shishlo, Moira Wedekind, Emily Wozinski
RTST Beamline Overview and Design Approach
The Second Target Station (STS) Accelerator Systems (AS) is responsible for the design, procurement, and installation of the Ring to Second Target Station (RTST) beamline, which transports a 1.3 GeV proton beam from the existing Ring to Beam Transport (RTBT) beamline to the Second Target.
Key RTST requirements include high reliability, minimal component and tunnel activation, and compatibility with existing systems. The RTBT beamline has operated reliably since 2006 with low activation, so the RTST design leverages the RTBT layout and 20 years of operational experience. Wherever practical, existing RTBT equipment designs are used, reducing spare management and design costs. New magnets are required only for beam extraction, designed at Fermi National Accelerator Laboratory (FNAL), while all other magnets, beam instrumentation, and the vacuum system follow proven RTBT designs. New magnet power supplies are required, as the original FTS supplies are no longer available.
The RTST beamline has three main sections:
RTBT extraction region – incorporates new magnet designs to divert protons from the RTBT.
RTST transport beamline – carries the diverted protons to the Second Target.
Final focusing region – sets the beam spot size and shape at the target.
Mechanically, the RTST begins at the gate valve separating the RTBT and RTST vacuum systems and ends at the interface with the Proton Beam Tube Assembly (PBTA), defining the full beam path from the RTBT to the Second Target.
RTST Extraction System Requirements and Operation
The RTST extraction system is designed to meet two primary requirements:
Extract proton pulses from the RTBT at a rate of ≤ 15 Hz (S02-R002).
Maintain a beam trajectory compatible with installation and maintenance access within the existing Stub from the Proton Power Upgrade (PPU) project (S02-R010).
The system selects every fourth pulse from a 60 Hz proton source and directs it into the RTST beamline toward the second target. Each pulse has a width of ~660 ns. While the source operates at 60 Hz, the extraction system is active at 15 Hz, remaining inactive for three out of every four pulses.
During beam tuning and commissioning, lower repetition rates are achieved by selectively blanking pulses using the beam scheduling software.
Beam Optics Design and Simulation
The optics design defines magnetic fields and magnet locations required to extract and transport the proton beam while minimizing beam loss. The model extends upstream to RTBT:QV07 and downstream through the final quadrupole, with particle tracking simulations performed from RTBT:QV07 to the target face. Scattering effects from the proton beam window (PBW) are not included in tracking and are instead treated in neutronics Monte Carlo N-Particle (MCNP) models within the TS scope.
Beam dynamics simulations were carried out using PyORBIT, a Python-based version of the SNS-developed Orbit code, validated during the design and commissioning of the Spallation Neutron Source ring and transport lines. PyORBIT has been benchmarked against Orbit and other codes, with beam clearance predictions further verified during STS extraction vacuum system design to ensure sufficient spacing between the RTBT beam and vacuum chamber wall.
The RTST beamline includes 15 dipole magnets and 56 quadrupole magnets to guide, steer, and focus the beam from extraction to target. The final four quadrupoles, located near the beamline end, shape and focus the beam spot on the target surface. Simulations indicate no beam loss and controlled horizontal and vertical beam sizes.
Beam spot sizes within the required range of 60–90 cm² are achievable, as confirmed by simulations of 2D beam density distributions at both upper and lower bounds; smaller spot sizes are also possible. The optics model excludes PBW scattering effects, which are expected to reduce peak proton density by approximately 5%.
2D Transverse Beam Density at RTBT:QV07 Entrance
Simulated Proton Beam Spot at Target Face
STS
The Second Target Station is being developed as a next-generation neutron source optimized for the production of cold neutrons. Designed to deliver world-leading peak neutron brightness, it marks a significant advance in experimental capability. By enabling measurements across broader ranges of time and length scales, the STS will open new scientific possibilities, including real-time studies and the analysis of smaller or more delicate samples.
 = 5 Å
SNS-STS
ESS (5 MW)
ESS (2 MW)
J-PARC
SNS-FTS (2 MW)
CSNS
SNS-FTS
ISIS TS2
ISIS TS1
HFIR
ILL
FRM-II
NIST
SONATE (est.)
PSI
ORPHEE
LUJAN
short-pulse
long-pulse
steady-state
USA
Asia
Europe
Planned
Existing
RTBT:QV09 Large Quadrupole
The replacement for RTBT:QV09 is a large-aperture quadrupole, increasing the aperture from 21 cm to 40 cm to accommodate trajectories for both first- and second-target protons. The magnet was designed by Fermilab.
The system includes the magnet, support stand, power supplies, and associated cabling. The stand sets the magnet mid-plane at a nominal beam height of 40.98 in above the floor, with an adjustment range of +3 in / −1 in.
RTBT:QV09 operates at a nominal current of 1538 A. To meet this requirement, the installation uses five parallel supply
Narrow-Core Quadrupoles
The narrow-core quadrupole is a modified version of the standard 21 cm aperture magnet, developed to address space constraints immediately downstream of the extraction region. At three locations, reduced clearances between beam pipes and adjacent hardware require a more compact core profile to prevent physical interference.
RTBT:QH10 and RTBT:QV11 are powered in series with existing quadrupoles; therefore, the narrow-core design must match the current vs. field gradient response of standard magnets within a few percent to preserve RTBT optics. The
Pulsed Dipole System
Pulsed dipoles in the extraction region operate at 15 Hz, with current rise, flat-top, and fall completed in < 33 ms (FTS pulse spacing). A single design is used for all four magnets, each operating at different currents. The magnets feature a C-shaped laminated electrical steel core to limit eddy currents and are mounted on three-point adjustable stands for precise alignment.
The generator output is waveform-shaped to meet timing constraints and minimize eddy current heating in the magnet and vacuum chamber, using SNS machine timing for control and triggering. The waveform uses minimal ramp rates within the 33.3 ms window, reducing induced voltage
RTST Transport System
After extraction, the beam travels ~220 m through three bends and two straight sections to the Second Target. The layout is defined by beam optics, setting magnet placement and spacing along the beamline. The system includes 15 × 17D120 dipoles (bending), 56 × 21Q40 quadrupoles (focusing), and 22 × 27CD30 correctors (trajectory control), distributed to steer and focus the proton beam to the STS. The lattice minimizes beam loss and follows RTBT-like spacing, except near the end where final quadrupoles set the beam spot size on target.
All magnet types are proven SNS Ring and RTBT designs with excellent reliability. Magnet stands are new designs based on existing SNS concepts.
17D120
21Q40
27CD30
PPS
Magnet systems in the extraction region interface with the PPS to enable safe access to the RTST Tunnel and Target Building, by locking out the extractions magnets, when beam is delivered to the FTS only.
A dedicated PPS interlock terminates beam if pulsed dipole magnets exceed 15 Hz, ensuring beam power to the Second Target remains within design limits.
Additional radiation safety features include removable shielding at the Labyrinth wall and Truck Access Tunnel entrance, and a Gamma Blocker at the beamline end to prevent target backshine during RTST maintenance. The design is based on the Ring Injection Dump system.
Beam Instrumentation
BCMs will be installed at each end of the RTST beamline. BLMs are installed at every quadrupole, and BPMs are installed at quadrupoles followed by corrector magnets.
Three Wire Scanner (WS) emittance stations are included for Twiss parameter measurements. A Harp at the beamline end will be used during commissioning to measure the transverse beam profile and proton density, it will remain available during routine operation for beam setup and as a backup to the TS harp near the Proton Beam Window (PBW).
BCM, BPM, BLM, and WS are existing SNS designs. The harp is currently under development by the RAD Beam Instrumentation group, with a prototype installed in the RTBT beamline performing well. A View Screen (VS) is also planned for commissioning and is the only new diagnostic design within the AS scope.
Vacuum System
The vacuum system is adapted from the RTBT design. It is divided into sections by sector gate valves for serviceability and includes a proportional number of thermocouple (TCG) and cold cathode (CCG) gauges, pump-down ports, and vent valves.
Ion pumps (IPs) maintain high vacuum after the initial pump-down, which is performed using a turbo pump (TMP) that is subsequently removed from the beamline.
A permanent TMP with a scroll backing pump is installed at the Proton Beam Tube Assembly (PBTA) end of the beamline to handle the anticipated leak rates from the PBW seal.
Radiation Safety
STS Accelerator Systems manages four radiation shielding configurations for different operational scenarios:
Labyrinth Shield Wall – protects personnel in the RTST tunnel when the beam is directed to the FTS.
Truck Tunnel Shield Wall – protects personnel outside the tunnel when the beam is directed to the STS.
STS Gamma Blocker – shields against backshine from the Second Target during maintenance and shutdown.
RTBT Beam Stop – expected to prevent the beam from reaching the FTS when directed toward the STS.
Proton Flux Simulation During Normal Operations - Plan View
Labyrinth Shield Wall
BPM
BLM
BCM
Wire Scanner
Harp
Labyrinth
Shield Wall
Truck Tunnel Shield Wall
STS Gamma Blocker
RTBT Beam Stop
Power Supply Location
Power supply placement is determined by magnet location: units serving the extraction region will be housed in the Ring Service Building (RSB), while those supporting the remaining transport magnet will be in the Central Service Building (CSB).
Conclusion
The proposed RTST beam transport line provides a robust and well-integrated solution for delivering high-quality proton beams to the Second Target Station. By combining proven design principles with targeted innovations, the system achieves the performance, reliability, and safety required for next-generation neutron science. This work establishes a strong technical foundation for STS, enabling enhanced experimental capabilities and supporting future advances in neutron scattering research.
Extraction Magnet Type | Quantity
Large Quadrupole 40Q70 | 1
Pulsed Dipole 25D50 | 4
Narrow Quadrupole 21Q40N | 3
Transport Magnet Type | Quantity
Quadrupole 21Q40 | 56
Dipole 17D120 | 15
Corrector 27CD30 | 24
1
1
1
1
2
3
3
3
1
25D50
2
40Q70
3
21Q40N
and eddy currents and includes a flat-top to verify current tolerance before second-target proton accumulation.
The shaped signal is amplified by commercial MRI gradient amplifier power supplies, producing the required differential current. Cable ampacity is set by equivalent RMS current: two 777 kcmil conductors (supply and return) provide 7% margin, at an operating point 6% above peak current requirements.
and five parallel return 777 kcmil DLO conductors, routed through two 6-inch conduits from the Ring Service Building (RSB). This configuration provides a 75°C ampacity of 1932 A, including a 20% de-rating factor for three to six conductors in conduit.
magnet was designed by Fermilab.
Power connections for RTBT:QH10 and RTBT:QV11 reuse existing RTBT cabling. For RTST:QH01, three parallel supply and three parallel return 777 kcmil DLO conductors are used, providing an ampacity of 1159 A and ~18% margin over the 980 A operating current.
17D120 Dipole Chamber
40Q70 Large Quadrupole Chamber