## Slide 1
MAGNI will be
A flexible short length instrument (~30m) with high flux, high spatial resolution, large field of view, utilizing the divergence and relaxed wavelength resolution
Complementing ODIN’s capabilities (ODIN is expected to be heavily oversubscribed)
Offering flexibility for time-sensitive industrial users
Allowing novel sample environments requiring beamline reconfiguration (gratings, neutron microscope etc.)
Enabling studies where flux and spectral data are crucial
Possibly enabling epithermal neutron resonance imaging (with series of Fermi choppers) for element-specific analysis and precise cross-section measurements
25.09.2025
MAGNI – Microscopy, Advanced and Grating Neutron Imaging
Markus Strobl (PSI/DTU) Luise Theil Kuhn (DTU) Robin Woracek (ESS) et al.
MP2
MP1
MP3
Illustration: NEUTRA 2.0@PSI

## Slide 2
25.09.2025
MAGNI – Microscopy, Advanced and Grating Neutron Imaging
Markus Strobl (PSI/DTU) Luise Theil Kuhn (DTU) Robin Woracek (ESS) et al.
MAGNI will enable neutron imaging studies of
large industrial
components
40
50
60 wt.% CuCrZr
Fast operando evolution of phases
Operando phase mapping in multi-material laser powder bed fusion: https://doi.org/10.1080/17452759.2024.2429132
Industrial processes
Multi-scale mapping
Nanostructures in macroscopic context
Revealing heterogeneous
dynamics in out of equilibrium
systems
Spectroscopic neutron imaging for resolving hydrogen dynamics changes in battery electrolytes: https://doi.org/10.1016/j.mtadv.2023.100405
Neutron imaging in 2D and 3D as a powerful tool to investigate electrolyte degradation and plating mechanisms in sodium-ion batteries: https://doi.org/10.1016/j.jpowsour.2025.237846
Operando studies of novel battery materials
Quench. 100 C/h 30 C/h 10 C/h 0.3 C/h
Hydrogen & hydrides in metal
Neutron radiography of detrimental hydrogen in nuclear fuel claddings

## Slide 3
MAGNI is different from ODIN:
Short: high flux
Fast operando measurements Faster and better than ILL Sufficient wavelength resolution for dark field imaging and inelastic so quantitative, 3D time resolved
Inelastic mapping
Gratings for phase mapping
Short: Large FoV, 40x40 cm2
Real-scale fabrication processes, components and devices
Short: high divergence
Neutron optics: Wolter and/or Fresnel zone plates and/or compound refractive lenses Neutron microscope with x100 flux and 50 mm resolution
Prototypes are pt. being developed through 2 projects 2xPhD + 1 postdoc and 2 high-tech spin-out companies
MAGNI – ESS STAP meeting
25.09.2025
MAGNI – Microscopy, Advanced and Grating Neutron Imaging
Markus Strobl (PSI/DTU) Luise Theil Kuhn (DTU) Robin Woracek (ESS) et al.

## Slide 4
25.09.2025
MAGNI – Microscopy, Advanced and Grating Neutron Imaging
Markus Strobl (PSI/DTU) Luise Theil Kuhn (DTU) Robin Woracek (ESS) et al.
short – high flux – high resolution - relaxed wavelength resolution - large field of view
MAGNI will exploit new neutron imaging methods
High resolution neutron imaging - a pioneering dedicated real neutron microscope exploiting the high divergence of short instrument
Dark-field contrast imaging – multiscale investigations, macroscopic to nanometer, using versatile gratings
Advanced spectroscopic neutron imaging – leveraging low wavelength resolution for inelastic scattering
Large field-of-view and/or depolarization imaging –enabling studies of industrial-scale components and devices during fabrication/operation