## Slide 1: Survey, Alignment and Metrology Fiducials Requirements
Fabien Rey
ESS Survey, Alignment and Metrology Group
ACCELERATOR TECHNICAL BOARD
23/09/2015

## Slide 2
2
Based on 3D free stationing technique with least squares adjustment calculus
Instrumentation: laser tracker, total station, digital and optical levels, 3D Arm, GPS, metrology software.
Two reference networks connected:
- One outside Geodetic Pillar Network (mm accuracy)
Measurements: GPS, Total Stations, Digital Levels.
- One internal reference network (0.1 mm accuracy)
Measurements: Laser Trackers , Total Stations, Digital Levels
Survey & Alignment Strategy at ESS

## Slide 3
LASER TRACKER
Measure angles in vertical and horizontal planes + distances
some models measure in interferometry mode
1.5” PRISMs
TRIPOd
Laser Trackers
10 m diameter
Accuracy below ± 50 micrometres

## Slide 4
Fiducialization Process
4
Fiducialization : report the sensitive part or axis of a component to external references used to align the component.
Mechanical axis used for construction / assembly
Sensitive Axis: magnetic axis, accelerating axis…
Fiducials to receive prism
Laser tracker
Fiducialization Bench

## Slide 5
Fiducials
ESS-0012977
6H7 Machined Hole
Cone directly machined
on the component
Assembly glued with M6 Hole
1,5” Prism
Cone Part
M6 Part

## Slide 6
Nominal beam axis
No Forced Centering for instruments
We place the instruments where convenient
Alignment Process

## Slide 7
Fiducials REQUIREMENTS
Quantity
Placement
Line of sight
Type
Goal: Get the fiducials implemented in the design

## Slide 8
Next Step
Fiducialization Report
Should contain :
Fiducialization Process ( instrument used, sensitive part measured)
Data : 3D coordinates of the fiducials expressed in a defined coordinate system

## Slide 9
Thank You