## Slide 1
Experiment Control & Data Curation?
Experiment Control & Data Acquisition?

## Slide 2: ECDC's role is turning this ...

## Slide 3: ... into this

## Slide 4: ECDC Responsibilities
  Experiment Control
  Beamline and Device Controls
  Detector Data Readout
  Readout Data Acquisition
  Detector Software Event Formation
  Data Streaming
  Scalable Cloud Storage
  Nexus File Writing

## Slide 5: ECDC System Architecture
EFU
readout
event formation
Lund - CPH
detectors
'RM'
slits
choppers
samp. env
...
EPICS
FW
'EPICS'
NICOS
data
controls
instrument hardware
site infrastructure
DMSC
filewriter
storage
AREA 51

## Slide 6: Readout, Event formation and file writing one for each instrument
Analog
Digital
Logical
Physical
('tof', r, j, q)
('tof', pixel)
(t, FEN, RING, ch, adc)
(V(t), A(t), Ohm)
EFU
Readout
Backend
Readout
Frontend
Scipp & friends
Deals with instrument configuration identifiers such as rings and front –end nodes + other digital and digitized values: grids, wires, strips, tubes, amplitudes or ADC values.
This step abstract all information on the left away and provides a 2D (3D) detector surface which can be used for commissio-ning, monitoring and calibration.
Conversion electronics ultimately measures charge, current or voltages.
Here, pixels are 'connected' with the physical instrument geometry: lengths, angles and detection volumes.

## Slide 7: Experiment & Device Control one for each instrument
NICOS
CLI and GUI to control & monitor
Shutters
Slits
Choppers
Sample Movement
Robotics

## Slide 8: Architecting all this requires
a tremendeous amount of collaboration
  DRAM, SCIPP, DST, DetG, ICS, chopper group, motion control, sample environment, Instrument scientists, IDS'es, user office, ...
a focus on commonality
  standard interfaces, configuration, calibration, data formats, documentation
a good development toolchain
  automatic sw builds and tests, measurable test coverage, automated deployments
tools for systems monitoring and debug

## Slide 9: ECDC Servers – Site
nicos 10.225
nicos 10.238
efu0632 (?)
kafka0619
filewriter0124
efu0633
efu0634
efu0635
efu0533
efu00534 (?)
efu0433
efu0434
efu0435
efu0436
efu0437
efu0631
filewriter0626 (?)
filewriter0628 (?)
filewriter0625
filewriter0627
kafka0621
kafka0521
kafka0523
kafka0525
kafka0527
kafka0413
kafka0421
kafka0423
kafka0425
kafka0427
kafka0429
kafka0431
kafka0517
kafka0519
kafka0529
kafka0531
filewriter0629
filewriter0630
Graylog 211.187.
Grafana 211.93
Generator 211.98
Graphite 211.24
AKHQ 211.94
AKHQ 211.85
Dashboard 211.156
Daqlite 211.41
Daqlite 211.67
kafka0415
kafka0417
kafka0419
bifrost-nicosserver
nmx-nicosserver
tbl-nicosserver
dream-nicosserver
loki-nicosserver
odin-nicosserver
March 2025

## Slide 10: Instrument Infrastructure
ESS

## Slide 11: Grafana Runtime Stats

## Slide 12: File writing (job) monitor

## Slide 13: DMSC integration

## Slide 14
Experiment Control and Data Collection
Epics Commands and Device Control
Event Creation and Data Compression