## Slide 1: SKADI Detector
Current status
PRESENTED BY Sebastian Jaksch, Ralf Engels, Romuald Hanslik, Tadeusz Kozielewski, Torbjörn Grahm

## Slide 2: Agenda
1 Housing
2 Integration Plan
3 Testing

## Slide 3: Housing
Detectors will be housed inside the air boxes moving inside the evacuated detector tube
Detector tube:
Vacuum housing with movable box inside
Detector box:
Air-filled boxed moved back and forwards along the axis of the detector tube
Different Components

## Slide 4: Detector tube
Has been manufactured by SDMS
Installation done
Includes the movable components for the air box (those are still awaiting MCA coordination/support)

## Slide 5: Cooling
Scale testing has been done
Complexity comes from long tubes for movable detectors
Conclusion
Less than 5000 l/min per detector box maximum  Kaeser cooling system is capable of handling that airflow
Hardware procured and delivered
@10 m/s flow rate:

## Slide 6: Air-Box
Necessary since detector is for operation in air only
Very thin front windows prevents using very high speed/pressures to be used for cooling
Self-contained system for the whole detector

## Slide 7: Plan for integration
Steps necessary for integration
Align firmware and ESS backend
Align time synchronization between ESS clock and detector
Create fully reduced data at the backend from neutron events at the front end
Available now
SANS images
Time synchronization in the lab with ESS timing system (single with ESS), ongoing
Time synchronization at ORNL with identical timing signal, but from different source (SNS or either pulse generator, ongoing)

## Slide 8: Proposed next steps
Test with new firmware: Running now
Workshop for integration of new team members as soon as possible
Improvement of firmware based on previous results
Second (final) test with firmware and full ESS stack: Based on availability late 2025

## Slide 9: Results from tests
Goals
Create SANS images
  AgBeh
  Nanoparticles
Time sync with external sources for appropriate timing signal (TTL signal)
Physical setup
1x5 (10x50 cm)
Beam central on the left tile
Scattering center and scattering image recorded as one
Measured sample AgBeh
Caveats
Only rudimentary collimation
High potential background/no shielding
Very low flux

## Slide 10: Time Synchronization: In general
General Setup
Internal clock is running on an oscillator
Whenever there is an external sync, this clock is set to zero (here pulse generator)
Real world time is calculated by adding the internal time to the external sync as an offset
Generally independent of how the external sync is created

## Slide 11: Time Synchronization: Tests
Time sync from SNS
TTL pulse delivered in sync with SNS (60 Hz)
White beam with maximum at either 2.1 Å or 6.4 Å
Exact data still under evaluation, but decay over time looks as expected for a Maxwell-Boltzmann spectrum
Data collected
Full beam
With samples
Incoherent scatterer

## Slide 12: Timing Spectrum
SNS Data currently being evaluated
Software to sort time slices currently being written
Test performed at SNS
AgBeh and Nanoparticles
Direct Beam
Incoherent scatterer
Different wavelengths
Blocked beam
gammas
6.4 Å neutron +
decay

## Slide 13: Unexpected Nuggets
SNS allowed for a nice test for gamma sensitivity
We will use this data to estimate gamma contribution to “useful” spectrum
Here ca. 1% gammas (but still working on details)
There was a primary beam, even when beam blocked
Since B4C was only blocking neutrons there were sufficient gammas to create a primary beam shadow
With B4C
Without B4C

## Slide 14: Backup slides by ECDC

## Slide 15: Proposed SONDE detector integration
The proposed SONDE detector data chain will be unique:
  No Read out Master Module (RMM)
  Network switches required to aggregate data
  Timing synchronisation with Event Receiver- EVR (no RMM)
  Individual pixel characteristics (each of 64 pixels, of each module)
SONDE is currently not aligned with ESS standard data chain infrastructure
Concept schematic. CB - Concentrator Boards

## Slide 16: Time synchronization
Current design synchronizes each concentrator board through a sequence (image)
Time initialization is ideally done rarely (days/ months)
Synchronization will be a 2 step process:
  Configuring the time counter to the correct time on CB
  Start syncing at the correct time with an electrical pulse (from EVR)
Each of the 208 CB must be synchronized, monitored and controlled individually.
A critical component
Proposed schematic of time synchronisation sequence
Schematic of time synchronization pulse distribution

## Slide 17: Data and data path
  Everything upstream the EFU is non standard
  From the EFU, the standardized ESS infrastructure can be used
  CB must package and send the data and the EFU must parse the data according to the agreed format
EFU
Schematic of data path. Standard ESS data path from EFU to file.
Example of data package format

## Slide 18: Project plans
  A concept architecture has been documented
  ECDC will provide a project leader to coordinate the integration project. The position is currently being filled
  Technical resources will be identified
  A project plan will be developed
  Project will start as soon as feasible

## Slide 19: Main challenges/design risks
Design still only theoretical
Readout chain performance
    Clear requirements needed, does the system design really meet real rates?
    No scale up experiments done
Stability
    Timing adjustment duration (on full system)
    Timing adjustment frequency (on full system)
Reliability
    Missed data from PMTs or undetected drop outs
Timing accuracy (uncharacterized)
    Timing could be off at times
    Undetected

## Slide 20: Main challenges
  New control architecture
  Communicating, controlling and monitoring 200+ devices(CBs) instead of one device (if RMM used)
  Time synchronization sequence is complex and untested
  EPICS needs to communicate with EFU
  EFU application will be unique for SONDE