## Slide 2: Radiation Safety Case: Context for and involvement by the Shielding&Safety Systems
PRESENTED BY Fabian lundkvist

## Slide 3: Agenda
1 Background: Achieving the INP License
2 Shielding&Safety Systems: Roles in Radiation Safety
3 SAR Checklist & Rad Safety Readiness Summary
4 Questions

## Slide 4
Background: Achieving the INP License
1

## Slide 5: License to Operate – INP NOW
A step wise approach to routine operation license
Siting permit
Submission Jan 2012
Received Jun 2014
Installation permit
Submission May 2016
Received Oct 2017 excl. NSS and H09 (rad waste)
Trial operation permit NCL
Submission Jul 2019
Received Oct 2020
Routine operation permit
Submission TBD
Received TBD
Installation permit NSS & H09
Submission Mar 2022
Received Sept 2022
Trial ops permit SCL
Submission Oct 2023
Received May 2024
Extension for new Instruments
Trial ops permit BOT, NSS, H09
Submission Dec 2024
Expected Oct 2025
INP = Intentional Neutron Production

## Slide 6: How do we get there?
Connection from engineering design to licensing
Several stages from Design to License to operate beam to Target
Define operations concept, systems, radiation hazards
Analyse ability to manage hazards (normal operations & accident analyses) -> define RSFs, WRSFs needed
System (SSCs): classification, design, verification/validation
Commissioning plan, OLC
Write cSAR
PSR and ISR reviews
SSM review Trial Operations
Respond to SSM RFIs License
Acronyms:
RSF – Radiation Safety Function
WRSF – Worker (only) Radiation Safety Functions
SSC – Structure, system, component
OLC – Operating Limits and Conditions
cSAR – current Safety Analysis Report
SRR
PSR – Primary Safety Review
ISR – Independent Safety Review
SSM – Swedish nuclear regulator
RFI – Request for information
SRR – Safety Readiness Review
Engineering & Analysis
Licensing

## Slide 7: Radiation Safety Analysis Purpose
Protect ESS workers and the public from potential radiological consequences
  Apply a systematic process to identify, evaluate, and control potential radiation hazards related to ESS areas.
  Identify hazardous conditions and events associated with the facility processes, operations, work activities, and natural phenomena
    High power beam impacting the tungsten target will create an inventory of nuclides
    3000 kg of tungsten, 5 MW proton beam, 5-year target wheel lifetime
  Understand potential hazardous conditions and scenarios
  Define necessary prevention and mitigation measures
    Input to system design requirements – Target systems, ACC systems, Instruments, Waste management, building features, shielding, HVAC, Controls, PSS, TSS
    Identify need for radiation safety functions
  Identify g evaluate g control these hazards (planned) and events (unplanned)

## Slide 8: Achieving the Operation License
How do we do this with respect to rad safety?
  Demonstrate
  That we understand the radiation hazards for the facility.
  That we have identified the necessary radiation safety functions to manage them.
  That we have properly implemented the systems to execute those functions.
    The systems meet the requirements defined by the analyses (functions, classification, reliability, quality, withstand appropriate loads, etc.).
    The systems follow ESS design rules.

## Slide 9: Areas involved for the Shielding&Safety systems
Areas of relevance:
D01
D03
E02

## Slide 10
Shielding&Safety Systems: Roles in Radiation Safety
2

## Slide 11: Shielding&Safety systems Safety
  ESS-5912419 - Comprehensive reference list for the Shielding and Safety systems

## Slide 12: S&SS Safety Case – 7-Step References
  Step 1
    NSS ConOps (ESS-0005817)
    NSS SDD (ESS-00377817)
  Step 2-3
    Proposed area classifications for D, E, & G buildings (ESS-0057612)
    NSS Provisions (ESS-2972939)
    Provisions Utility block (ESS-2027007)
  Step 4
    NSS – Rationale for selection of bounding events (P/W) (ESS-0281261)
    Qualitative Identification of NSS Events(ESS-4868730)
  Step 4-5 (AAs)
    Earthquake: NSS2P (ESS-1834687), NSS2W (ESS-3918239)
    Shielding: NSS4P (ESS-1163894), NSS4W (ESS-1273763), NSS9P (ESS-3820989), NSS9W (4041791),
    Human presence: NSS11W (ESS-2135635), NSS12W(ESS-5162140)
    Summary of Unplanned Event assessments (ESS-5667527)
  Step 6 (Classification)
    ESS categorisation (ESS-3730670)
    Classification report: Shutters (ESS-5033510),
    Step 7 (DID):
      NSS DiD (ESS-3872939)
      NF DiD (ESS-0061641)
S&SS Systems

## Slide 13: What systems?
  Monolith inner and outer Shielding
  Beamline shielding
        Up to shutter
  Neutron Beam Port Plug (NBPP)
  Neutron Beam Port Insert (NBPI)
  Neutron Beam Optical Assembly (NBOA)*
  Bunker Wall Insert (BWI)*
  Collimators*
  Bunker Walls / Roof
  Instrument shutters (Active/Inert)
  Temporary Beam stops
  Light Shutter System (LSS)
  Personnel Safety System (PSS) – Bunker
S&SS SSCI2S (structure, system, components important to safety)
*Not explicit SSCs – affects shielding calculations
Boundary for the S&SS

## Slide 14: S&SS in Rad Safety
  Important for public
  Execute Radiation Safety Function (RSF)
  Related Administrative Measure (AM)
    Procedure related to system operations, maintenance, facility operations/emissions
  RS Classified
    EI&C, Mechanical, Civil, HVAC, lifting
  Act as barriers
  Involved in Operational Limits & Conditions (OLC)
    operability requirements, compensatory measures, MCR-owned
  Involved in Facility Safe State
  Service SSC - Enables another system to maintain RSF during accidents wrt public
  Important for workers (not public)
  Execute Worker Radiation Safety Function (WRSF)
  Worker Administrative Measure (WAM)
  RS Classified
    EI&C, Mechanical, Civil, HVAC, lifting
Roles for SSCs in Radiation Safety

## Slide 15: Systems in RS for Public
S&SS SSCs – Functional requirements
  Monolith Shielding:
    RSF-P-TUB-L1-003_Shield_: Shield monolith sources
    RSF-R-TUB-L1-012_Shield_: Shield monolith sources
  Bunker Wall/Roof:
    RSF-P-NSB-L1-001_Shield_: Shielding of monolith/prompt gamma radiation/scattered radiation
    RSF-P-NSB-L1-002_Shield_: Shield by movable shielding and manage shielding configuration
  NBPP/NBPI:
    RSF-P-NSB-L1-024_Shield_: Shield monolith components permanent shielding
  BWI/Collimator/NBOA:
    RSF-P-NSB-L1-002_Shield_: Shielding of monolith/prompt gamma radiation/scattered radiation
    RSF-P-NSI-L1-003_Shield_: Shield by movable shielding and manage shielding configuration

## Slide 16: Systems in RS for Public
S&SS SSCs – Functional requirements
  Instrument shutter (Inert)
    RSF-P-NSB-L1-026_Shield: Shield by movable shielding
  Temporary beamstop:
    RSF-P-NSB-L1-026_Shield_: Shield by movable shielding
  Beamline shielding:
    RSF-R-NSI-L1-009_Shield_: Shield by permanent shielding
    RSF-P-NSI-L1-003_Shield_: Shield by permanent shielding

## Slide 17: Systems in RS for Workers
S&SS SSCs – Functional requirements
  LSS:
    WRSF-R-NSB-L1-007_Stop flux_: Stop gamma flux by LSS
  NBPP/NBPI:
    WRSF-R-NSB-L1-025_Shield_: Shield monolith components permanent shielding
  BWI/Collimator/NBOA:
    WRSF-R-NSB-L1-004_Limit irradiation flux_: Limit number of particles
    WRSF-R-NSI-L1-007_Limit irradiation flux_ : Stop gamma flux by LSS
  Instrument shutter (active):
    WRSF-P-NSI-L1-002_Shield_: Shield by movable shielding and manage shielding configuration
  PSS (Bunker):
    WRSF-R-NSB-L2-020_Stop flux_: Interlock LSS to ensure that gamma flux is stopped
    WRSF-P-NSB-L2-021_Grant/prevent human presence_: Prevent access to Bunker
    WRSF-P-NSB-L2-022_Prevent flux_: Interlock accelerator bending magnets
Notes: Red circle: procedures are documented in the MM, but decont never trained on and full filter exchange not trained on (light version trained on).

## Slide 18: AMs/WAMs for RS for S&SS
  Bunker Wall/Roof (P) :
    RSF-P-NSB-L1-002_Shield_: Manage the configuration of the bunker roof shielding
    RSF-R-NSB-L1-006_Shield_: Manage the configuration of the bunker roof shielding
  LSS (W):
    WRSF-R-NSB-L2- 023_Stop flux_: Verify that the light shutters are in closed position / Isolate motion energy sources from the LSS in Maintenance mode when maintenance activities require major beamline component removal.
Notes: Red circle: procedures are documented in the MM, but decont never trained on and full filter exchange not trained on (light version trained on).

## Slide 19: Ams/WAMs for RS for S&SS
  RP (W):
    WRSF-R-NSB-L1-005_Optimise decay time_: RP group: access procedure to Bunker Interior
    WRSF-P-NSB-L1-013_Prevent flux_: RP group: prevent neutron production during human presence in Bunker
    WRSF-P-NSB-L1-014_Grant/prevent human presence_: RP group: control access to Bunker Roof
    WRSF-P-NSB-L1-015_Grant/prevent human presence_: RP group: prevent access to the Bunker Interior
    WRSF-R-NSB-L1-016_Grant/prevent human presence_: RP group: control access to Bunker Roof and Bunker Interior Inner and Outer Areas
    WRSF-P-NSI-L1-018_Grant/prevent human presence_: RP group: precent access to beamline vicinity
    WRSF-R-NSI-L1-020_Grant/prevent human presence_: RP group: control access to beamline vicinity
  Other (W):
    WRSF-R-NSB-L1-003_Optimise the choice of material type_: Procedures according to the ESS Materials Handbook (ESS-0028465)
    WRSF-R-NSB-L1-004_Limit irradiation flux_: Boron layer included in components
    WRSF-R-NSB-L1-008_Shield_: Temporary shielding
    WRSF-C-NSB-L1- 012_Confine_: Stabilising surface treatment
Notes: Red circle: procedures are documented in the MM, but decont never trained on and full filter exchange not trained on (light version trained on).

## Slide 20: Procedural readiness
Procedures in the safety case – relevant for maintenance
  WRSF-R-NSB-L1-005_Optimise decay time_ : RP group: access procedure to Bunker Interior
  WRSF-R-NSB-L1-008_Shield_: Temporary shielding
  RSF-R-NSB-L1-006_Shield_: Manage the configuration of the bunker roof shielding
  Procedures described in:
    ESS Procedure for Radiation Protection requirements to access the Bunker (ESS-5162257)
    Bunker Access Management Working Group Report (ESS-5063342)
    ESS Handbook for Radiation Protection Chapter 2. General Radiation Protection Rules (ESS-0239718)
  WRSF-R-NSB-L2- 023_Stop flux_: Verify that the light shutters are in closed position / Isolate motion energy sources from the LSS in Maintenance mode when maintenance activities require major beamline component removal.
    TSAR-254: Develope & validate procedure for LSS operation not yet resolved.

## Slide 21: Classified S&SS SSCs
Disciplines: Mechanical, Electrical and Instrumentation & Control
SSC (FBS) | Mechanical | Electrical/ I&C | Reference
Instrument shutters (=ESS.NSS.H01.INSTR.A01.R03.R01) (P/W) | MQC4 | EIC0 | ESS-5033510
Classification -> Design, inspection, quality requirements

## Slide 22: Facility Safe State (ESS-5217883)
  Proton beam is switched off with no possibility of being restarted
  Any residual radiation is shielded
  Worker*: PSS prevents any access to the Bunker
  Worker*: The LSS is closed
  Checklist 6.2.3, #17: Are “Safe State” defined and corresponding procedure to reach safe state established, according to “Safe state of ESS regarding radiation hazards"?
    Yes. For public.
    ESS-5217883 Rev4 – released Nov2024
    In INP application
    Safe state for workers need to be defined.

## Slide 23
3
SAR Checklist & Rad Safety Readiness Summary

## Slide 24: Which SSCs finish validation after BOT?
RS classified Target Group SSCs
  Checklist item #2: Do systems in the review scope that are classified as SSCI2S, have their radiation safety requirements covered by completed tests, documented and released?
    See ESS-5912419 - Comprehensive reference list for the Shielding and Safety systems
    Concludes that the majority of the documents are released. Completed tests are documented and also released in CHESS. The following have their documents in status preliminary:
      NBOA (Beer/Miracles/Magic/T-Rex/Heimdal/Estia/Skadi/Vespa/Dream/Freia)
      BWI (Miracles)
    Performance of shielding can only be verified with beam on

## Slide 25: Radiation Safety barriers
Target Group SSC involvement
  The Barrier integrity assessment NSS (ESS-4089724, Rev4), identifies the following systems to be barriers for prompt and residual radiation:
    Bunker and beamline shielding
Notes: Barriers for contamination hazards prevent the dispersion of radioactive substances within the facility and release of radioactive substances to the surroundings

## Slide 26: Facility Safe State (ESS-5217883)
S&SS SSC involvement
  Checklist #19: Are “Safe State” defined and corresponding procedure to reach safe state established, according to “Safe state of ESS regarding radiation hazards"?
    Yes, for public.
    ESS-5217883 Rev4 – released Nov2024
    Safe state for workers needs to be defined (work in progress).
✅
If there has been an accident
Safe State minimises the hazard profile of any remaining risk

## Slide 27: INP OLC (ESS-0357253)
S&SS SSC involvement
  Monolith shielding (Permanent&Removeable)
  Temporary beamstops (This may consist of the instrument shutter (with motion disabled) or a dedicated Temporary Beamstop (TBS (=ESS.NSS.F01.F01.F07))
  Beamline shielding
  Bunker roof
  Bunker walls
  NBPI/NBPP
  Checklist #18: Is Operational Limits and Conditions released in CHESS for the upcoming commissioning step released and known by relevant staff? ?
    Yes
    ESS-0357253, Rev19 released 19-Sept2025
    Note: Rev19 in progress to address SSM-3105 for INP compl. 4 response
✅

## Slide 28: JIRA tasks – radiation safety
S&SS STATUS
  Issue Tracker
      NIT-498 - Clarify requirements of the physical access control function of Bunker PSS areas
      NIT-497 - Install radiation area signage
      NIT-424 - BUNKER D03: SAT compliment
      NIT-415 - BUNKER D03: Closure and Verification of shielding
      NIT-413 - BUNKER D01: Closure and Verification of shielding
      TSAR-254 - Develope & validate procedure for LSS operation

## Slide 29: Rad Safety Readiness - Summary
What is left from a radiation safety point of view?
  Before SRR5:
  Any discrepancies in installation shall be addressed in ESS-5912419/ESS-5850978.
  Any unreleased reports in CHESS must be released.
  Finish NIT-tasks related to Rad Safety.
  Before BoT:
  Finish TSAR-254
  NBPI/NBPP not classified – Can we update the NSS Step2-3 wrt to this?
  After BoT:
    Capture changes in configurations of instruments in ESS-5912419/ESS-5850978
    Verify functionality of the shielding – does it perform as intended?

## Slide 30
4
Questions