## Slide 1
ESS Spoke Cryomodules:
How does it work ?
First results on prototype
ESS AD Retreat, Lund, 12th Nov. 2015
On behalf of the IPN Orsay Team
Sebastien Bousson

## Slide 2
ESS Linac Overview
SCRF linac (T=2K)
Warm linac
Top-level requirements | 
Pulse length (ms) | 2.86
Energy (GeV) | 2
Peak current (mA) | 62.5
Pulse repetition frequency (Hz) | 14
Average power (MW) | 5
Peak power (MW) | 125
95% of the energy gain with 146 SCRF cavities
2 types of cavities & 3 beta families
ESS Linac is special and innovative:
Mainly based on SRF (Superconducting Radio Frequency ) technology
Very powerful (~4 times higher than SNS)
First accelerator to use spoke cavities
Challenging accelerating gradients

## Slide 3
ESS Cryomodules
ESS Cryomodules :
3 different types (spoke, medium beta, high beta)
x13 spoke, x9 medium beta, x21 high beta
Beta (b) is the reduced particle velocity; b = v / c
=1 means that the particle has the speed of light
What is a cryomodule ?
A cryomodule is a device which gives the appropriate environment and conditions to efficiently operate the accelerating superconducting cavities (and possibly superconducting magnets)
It may group several cavities
What is an accelerating superconducting cavity ?
An accelerating cavity is the device that provide acceleration to the charged particle, by means of a voltage
Superconducting means the use of a special state of some materials, called superconductors, which below a critical temperature (Tc), exhibits extraordinary properties such as the absence of electrical resistance.

## Slide 4
How does an RF accelerating cavity works ?

## Slide 5
Superconducting Cavities
Frequency f
50 MHz to 3 GHz
Size
Proportional to 1/f
Temperature T
1,5 K to 4,5 K
Accelerated particle velocity
=v/c from 0,01 to 1
0 K  - 273,15 °C
c  2,998 . 108 m/s
« CAVITY » = Electromagnetic resonant cavity
    RF fields (electric and magnetic)
     To accelerate charged particles
« SUPERCONDUCTING » : very low operating temperature (Liquid Helium)
 Superconducting state of the matter
Superconducting cavity (IPN Orsay) – 5 cells, 700 MHz, =0,65
Incident
beam
Accelerated beam
equator
iris
Power port
cell
length  1 m
Beam tube

## Slide 6
Superconducting Cavities
(1) An electric field is created on the beam axis , and is available to accelerate charged particles
PRF
Electric field E
This E field is time and space dependant
With f the cavity frequency, T = 1 / f
Ex : f = 700 MHz  T = 1,43 ns

## Slide 7
Superconducting Cavities
E
q
Proton case q > 0, velocity v
F
The charged particle enter the : for an efficient acceleration, the particle should be synchronized with the RF wave
The particle should arrive at the right time in the cell
The cell length should be adjusted to the particle velocity
Lcell
Synchronism condition :
The time for the particle to cross one cell should be TRF/2 
The cell length should verify: or

## Slide 8
Superconducting Cavities
Energy gain :
or
Eacc: accelerating field of the cavity (for a given particle velocity)
Lacc: cavity accelerating length
 : particule phase with respect to the RF wave
Ex : f = 700MHz ; 5-cell proton cavity  = 0,65 (Lacc=514cm); Eacc= 10MV/m ;  = 0°
 Energy gain : U = 1eV  10MV/m  0,7m  1 = 7 MeV
Lacc=Ncell  Lcell
Proton case
q > 0, velocity v

## Slide 9
Superconducting Cavities
(3) Beam acceleration : particles should be bunched and synchronized with the electromagnetic wave
Tbeam = n TRF (n=1,2,3…)
« the cavity resonant frequency should be a multiple of the beam frequency that
it wants to accelerate»
Ex: if fbeam=350 MHz (Tbeam=2,86ns), then the cavity should resonate at :
f = 350 MHz (TRF=2,86ns), or f = 700 MHz (TRF=1,43ns), or f = 1050 MHz (TRF=0,95ns), etc.
Proton case
q > 0

## Slide 10
Superconducting Cavities
RF power transmitted to the beam
Pbeam = U  Ibeam
PRF
Pcavity
Pbeam
Total RF power to give to the cavity
PRF = Pbeam + Pcavity
Order of magnitude (700 MHz cavity -  = 0,65 - 5 cells- 10MV/m - =-30° - protons beam 10 mA)
SC cavity (Q0  1010) : Pbeam = 6 MeV  10 mA = 60 kW
Pcavity  16 W
"Warm" cavity (Q0  3.104) : Pbeam = 60 kW also
Pcavity  5,5 MW !!!  not possible in CW !
Dissipated RF power on
the cavity walls
Pcavity  (EaccLacc)² / Q0
Q0 : cavity « quality factor »

## Slide 11
Superconducting Cavities
Intrinsic advantage of cold cavities
Almost no losses on the cavity wall (thanks to superconductivity)
 100% of the injected RF power goes to the beam : very high efficiency !!!
Operating cost gain as compared to warm structures (which dissipate 105 times higher)
Possibility to accelerate CW beams or beams with a high duty cycle (> 1 %) with high accelerating gradients (impossible with warm structures)
Possibility to relax the constraints on the cavity RF design: choosing larger beam port aperture is possible  reduction of the activation hazard = security gain
High potential for reliability and flexibility
Main drawback : need to be operated at cryogenic temperature

## Slide 12
The Superconducting Cavities bestiary !
= 1
= 0,1
= 0,01
Structures inter-digitales (ATLAS, Argonne)
48 et 72 MHz -  = 0,009 à 0,037
RFQs supra (Legnaro)
80 MHz -  = 0,009 à 0,035
Cavité ré-entrante (Legnaro)
352 MHz -   0,1
Résonateurs split-ring (ATLAS, Argonne)
97 et 145 MHz -  = 0,06 à 0,16
Résonateurs quart d’onde (ALPI, Legnaro)
80 à 352 MHz -  = 0,047 à 0,25
Cavités spoke (CNRS Orsay)
352 MHz -  = 0,15 et 0,35
Cavités elliptiques
350 MHz à 3 GHz -  = 0,47 à 1
Cavité TTF
1,3 GHz -  = 1
Cavité APT (Los Alamos)
700 MHz -  = 0,64
Résonateur demi-onde (Argonne)
355 MHz -  = 0,12

## Slide 13
Superconducting Cavities
A spoke cavity is a superconducting RF cavity well adapted for (proton) particle acceleration between 50 MeV and 200 MeV
Has all advantages of any superconducting cavity
Is very stiff and less subjected to perturbations induced by vibrations
Can be multi-cell -> compactness
Has potential to reach high accelerating gradients
ESS double spoke
Name refers to spoke in bicycle wheels

## Slide 14
How does a cryomodule works ?

## Slide 15
Cryomodules
The main functions of a cryomodule
Give the cryogenic environment for the cold mass, i.e. the cavity and/or magnet (only cavity in the ESS case): perform the cryofluids distribution
  Helium (LHe) and/or Nitrogen (LN)
  Handle the liquid and vapor phase of the cryofluids
    Cavity operating temperature: 4K (atm. Pressure) or 2K (~30 mbar)
    Thermal shield could be actively cooled by cold He gaz or LN
    Power coupler might required an active cooling
Perform the thermal insulation against all heat transfer from room temperature to the cold mass:
  limit losses by conduction, convection or radiation
Supporting and positioning of the components:
  Structural support for the cold mass
  Precise alignment of the cavities with respect to the beam axis and keep the alignment over the thermal cycles
Provide magnetic shielding to the cavities

## Slide 16
ESS spoke cryomodule: components to integrate
Power Coupler
Cold Tuning System
Ceramic disk, 100 mm diameter
400 kW peak power (335 kW nominal)
Antenna & window water cooling
Outer conductor cooled with SHe
Doorknob transition from coaxial
to ½ height WR2300 waveguide
Slow tuning (stepper motor):
Max stroke: ~ 1.3 mm
Tuning range: ~ 170 kHz
Tuning resolution: 1.1 Hz
Fast tuning (piezo-actuator):
Applied voltage up to +/- 120V
Tuning range at 2K: 675 Hz (min)
Double Spoke
SRF Cavities
Double spoke cavity (3-gaps), 352.2 MHz, b=0.50
Goal: Eacc = 9 MV/m [Bp= 62 mT ; Ep = 39 MV/m]
4.2 mm (nominal) Niobium thickness
Titanium Helium tank and stiffeners
Lorentz detuning coeff. : ~-5.5 Hz/(MV/m)2
Tuning sentivity Df/Dz = 130 kHz/mm

## Slide 17
Main cryomodule components
Cold mass
(cavity, magnet)
Components for Cryo distribution
(valves, tubing, heat exchanger)
Magnetic shielding
Thermal screen
Vacuum vessel
Supporting system
Instrumentation (measurement of T,
P, cryo levels, vacuum)
ESS Spoke Cryomodule

## Slide 18
Constraints for cryomodule design

## Slide 19
Constraints for cryomodule design
1. Limit as much as possible heat transfer
Cold mass (spoke cavities) needs to operate at 2K.
And 1 W dissipated @ 2K costs ~700 W of electrical power to maintain @ 2K !
-> optimization of running cost for the accelerator
The 3 heat transfer mechanisms:
Use of material exhibiting poor thermal conductivity
Use small sections for the interface rods
Use thermal intercepts
Operate in vacuum !
Use thermal shields at intermediate temperature
Use low emissivity materials
Use multi-layer insulation

## Slide 20
2. Mechanical constraints
Isolation vacuum:
The cryomodule external vessel has to sustain external pressure
Thermal gradients:
Thermal contractions induces mechanical constraints
Gravity: component mass
A fully equipped cavity can weight > 250 Kgs
They all have an impact on the alignment and component stability
Temperature map in the ESS spoke cryomodule
Use material with low thermal contraction coefficient (ex: TiA6V, composite materials)
Use geometrical “tricks” to add flexibility (bellows, bended tubes,…)
Use of materials with high elastic limit to sustain the forces
Constraints for cryomodule design

## Slide 21
3. Assembly and maintenance constraints
The cavity string is prepared and sealed in a clean room
  Reduce as much as possible the amount of material inside clean room for improved contamination control
  Optimize the number of assembly operations inside the clean room
Design a cryomodule which can be “easily” assembled and maintained
    Optimize parts and components access
    During all assembly steps, maintain or control/monitor alignment
4. Cost constraint !
    Obvious: optimize the cryomodule component cost but also the required amount of manpower to assemble
    Also think about the cost of assembly tooling
Constraints for cryomodule design

## Slide 22
ESS Spoke cryomodule status

## Slide 23
ESS spoke cryomodule status
Most of the parts are fabricated and delivered
Cold/warm transition
Gate valves
Inter-cavity belows
Thermal shield
Vacuum vessel & Mechanical support
First blank assembly of some parts

## Slide 24
ESS spoke cryomodule status
MLI for the cavity
Magnetic shield
(2-layer Cryophy, actively cooled)
Coupler baking stand
Double-walled
tube
RF conditioning
Cavity with water cooling loop
Power coupler
window
Doorknob
1/2 height
WR 2300

## Slide 25
ESS spoke cryomodule status
Fabrications in progress
  Cryogenic circuits
  MLI for the thermal shield
  Valve box
Detailed studies in progress
  Tooling and assembly procedures

## Slide 26
ESS spoke cryomodule status
View of the cavity inside: the spoke bars
Romea
Giulietta
Germaine
The 3 ESS spoke prototypes

## Slide 27
ESS spoke cryomodule status

## Slide 28
Next steps…
Prototype cryomodule test:
Conditioning of power couplers to start in end November -> first time the power coupler will be submitted to 400 kW !
Start of first assembly of the prototype cryomodule in January 2016
Cryogenic test at IPNO in february/march 2016
Full test at nominal RF power at Uppsala in Spring 2016
Series production:
Preparation of the IPNO infrastructure to handle the series production (preparation, assembly and test)
First “big market” to be released 2nd week of December for the procurement of the Niobium (4 tons !) and the 26 spoke cavities