## Slide 1: Isolator performance - a Magic or a Expected Performance ?
Rutambhara Yogi
www.europeanspallationsource.se
12 November 2015

## Slide 2
Suppliers:
Many thanks to
Colleagues:
ESS: David McGinnis, Anders Sunnesson, Morten Jensen, A. Johansson
Carlos Martins, Rihua Zeng, Rafael Montano, Chiara Marrelli,
Stevo Calic, Bruno Lagoguez, Staffan Ekström, Daniel Lundgreen, Carl Johan Hardh
FREIA: Rolf Wedberg, Lars Hermansson, Roger Ruber, Magnus Jobs & other colleagues
CERN: Eric Montesinos, Olivier Bruner
SNS: Crofford Mark

## Slide 3: Circulator
Ideal Circulator: Like a round about
Can have either 3 ports or 4 ports
Can use coaxial line / waveguide
Direction – clockwise / anti-clockwise
2.856 GHz
P = 6 MWp
Pavg = 25 kW
Indigenous development done in SAMEER (India) in 1999 using OFHC plates. Design, brazing, plating etc was performed in house. Installed on medical linac.
352 MHz
P = 400 kWp
Pavg = 20 kW
Technology demonstrator
for ESS spoke linac (without
Pressurization)
Notes: After lot of technical negotiations this unpressurized circulator in 6 inch coax was developed.

## Slide 4: Construction of 3-port Circulator
Ferrite:

## Slide 5: Ideal & Practical Isolator
1
2
3
A
Load
Isolator
Amplifier is completely isolated from
unwanted reflections
Ideal: Infinite Isolation
Practical: Finite Isolation
A
1/1000 of
power
Isolation = - 30 dB
Input power = 400 kW
400 W will travel back
Load – Dissipate RF power from amplifier
dB – logarithmic unit
dB = 10 log(P2/P1)

## Slide 6
Load
A
Cavity
1
2
3
Isolation = - 30 dB
Load return loss = - 20 dB
Shouldn’t care about load return loss ??
400 W
4 kW
4 W
Full reflection from cavity
S11 = - 30 dB
400 W
According to specifications that we write in SoW
Practical Isolator: Is it True ?
Is reflected power
804 W ?
400 kW
?
Load Cost
α
Offered return loss

## Slide 7
P = V2 / Zo
VT = Vi + VR
where Vi and VR add in phase, VT = 2 Vi
PT = (VT2/ Zo) = (2 Vi)2/ Zo = 4 Pi
Worst case Reflected Power
For 100% reflection, when arcing occurs or during cavity filling
& not 2 Pi
Notes: Circulator tender
Interetesting to think about coupler conditioning

## Slide 8
Factory Acceptance Testing
Amplifier
Isolator = Circulator + Load
Don’t have circulator,
Always tested with a very good load
Load return loss > 32 dB
Don’t have high power RF source. Simulation of high power test using low power.
Tin + 10 C
Tin – 2 C
Tin
Tin + 2 C
Pin = 400 kW,
Pavg ≈ 20kW
For circulator : ΔT = 2 C
For load : ΔT = 10 C
Return loss > 30 dB
Tetrode 1
Tetrode 2
Total power
Courtesy: Magnus Jobs at FREIA

## Slide 9
TH595 based RF Power Station
High power Test

## Slide 10
Tests on Matched load:
No problem.
Return loss was poor (about 25 dB)
Tests with variable short: Difficult test
1
2
3
Reflective short
to simulate worst
cavity behavior
Load
A
1
2
3
Load
Load
A
Every time the Amplifier was tripping
due to high reflected power.
Trip level was set at 20 dB
Return loss of Isolator:
poor than 20 dB why ??
Difference of a factor of 10 !
At some locations,
VT = 2 Vi (depending on phase)
MAGIC ??
Problem faced at high power

## Slide 11: High Power Model of Isolator
Load
Finite Isolation
Finite load
Return loss
A
P1
P2
P3
(V1)
(V2)
(V3)
VT = V1 + V2 +V3
A small program is written for effective return loss calculation
(Ref: ESS-0043091)

## Slide 12
RF Parameters of circulator
in SoW used for simulation:
S11= 30 dB
S12 = 26 dB
S21 = 0.5 dB
NO higher order harmonics
Variation of Effective return loss of Isolator with return loss of load
Amplifier
Specification
We should care about load
return loss.
We need a GOOD LOAD:
Good return loss

## Slide 13
Variation of Effective return loss of Isolator with Phase of load return loss
Circulator tests at low power
S11 = 36 dB
S12 = 34 dB
S21= 0.05 dB
Load tests at low power:
S11 = 38 dB
Explains poor return loss seen
experimentally– Expected
performance
Assumptions:
Amplifier is perfectly matched.
Uncertainties in S-parameter
measurement not considered
GOOD Load:
Phase of return loss: stable

## Slide 14: Testing of concept
Courtesy: Magnus Jobs at FREIA
Short
Towards VNA
Load with phase of return loss
variation
Trend of both the curves is same
Good return loss when phase of load return loss
is 180 o
Further experimentation is planned with high
Circulator and load in FREIA.
Experiment

## Slide 15: Additional Usefulness for ESS ?
Circulator
Load
Gallery layout for HB/MB
By adjusting phase of load return loss 180 ± X,
Adjust distance between load and circulator accordingly
Need to install a huge
number of Systems: 155
Commissioning becomes
efficient.
Easily good
Performance can be
achieved

## Slide 16
Thank you !