## Slide 2: Instrument presentation MIRACLES + CSPEC
DMSC STAP 2026
Christian Beck, Instrument Data Scientist

## Slide 3: Agenda
1. MIRACLES
1.1. Instrument Description and Timeline
1.2. Current Status
1.3. Next Steps
2. CSPEC
2.1. Instrument Description and Timeline
2.2. Current Status
2.3. Next Steps

## Slide 4
MIRACLES
time-of-flight backscattering spectrometer
1

## Slide 5: MIRACLES: Instrument Description & Timeline
Near backscattering spectrometer
Primary Spectrometer
2 Counterrotating PWD Choppers (max 308 Hz)
PS Chopper (max 42 Hz)
FO Chopper (max 98 Hz)
Secondary Spectrometer
Si111 analyzer crystals
Two detector banks
ESS Instrument with highest energy resolution δE
Wide dynamic range ΔE
Q-range dependent on analyzers (Si111: 0.2 Å-1 <q<2.0 Å-1)
Chopper settings allow tuning of flux, δE and ΔE to match experimental requirements.
Notes: PWD Pulse-shaping / width definition chopper
PS Pulse-selection
FO frame overlap chopper

## Slide 6: MIRACLES: Current Status
McStas Simulations of Instruments with event data as output
First version for data reduction workflow in scipp resulting in S(q, ) with continuous and q based on user-defined binning
Characterization of different operation modes with different chopper settings

## Slide 7: MIRACLES: Next Steps
  Data reduction
    Normalization
    Masking
    Integration into essspectroscopy
  Data workflow
    File format
    Setting up data pipeline
  HC tools
    Visualization of monitors
    Instrument control
    Possibility to easily compare to Mcstas

## Slide 8
CSPEC
direct geometry time of flight spectrometer
2

## Slide 9: CSPEC: Instrument Description & Timeline
cold chopper spectrometer

## Slide 10: CSPEC: Current Status
  Discussions started for :
    McStas simulations
    Data reduction workflow

## Slide 11: CSPEC: Next Steps
McStas simulations
Creation of simulated data
Data reduction workflow
Define operation modes
Repetition rate multiplication (RRM)
Visualization tools
  HC tools
    Visualization of monitors
    Instrument control
    Possibility to easily compare to Mcstas

## Slide 12: Thank you for your attention

## Slide 13: Example with chart
Sub-headline to strengthen the headline above
Chart: 
| Index 1 | Index 2 | Index 3 | Index 4 | Index 5 | Index 6
Värden | 3 | 5 | 6 | 4 | 3 | 5

## Slide 14: Example with chart
Sub-headline to strengthen the headline above
Chart: 
| Index 1 | Index 2 | Index 3 | Index 4 | Index 5
Value 1 | 0.165 | 0.65 | 0.9 | 0.33 | 0.5
Value 2 | 0.2 | 0.55 | 0.8 | 0.15 | 0.6
Value 3 | 0.25 | 0.6 | 0.6 | 0.25 | 0.7
Value 4 | 0.35 | 0.5 | 0.75 | 0.3 | 0.6

## Slide 15: Example with coloured table
Column A | Column B | Column C | Column D | Column E
Row 1 | Data | Data | Data | Data
Row 2 | Data | Data | Data | Data
Row 3 | Data | Data | Data | Data
Row 4 | Data | Data | Data | Data
Row 5 | Data | Data | Data | Data
Row 6 | Data | Data | Data | Data
Row 7 | Data | Data | Data | Data
Row 8 | Data | Data | Data | Data
Row 9 | Data | Data | Data | Data
Sub-headline to strengthen the headline above