## Slide 1
Welcome
Mats Lindroos
Head of the ESS Accelerator Division
EPG 5/12/2011

## Slide 2: ESS accelerator design High level objectives
ESS accelerator high-level technical objectives:
  5 MW long pulse source
    -2.86 ms pulses
    -14 Hz
    -Protons (H+)
    -Low losses
    -High reliability, >95%
    -Cryostats for minimum
    Energy consumption
    -Flexible design for
    a future power upgrade

## Slide 3: LINAC layout
 | Length (m) | Input Energy (MeV) | Frequency (MHz) | Geometric β | # of Sections | Temp (K)
RFQ | 4.7 | 75 × 10-3 | 352.2 | -- | 1 | ≈ 300
DTL | 19 | 3 | 352.2 | -- | 3 | ≈ 300
Spoke | 58 | 50 | 352.2 | 0.57 | 14 (2c) | ≈ 2
Low Beta | 108 | 188 | 704.4 | 0.70 | 16 (4c) | ≈ 2
High Beta | 196 | 606 | 704.4 | 0.90 | 15 (8c) | ≈ 2
HEBT | 100 | 2500 | -- | -- | -- | --
3
H. Danared, M. Eshraqi, A. Ponton, ESS

## Slide 4: ESS Programme Organisation
Data Management
ESS AB Board
CEO
C. Carlile
Accelerator
Target
Conventional Facilities
Instruments
Administration
Director
Machine Director
Science
Director
Steering Comm (STC)
Adm Financial Comm
Programme Director
Programmme Office
Science Adv. Comm
Technology Adv. Comm
Preconstruction
Construction
Operation Phase
Collaboration Partners
Neutron Science

## Slide 5: Accelerator Design Update
Work Package (work areas)
1. Management Coordination – ESS (Mats Lindroos)
2. Accelerator Science – ESS (Steve Peggs)
3. Infrastructure Services – Tekniker, Bilbao (Josu Eguia)
4. SCRF Spoke cavities – IPN, Orsay (Sebastien Bousson)
5. SCRF Elliptical cavities – CEA, Saclay (Guillaume Devanz)
6. Front End and NC linac – INFN, Catania (Santo Gammino)
7. Beam transport, NC magnets and Power Supplies – Århus University (Søren Pape-Møller)
8. RF Systems – Uppsala university (Roger Ruber)
Josu Eguia
Guillaume Devanz
Sebastien Bousson
Søren Pape Møller
Roger Ruber
Romuald Duperrier (30 years ago)
Steve Peggs
Cristina Oyon
Mats Lindroos
Santo Gammino

## Slide 6: Some of the committees…
EMT: ESS management team which consists of the ESS CEO, the thre directors and the head of administration
EPG: ESS Project management group which consists of EMT, AD head, TD head and ID head
CCB-M and CCB-F: Change control and coordination of machine and facilities

## Slide 7: ESS Master Programme Schedule
 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
ESS Program Phases, Gates and Milestones Program level |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Accelerator |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Target |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Instruments |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conventional Facilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Program Initiation
Program Set-up
Delivery of Contsruction phase
PG 3
PG 2
PG 1
PG 4
Full beam power on target
Design Update
Prepare to Build
Construction
Technical Design Report
Design Update
Prepare to Build
Construction
Concepual Design
Installation 1-22
Installation
Design Update
Site preparation
Construction
# 7
List
Ground Break
Pre-construction phase
Operations
Installation
Design and Manufacturing 22 instruments
Construction
First Building
First Neutrons
to Instruments
losure
Pre Construction Report

## Slide 8: Progress in 2011
Recruitment of staff in Lund, we are now 25!
  Experts present in Lund for shorter and longer periods to support AD and ADU project
Kick-off of ADU project
  Regular TB meetings for change control and coordination
  Work has started in all WPs
  First revision of Parameter lists, available at AD homepage in PDF form
  Collaboration board had its first meeting
Conceptual Design Report in V1 (going to V2)
Modulator ordered for CERN test stand
Project support in Lund at AD for ADU and P2B
  Reporting fully operational and first project review passed
  Alfresco, please use it!
  Suzanne Gysin, what a star!
The project office in Lund
  CCB and EPG meetings for chnage and configuration control, project reviews and coordination
  More from Johan Brisfors

## Slide 9: Some on-going work…
Strategy for Elliptical cavitiy cryomdoule prototyping
  Several visit to potential partners and one workshop in Lund
  To be presented to ESS senior management in the end of February
Strategy for modulator prototypes
  Discussions between Uppsala University, Lunds university and ESS on how to optmize existing reources and assure a coherent plan and division of responsibilities
  To be presented to senior management in February for decision
New baseline to be “downloaded” in January and April 2012
  Issues: Hybrid or not, MEBT design, DTL length, transition energies, RFQ length,…
  Beam physics is the integrating cavity for any accelerator project
CDR to become a living document which will progress to TDR under change control
  Steve is the chief Editor and CCB and EPG manages change control
Internal reviews for all ADU activities and future P2B and construction activities
  Suzanne will present next steps at TB meeting
Planning, re-planning and launching of ADU and P2B Wus and WPs
  Launched as we are ready to go: CM prototyping, Uppsala test stand, Infrastructure and services
Planning for construction project under PMO
  WBS to level 3, schedule and costing to enable us to enter into construction in 2013

## Slide 10
First thoughts -
CM production line (XFEL)
SDMS, ZANON, RI, …
Other Manufacturer

## Slide 11: Upgrade options
Increase the repetition rate
  Requires new RF sources
  Not favored for operation with operation at a single target station as it would require moving the instruments
Increase the beam current
  Requires additional RF sources and/or additional cryomdoules and that linac and shielding is design for higher currents (with some additional cost)
  Favored from instrument study (power upgrade with preserved time structure improves almost all instrument performance almost linearly)
Increase the pulse length
  Will require new RF sources
  Not all instruments would benefit
Add a second target station
  Could be combined with increased repetition rate
Short pulse operation with H- and ring
  Can be combined with H+ operation but would require new RF sources and a new front-end
Increase beam energy
  Only moderate beam energy increase can be handled by the target and moderators
EPG adopted guidelines for upgrade studies:
  Beam current limitation at 90-100 mA with a single front-end
  Beam energy limitation at 3.5 GeV set by shielding and target

## Slide 12: Upgrades
The mandate is to build a 5 MW accelerator!
The presently favored upgrade scenario is a power upgrade to higher power with maintained time structure
  Present understanding at AD is that this best is achieved with a higher beam current or/and a moderate beam energy increase
We will study how this can be prepared within the present 5 MW baseline
  The additional cost should be understood and made apparent in the costing of the 5 MW baseline
  First technical studies and financial estimates for the upgrade itself should be done as part of the ADU project

## Slide 13: Headlines
We are designing the ESS accelerator
  Good progress in all areas
  Many thanks for your contribution
We should plan for entering construction in 2013
  Will require that we deliver in time on all deliverables and that we that we launch key P2B activities in 2012
  Will require that we deliver on construction project planning to PMO
  Will require that we prepare through internal reviews with external experts for a comprehensive technical review of the ESS accelerator construction project
None of this would be possible without you and your collaborators at our partner institutes and labs.

## Slide 14: Greetings from Bejing

## Slide 15
Thank you for your attention!