## Slide 1
Elliptical
G.Devanz CEA-Saclay
AD retreat Lund 12/05/2012

## Slide 2
Elliptical superconducting cavities
page
beta | Eacc VT (MV/m) | Eacc Linac (MV/m)
0.65 | 17 | 15
0.86 | 20 | 18
5-cell cavities, bulk niobium
two beta families
frequency = 704.42 MHz
operating temperature 2K
gradient specifications :
Peak field specifications : Epk < 40 MV/m

## Slide 3
Elliptical cavities cryomodules
page
Cavity string building block : fully dressed cavity
Cryomodule options:
Hybrid
Segmented
Comparison of static losses has started, first indications is that a segmented design could competitive on this parameter (might also be shorter!)

## Slide 4
page
From W. Hees

## Slide 5
Elliptical cavities cryomodules
page
XFEL string layout example, With SC Quads
CAVITY
QUAD
Lmag 166 mm
physical length 300 mm
COLD BPM
BELLOW
10 convolutions
100 long
78 mm diameter
VALVE
BELLOW

## Slide 6
Elliptical cavities cryomodules
page
8 cavities with 2 sc quads

## Slide 7
Elliptical cavities cryomodules
page
8 cavities segmented scheme, room temperature quads

## Slide 8
RF design
b g=0.86 |  | unit
Frequency | 704.42 | MHz
Nr of cells | 5 (sym.) | 
Cell to cell coupling | 1.8 | %
p and 4p/5 mode separation | 1.2 | MHz
Epk/Eacc | 2.2 | 
Bpk/Eacc | 4.3 | mT/(MV/m)
Max. r/Q | 477 @ b=0.92 | W
G | 241 | W
Low field Qo | 3e10 | 
Qo at nominal Eacc | 6e9 | 
Advantages of high cell to cell coupling for TM01:
easier to obtain field flatness, control over peak fields distribution among cells
more consistent Qext across cavities
enhanced mode separation between p and 4p/5 modes
HOM also better coupled to the outer cells (needed for damping)

## Slide 9
RF design – End groups and Qext
page
 | Cut-off frequencies (GHz) |  |  |  |  |  | 
Diameter (mm) | TE11 | TM01 | TE21 | TM11 | TE01 | TE31 | TM21
130 | 1.3535 | 1.7683 | 2.2405 | 2.8143 | 2.8143 | 3.0769 | 3.7831
140 | 1.2568 | 1.6420 | 2.0804 | 2.6132 | 2.6132 | 2.8571 | 3.5129
Lc could be reduced to 30 mm (Ti vessel option)
Using a conical tip decreases Qext by ̴̴15% for a given antena penetration
140 mm tube, flat antenna tip w/ fillet

## Slide 10
Fundamental passband modes
page

## Slide 11
HOM - monopoles
page
Monopole HOM for the 5-cell below cutoff
+TE passband 1454-1476 MHz

## Slide 12
First monopolar HOM band
page
Freq Q Max. r/Q
1,420314E+09 1,58E+05 8
1,421856E+09 4,30E+03 17
1,431672E+09 3,22E+04 4
1,442845E+09 3,30E+04 29
1,456038E+09 4,41E+04 60
RF window included
Copper losses from
- power coupler
inter-cavity bellows
BUT OPTIMISTIC (matched termination)
Simulations including the doorknob and waveguide confirm the Qext is below 5e7 for all non-propagating non TE monopole modes

## Slide 13
HOM damping
page
Freq Q Max. r/Q
1,480140E+09 1,98E+04 5
1,491491E+09 1,33E+04 17
1,505236E+09 1,40E+04 4
1,518154E+09 1,87E+04 4
1,527895E+09 4,57E+04 0,2
RF window included
Copper losses from
- power coupler
- inter-cavity bellows

## Slide 14
RF/Mechanical design
page
Optimal compensation ring radius (mm) | 84
KL fixed ends (Hz/(MV/m)²) | -0,36
KL free ends (Hz/(MV/m)²) | -8.9
Stiffness (kN/mm) | 2.59
Df/Dz (kHz/mm) | 197
max VM stress /1mm (MPa) | 25
KP fixed ends (Hz/mbar) | 4,85
KP free ends (Hz/mbar) | -150
max VM stress /1bar fixed (MPa) | 12
max VM stress /1bar free (MPa) | 15
Aiming at kext=30 kN (tuner and He vessel combined stiffness) to get KL = -1 Hz/(MV/m)2
At Eacc=18 MV/m the corresponding static detuning is 324 Hz (1/3 of cavity bandwidth), need to be compensated by piezo tuner
DP
5 bar
Simulation of cavity deformation with a plastic model, 3.6 mm thickness
The differential pressure is cycled : 0-5-0 bars at room temperature
external rig used to maintain cavity length : fixed ends
max residual deformation after 1 cycle : 7mm for 1 cycle, detuning -560 Hz

## Slide 15
He vessel and tuner integration
page
Stainless steel vessel option
Titanium vessel option
Derived from CARE-HIPPI b = 0.5 cavity
Derived from SPL Ti tank design
New Saclay piezo tuner for SPL cavities
Titanium tank
NbTi flanges, Al Hex seals
(single bellow)

## Slide 16
New cavity tooling at Saclay
page
Field flatness tool :
Designed for SPL beta=1 cavities, compatibility with ESS high beta cavity included (larger flanges, stiffening rings, shorter cells)
New Saclay vertical EP station

## Slide 17
Prototype cavities planning
page

## Slide 18
Summary on beta 0.86 cavity
page
RF design of the cavity is done
Mechanical design of cavity and helium vessel done
Order of RRR>250 Nb launched in early october
Technical specification for cavity fabrication done
Call for proposal for cavity manufacturing : 3 candidates
Launch of call for tender foreseen this week

## Slide 19
Power coupler RF design
Starting from Saclay HIPPI 1MW 10%DC coupler (KEK type window)

## Slide 20
Power coupler RF design
|E|
|H|
HIPPI doorknob
T-bar transition
T-bar transition has 3 times the current doorknob bandwidth
potentially less sensitive to geometrical errors
however implementation of biasing may be difficult