## Slide 1: LSS Detector update
Dorothea Pfeiffer on behalf on the ESS detector group
Thanks to G. Croci and F. Piscitelli for their slides
18.02.2016

## Slide 2
Detectors for SKADI: SoNDe grant
SKADI SANS instrument needs detectors which can take higher rates than existing Anger Cameras
H2020 4MEUR Grant: Julich + LLB + IDEAS(NO) + Lund U +ESS
See Sebastian Jaksch's talk this afternoon in the detector session

## Slide 3: LOKI detectors
Detector Top and Exploded view – 3D Cathode
Total of 100 lamellas (separated by 4 mm gap) are foreseen to realize the demonstrator
Tilting the detector by few degrees ensures high detection efficiency
337 mm
400 mm
Cathode
10B4C Lamellae system
Triple GEM
Readout anode
LOKI rear detector UMBRELLA
One Lamella element: 24 Al/Ti strips coated by 1 µm 10B4C on both sides
Geometrical dimensions of the demonstrator defined in order to equip all the rear area by using 8 modules
For further information, please refer to the poster by G. Groci et al.

## Slide 4
Boron Array Neutron Detector (BAND) - GEM
6 cm
2 mm

## Slide 5: BandGEM Demonstrator Design 1/2

## Slide 6: BandGEM Demonstrator Design 2/2

## Slide 7: Performance: Prototype and Demonstrator
 | Prototype - Achieved | Demonstrator - Simulated
Lamella Distance | 2 mm | 4 mm
B4C/empty ratio on lamellas | 1 | 3
Full Lamella System lenght | 6 cm | 9 cm
Lamella Thickeness | 250 µm | 100 µm
Lamella Material | Aluminium Oxide | Aluminium/Titanium
Optimal tilt angle | 7 degrees | 2.4 degrees
Pulse Height Threshold | 70 keV | 100 keV
Cathode geometry | 10x10 cm2 - Square | Trapezoidal
Count Rate Capability | 10 MHz/cm2 | 12 MHz/cm2
Gamma Ray Sensitivity | 5*10-5 | 10-7
Measured Efficiency @ 1.5 Å | 18.5% | //
Expected Efficiency @ 2.0 Å | // | 37%
Expected Efficiency @ 6 Å | // | 55%
Expected Efficiency @ 12 Å | // | 61%
Resolution FWHM @ 2,6,12 Å | // | 5.5 – 6 mm
Front-end ASIC | CARIOCA – 8 channels/chip | GEMINI – 16 channels/chip

## Slide 8: NMX detectors

## Slide 9
The Gd-GEM project
Task 4.1 Neutron Detectors – The Resolution Challenge
Sept. 15
Sept. 16
Sept. 17
Sept. 18
Deliverable
Milestone
3 years
The key objective of WP4 is the technological
evolution of neutron detectors in terms of
resolution, intensity and dimensions.

## Slide 10: Requirements and challenges
200 μm position resolution (beyond state of art for time resolved neutron detectors)
High rate requirements with up to MHz/cm2
High gain stability and count rate stability
Mechanical robustness (detectors mounted on freely movable robotic arms)
Reasonable gamma suppression
=> Gd-GEM detector
GEM foil
Electrical field in holes

## Slide 11: Natural Gadolinium converters
Baseline: Backwards and forwards mode. Optimum thickness 6 um, thinnest available foil 10um:
20% efficiency at 1.8 A
28% efficiency at 3.5 A
Alternative: Backwards mode, one detector: Optimum thickness >=50 um
14% efficiency at 1.8 A
20% efficiency at 3.5 A
neutron
Backwards detector
Forwards detector
Gd
e-
e-
Efficiency at 1.8 Å
Upgrade with 157 Gd: up to 38% efficiency at 1.8 A
and 42% efficiency at 3.5 A

## Slide 12
Capping layer for Gd foil not needed
XPS measurements w/o Al capping layer
- no benefit with Al capping
- capping process “adds” O
- foils are stable
- GdO layer with O surplus builds up but does not grow significantly
Thanks to Susann Schmidt

## Slide 13: GEM Rate capabilities with Gd
Thanks to Filippo Resnati
Gain modification caused by charge density
Gd ce deposit on average
28 keV in 10 mm drift space
For Gd: 3 MHz/cm2
Standard Triple GEM
Ar/CO2 70%/30%
Cu X-rays ~ 8 keV
E. Perelli Cippo et al., A GEM-based thermal neutron detector for high counting rate applications”, JINST 10(2015) 10, P10003

## Slide 14: Gd-GEM backwards setup
neutron
conversion electron
Start of track

## Slide 15: Position resolution
Intrinsic position resolution: σ <= 400 um
Scales with strip width (200 um strips possible)

## Slide 16: Optimum drift size of Gd-GEM
Ekin in converter
Ekin leaving converter
Edep in drift
Ideal drift thickness: 10 mm – 20 mm

## Slide 17: Simulated and measured gamma sensitivity in 10 mm drift
Measured values 250 um Gd and 3 keV threshold
backwards forwards
6E-03 241 Am 59.5 keV gamma 1E-03 241 Am 59.5 keV gamma
2E-03 22 Na 511 keV/1274.5 keV gamma 2E-03 Na 511 keV/1274.5 keV gamma
Backwards without threshold
Forwards without threshold

## Slide 18: Neutron and gamma sensitivity of 50 um Gd in backwards configuration
Depending on threshold and gamma energy, gamma sensitivity around 10-3
10 mm drift
Neutrons
Gammas

## Slide 19: Results from 2015
Gd-GEM detector works
Detection efficiency (2 Å neutrons) is with 12% as expected from simulations (without scattering 15%)
Tracking of electrons works
Intrinsic position resolution of σ <400μm (relates directly to 400 μm strip pitch)
With smaller pitch σ = 200 μm achievable
Fast readout electronics are under development, VMM2 being tested at the moment
Gamma sensitivity with reasonable energy threshold around 10-3, 50 keV – 500 keV gammas are the biggest problem since their energy deposit is identical to the Gd conversion electrons

## Slide 20: Gd-GEM Outlook for 2016
Further study gamma sensitivity
Determine optimum drift thickness
Study stability with 2 GEM foils
Evaluate low scatter readout material
Study smaller strip pitch
Build 10cm x 10 cm prototype to participate in neutron scatter experiment to show performance

## Slide 22
Reflectometry at ESS: FREIA and ESTIA
Horizontal Reflectometer
(FREIA)
Suitable for liquids
(limited angular range)
Vertical Reflectometer
(ESTIA)
Not suitable for liquids
More versatile
(wide angle range)

## Slide 23
The Multi-Blade project
Wigner Research Institute
Budapest Neutron Centre
Task 4.2 Neutron Detectors – The Intensity Frontier
Sept. 15
Sept. 16
Sept. 17
Sept. 18
Deliverable
Milestone
3 years
The key objective of WP4 is the technological
evolution of neutron detectors in terms of
resolution, intensity and dimensions.

## Slide 24
concept introduced in 2005
proof of concept in 2012
University of Perugia
Institut Laue-Langevin
Institut Laue-Langevin
The Multi-Blade project

## Slide 25
neutrons
5 degrees
θ
Efficiency 45% at 2.5Å
A single Boron layer inclined at 5 degrees
Efficiency
The intensity is spread over a wider surface
(5 degrees = factor x10)
substrate
10B4C

## Slide 26
Multi-Blade
sample
neutrons
neutrons
hit the layers at 5˚
proof of concept in 2012
4 cassette demonstrator:

## Slide 27
4 cassette demonstrator:
Results:
Measured Efficiency 45% at 2.5Å
Spatial Resolution 4mm x 280μm
Counting rate capability ~5000 n/s/mm2 at 2.5Å
(limited by the electronics)
Atmospheric pressure operation
  (thin vessel window, low scattering)
  (cost effective materials)
0.9mm
Neutron beam (~0.2mm)
x = 280μm
Efficiency

## Slide 28
4 cassette demonstrator:
Results:
Measured Efficiency 45% at 2.5Å
Spatial Resolution 4mm x 280μm
Counting rate capability ~5000 n/s/mm2 at 2.5Å
(limited by the electronics)
Atmospheric pressure operation
  (thin vessel window, low scattering)
  (cost effective materials)
Max local rate | 105 n/s/Å/mm2 | Conventional refl. 105 n/s/Å/mm2 High intensity mode 104 n/s/Å/mm2
Spatial resolution | 4mm x 1mm | 4mm x 0.5mm
The ESS requirements

## Slide 29
4 cassette demonstrator:
Results:
Measured Efficiency 45% at 2.5Å
Spatial Resolution 4mm x 280μm
Counting rate capability ~5000 n/s/mm2 at 2.5Å
(limited by the electronics)
Atmospheric pressure operation
  (thin vessel window, low scattering)
  (cost effective materials)
The state of the art
Max local rate | 105 n/s/Å/mm2 | Conventional refl. 105 n/s/Å/mm2 High intensity mode 104 n/s/Å/mm2
Spatial resolution | 4mm x 1mm | 4mm x 0.5mm
The ESS requirements
x10
x20
x300

## Slide 30
4 cassette demonstrator:
Results:
Measured Efficiency 45% at 2.5Å
Spatial Resolution 4mm x 280μm
Counting rate capability ~5000 n/s/mm2 at 2.5Å
(limited by the electronics)
Atmospheric pressure operation
  (thin vessel window, low scattering)
  (cost effective materials)
The state of the art
Max local rate | 105 n/s/Å/mm2 | Conventional refl. 105 n/s/Å/mm2 High intensity mode 104 n/s/Å/mm2
Spatial resolution | 4mm x 1mm | 4mm x 0.5mm
The ESS requirements
x10
x20
x300

## Slide 31
4 cassette demonstrator:
Results:
Measured Efficiency 45% at 2.5Å
Spatial Resolution 4mm x 280μm
Counting rate capability ~5000 n/s/mm2 at 2.5Å
(limited by the electronics)
Atmospheric pressure operation
  (thin vessel window, low scattering)
  (cost effective materials)
Next demonstrator:
Counting rate capability
Overlap and uniformity
Max local rate | 105 n/s/Å/mm2 | Conventional refl. 105 n/s/Å/mm2 High intensity mode 104 n/s/Å/mm2
Spatial resolution | 4mm x 1mm | 4mm x 0.5mm
The ESS requirements

## Slide 32
Next demonstrator (9 cassettes):
Counting rate capability
Overlap and uniformity
Build technology prototype
Tests at both beam line and Reflectometry beam line
Electric filed modeling
Testing and availability of beam line
Build technology prototype
Data analysis
Detailed GEANT4 on detector performance
All three partners will work together on the final detector for the ESS Reflectometers

## Slide 33
Wigner Research Institute
Budapest Neutron Centre
Francesco Piscitelli
János Orbán
Tibor Zsíros
Eszter Dian
Péter Pázmándi
Gábor Kiss
Dezső Varga
Richard Hall-Wilton
Meeting at BNC - December 2015

## Slide 34
neutrons
strips Y
wires X
substrate
10B4C
Electric field modeling

## Slide 35
Any material holding the strips at 5deg scatters too much!
neutrons
cassette
strips Y
wires X
10B4C
substrate
Old Design
scattered or absorbed flux
Materials evaluation

## Slide 36
Efficiency saturated (5degrees)
At 5deg not much survives to the 10B4C
Substrate as thick as necessary
Kapton (strips) shielded by 10B4C
neutrons
strips Y
wires X
cassette
substrate
10B4C
New Design
Materials evaluation

## Slide 37
~7 mm single-side
200x300mm2 Al-plates single-side coated
1mm 2mm 3mm
1mm
2mm
3mm
2mm
Planarity is an issue on large surfaces
Materials evaluation
10B4C
Si

## Slide 38
Multi-Blade mechanical design
amplifier board
amplifier board
cathode strips
anode wires
holding frame
10B4C substrate
neutrons
10x10cm2 demonstrator

## Slide 39
Assembly completed in December 2015
1 blade area: ~120x120 mm2
9 cassettes (10 blades)
Coating area: ~ 10x120x120 mm2 (single side)
Detector active area: ~10x9x120mm2=90x120mm2

## Slide 40
Demonstrator ready!
Tests to come:
  SF (Lund University) - Now
  BNC (Budapest) - February
  Real instrument - …

## Slide 41
Thank you for your attention !
Very..
Life is tiring..

## Slide 42
No point in getting up..
You say it..