## Slide 1: Mitigation Devices External Interface ICS
Nick Levchenko
Lund
Date: 2015-12-09

## Slide 2: Scope
Magnetron
LEBT Chopper

## Slide 3: Magnetron (Overview)
Provides microwaves to generate plasma in the plasma chamber
Model: Sairem GMP 20 KE/D
Disabling magnetron will stop microwaves generation, therefore collapsing plasma and stopping the beam production
Beam stop time: relatively slow, approximately 100 µs
Details of magnetron internal circuit boards drawings are expected from Sairem to be reviewed by ESS

## Slide 4: Magnetron (Interfaces)
Timing System (Triggering)
Integrated Control System (Control & Monitoring)
Beam Interlock System (Machine Protection)

## Slide 5: Magnetron (Architecture)
HV Fast Shutdown Rack
Magnetron Head
Magnetron HV Supply
External
Interfaces:
Timing System
ICS
BIS
Modbus Gateway
Fault Control
HV Fast Shutdown
Power Supply
BIS

## Slide 6: Magnetron(External Interfaces)
Signal | Type | Format | Connector
On/Off | Digital In | Optical Fibre | HFBR
On/Off | Digital Out | Optical Fibre | HFBR
Fast Stop | Digital In | Optical Fibre | HFBR
On/Off | Digital Out |  | M12
On/Off | Digital Out |  | M12
Fault | Digital In |  | M12
Fault | Digital In |  | M12
Control & Monitor | Various | Modbus | RJ45

## Slide 7: LEBT Chopper (Overview)
Chops the beam pulses
Custom made by INFN (Catania), based on the design for Spiral2 (France)
Enabling high voltage (10 kV) will deviate the beam to the beam dump preventing it from travelling any further to the target
Beam stop time: approximately 300 ns
Using chopper to stop the beam is an additional measure to improve the slow response time of primary beam stop method (magnetron)
Primary method (magnetron) must be deployed, as chopper will overheat beam dump
Details of chopper external interface and internal circuit boards drawings had been provided by INFN and are being reviewed by ESS at the moment

## Slide 8: LEBT Chopper (Interfaces)
Timing System (Triggering)
Integrated Control System (Control & Monitoring)
Beam Interlock System (Machine Protection)

## Slide 9: LEBT Chopper (Architecture)
HV Module
Beam
Vacuum chamber with deflecting electrodes
Feedthrough
HV PS (0 – 10 kV)
HV Switch
LV Module
PS
Control, monitoring and alarm circuit boards
External
Interfaces:
Timing System
ICS
BIS

## Slide 10: LEBT Chopper (HV Module)

## Slide 11: LEBT Chopper (External Connections)

## Slide 12: LEBT Chopper (External Interfaces)