## Slide 1: FMEDA of the Fast Beam Interlock System
Riccard Andersson
Machine Protection Review
2015-12-09

## Slide 2: The Beam Interlock System

## Slide 3: Analysis Approach
Failure Modes, Effects, and Diagnostics Analysis
Greatly inspired by Ben et al.’s analysis for LHC
One FMEDA per module
  Gives overall failure rate, per failure mode
ReliaSoft BlockSim for system-level calculation
FBI_D
FBI_DIF
FBI_MASTER
FBI_ACTUATOR
Input Signal (BLM, BCM etc)
Actuators (Choppers, PS)

## Slide 4: Analysis Approach
Military Handbooks (MIL-HDBK-217F and 338B)
Component manufacturer documentation
System Effects are
  Negligible
  Maintenance
  Trip
  Blind
  To Be Tested (TBT)
Detection ways are
  Hidden
  Inspection
  Diagnostics
  Test

## Slide 5: Failure Sheet – Excerpt from FBI_DIF
 |  | THICK FILM RESISTOR |  |  | 27.17 |  | Open Circuit | 0.59 | 16.03 | Trip | Diagnostics
R4_T | Test | 100 OHM, 125mW | Farnell | 1632456 | 27.17 | 9.2 | Value Drift | 0.36 | 9.78 | Negligible | Hidden
 |  | 150 V |  |  | 27.17 |  | Short Circuit | 0.05 | 1.36 | Trip | Diagnostics
 |  | Surface Mount Thick Film Resistor |  |  | 27.17 |  | Open Circuit | 0.59 | 16.03 | Negligible | Hidden
R5_T | Test | MCWR Series, 1 kohm | Farnell | 2447587 | 27.17 | 9.2 | Value Drift | 0.36 | 9.78 | Negligible | Hidden
 |  | 125 mW, ± 1%, 150 V |  |  | 27.17 |  | Short Circuit | 0.05 | 1.36 | Trip | Test
 |  | Surface Mount Thick Film Resistor |  |  | 27.17 |  | Open Circuit | 0.59 | 16.03 | Trip | Diagnostics
R2_P | Permit | 20 kohm, 125 mW | Farnell | 2447603 | 27.17 | 9.2 | Value Drift | 0.36 | 9.78 | Negligible | Inspection
 |  | 150 V |  |  | 27.17 |  | Short Circuit | 0.05 | 1.36 | Trip | Diagnostics
 |  | Surface Mount Thick Film Resistor |  |  | 27.17 |  | Open Circuit | 0.59 | 16.03 | Trip | Diagnostics
R3_P | Permit | 20 kohm, 125 mW | Farnell | 2447603 | 27.17 | 9.2 | Value Drift | 0.36 | 9.78 | Negligible | Inspection
 |  | 150 V |  |  | 27.17 |  | Short Circuit | 0.05 | 1.36 | Negligible | Inspection
 |  | IC, INVERTING SCHMITT TRIGGER |  |  | 264.70 |  | Fails Low | 0.5 | 132.35 | Trip | Test
U5_T | Test | 5 pins, 2/6 V | Farnell | 1468757 | 264.70 | 5.1 | Fails High | 0.5 | 132.35 | Trip | Diagnostics
 |  | Trip at Test | No Effect | Maintenance | Trip | Blind | To Be Tested | Sum | 16863.48 |  | 
 |  | 1676.85 | 6571.14 | 1743.42 | 8084.61 | 372.57 | 91.74 |  |  |  | 
Color coded cells for quick overview
  System Effect and Detection
Name | Location | Description | Supplier | Supplier ID | Component Failure Rate | Reference | Failure Mode | Ratio | Mode Failure Rate | System Effect | Detection
 |  |  |  |  | [1/1E9 hours] | MIL-HDBK-217F | MIL-HDBK-338B | MIL-HDBK-338B | [1/1E9 hours] | Blind, Trip | Test, Diagnostics
 |  |  |  |  | Sheet:Calculator |  |  |  |  | Maintenance, Negligible | Inspection, Hidden

## Slide 6: Hardware Draft Results
Failure rate per hour versus design prototype
15% of PIL2
DRAFT

## Slide 7: Hardware Draft Results (extended)
A few more design options
Chart: 
| No Redundancy | Doubly Redundant | Test 30 min | Test 20 min | Test 10 min | 2oo3 Redundancy | 2oo3, test 20 min
Trip | 0.0013466 | 0.002675 | 0.00535 | 0.008025 | 0.01605 | 2.521e-05 | 7.563e-05
Blind | 0.0001921 | 2.555e-07 | 1.278e-07 | 8.518e-08 | 4.259e-08 | 2.559e-07 | 8.53e-08
15% of PIL2
DRAFT

## Slide 8: Reliability
Beam trip allocation from RAMI group
50 per year for all of ICS 34 per year from BIS only
DRAFT

## Slide 9: Summary and Discussion Points
Trade off between
  Protection Function
    Highest is a PIL2 PF
  Reliability
    “95% user happiness”
Expand the analysis to
  Monitor inputs (BCM, BLM, BPM)
  Actuators
How to include e.g. firmware and operational errors?
Reliability analysis without complete schematics

## Slide 10: Thank You

## Slide 11
PROTECTS THIS MACHINE